## Slide 1: Chapter 1-2 Fundamentals of Quantitative Design and Analysis

## Slide 2: Computer Design Engineering life cycle
User requirement
Analysis(1.2)
Evaluating Existing
Systems for Bottleneck(app.A)
Technology Trend 1.4
Power Trend 1,5
Cost Trend 1.6
Dependability 1,7
Quantitative Principles
1.9
Simulate New
Designs and
Organizations
Workloads
Implement Next
Generation System
Benchmarks(1.8)
Evaluating for energy-performance cost (1.8)
Notes: Requirement Analysis:
Market analysis: who you will sell 4-1.2
desktop, server, embedded system, HPC
Different markets has different driven motivations.
When design a desktop, it aims to obtain best price-performance.
For the servers, dependability is critical, then the scalability, and throughput.
For the embedded computer systems, price is a key factor, while real-time performance is important . And power efficiency and memory size is always under consideration.
2. Functional requirement: 4-1.3
3. Performance requirement:
4. Power
5. Unfuntional requirements: availability, dependibility 1.7
7. Cost/price

## Slide 3: Topics in Chapter
1.1 Introduction
1.2 Classes of computers
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summerizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 4: 5 computing markets
Feature | PMD | Desktop | Server | Clusters/ warehourse-scale computer | Internet of things /Embedded
Price of system | $100-$1000 | $300-$2500 | $5000 -$10,000,000 | $100000-$200,000,000 | $10 -$100,000
Price of microprocessor module | $10-$100 | $50-$500 per proc. | $200 -$2,000 per proc. | $50-$250 | $0.01 -$100 per proc.
Critical system design issues | Cost, energy, Media perf. responsiveness | Price-perf., Energy, Graphics perf. | Throughput, availability, Scalability, energy | Price-perf., Throughput, energy proportionality | Price, energy, application-specific performance.

## Slide 5: Personal Mobile Devices
Wireless devices with multimedia user interfaces
ex. Smartphone, tablet computer,…
Application
  Web-based， media-oriented
  Responsiveness， predictability
Requirement:
  Cost, energy efficiency ( battery, no-fan)
  Real-time performance
  Minimize memory  flash memory

## Slide 6: Desktop Computing
The first, and still the largest market in dollar terms, is desktop computing. （laptop > 50% market of desktop )
Requirement:
  Optimized price-performance
  highest-perf. & cost-reduced Microprocessor appear first in desktop systems
New challenges:
  Web-centric, interactive application
  How to evaluate performance ?

## Slide 7: Servers
The role of servers to provide larger scale and more reliable file and computing services grew.
Requirement:
  First, availability is critical.
  A second key feature of server systems is an emphasis on scalability. memory,storage and I/O bandwidth is crucial.
  Lastly, servers are designed for efficient throughput.

## Slide 8: Cost with downtime
Application | Cost of downtime per hour | 1% 87.6 hrs/yr | 0.5% 43.8 hrs/yr | 0.1% 8.8 hrs/yr
Brokerage operations | $6,450,000 | $565,000,000 | $283,000,000 | $56,500,000
Credit card authorization | $2,600,000 | $228,000,000 | $114,000,000 | $22,800,000
Package shipping services | $150,000 | $13,000,000 | $6,600,000 | $1,300,000
Home shopping channel | $113,000 | $9,900,000 | $4,900,000 | $1,000,000
Catalog sales center | $90,000 | $7,900,000 | $3,900,000 | $800,000
Airline reservation center | $89,000 | $7,900,000 | $3,900,000 | $800,000
Cellular service activation | $41,000 | $3,600,000 | $1,800,000 | $400,000
Online network fees | $25,000 | $2,200,000 | $1,100,000 | $200,000
ATM service fees | $14,000 | $1,200,000 | $600,000 | $100,000

## Slide 9: Cluster/Warehourse-Scale Computers
SaaS (Search,social networking, video sharing, multiplayer games, online-shopping)
WSC—tens of thousands of servers act as one
Requirements:
  Price-performance, Power ( 10% saves $7M )
  Availability is critical
  Scalability ( Note the difference with server )
  (Note the difference with supercomputer)

## Slide 10: Embedded systems
Thin Clients
Network Devices
Office Automation
Kiosk/ATM
Game Platforms
Industrial Automation
Retail POS
Set-Top-Box
Gateway/Media Store
Intel® Architecture
Intel® XScale™

## Slide 11: Embedded Computers
The fastest growing portion of the computer market with widest spread of processing power and cost.
Requirements
  Real time performance (soft & hard)
  Strict resource constraints
  limited memory size, lower power consumption,...
The use of processor cores together with application-specific circuitry.
  DSP, mobile computing, mobile phone, Digital TV

## Slide 12: Other classification
Quantum computer vs Chemical computer,
Scalar processor vs Vector processor
Non-Uniform Memory Access (NUMA)/ UMA
Register machine vs Stack machine vs Accumulater machine
Harvard architecture vs Von Neumann architecture
/Non Von Neumann architecture （ 类脑芯片：达尔文2）
RISC vs. CISC
Cellular architecture
Notes: Cellular architecture takes multi-core architecture design to its logical conclusion, by giving the programmer the ability to run large numbers of concurrent threads within a single processor. Each 'cell' is a compute node containing thread units, memory, and communication. Speed-up is achieved by exploiting thread-level parallelism inherent in many applications.

## Slide 13: Cellular architecture
IBM's Cell microprocessor is the first one to reach the market.
Cellular architecture takes multi-core architecture design to its logical conclusion, by giving the programmer the ability to run large numbers of concurrent threads within a single processor. Each 'cell' is a compute node containing thread units, memory, and communication. Speed-up is achieved by exploiting thread-level parallelism inherent in many applications.
Cyclops64 (known as Blue Gene/C)

## Slide 14: Classes of Parallelism and Parallel Architecture
Two kinds of parallelism in application
  Data-level Parallelism（DLP）
  Task-level Parallelism （TLP）
Hardware exploit in 4 major ways
  Instruction level Parallelism
  Vector Architecture and GPUs
  Thread-Level Parallelism
  Request-Level parallelism

## Slide 15: Classes of computers
Flynn’s Taxonomy: A classification of computer architectures based on the number of streams of instructions and data
Notes: Proposed at 1966.
^ Flynn, M., Some Computer Organizations and Their Effectiveness, IEEE Trans. Comput., Vol. C-21, pp. 948, 1972.
^ Duncan, Ralph, "A Survey of Parallel Computer Architectures", IEEE Computer. February 1990, pp. 5-16.

## Slide 16: classification

## Slide 17: SISD
A serial (non-parallel) computer
Single instruction: only one instruction stream is being acted on by the CPU during any one clock cycle
Single data: only one data stream is being used as input during any one clock cycle
Deterministic execution
This is the oldest and until recently, the most prevalent form of computer
Examples: most PCs, single CPU workstations and mainframes

## Slide 18: SIMD
A type of parallel computer
Single instruction: All processing units execute the same instruction at any given clock cycle
Multiple data: Each processing unit can operate on a different data element
This type of machine typically has an instruction dispatcher, a very high-bandwidth internal network, and a very large array of very small-capacity instruction units.
Best suited for specialized problems characterized by a high degree of regularity,such as image processing.
Synchronous (lockstep) and deterministic execution
Two varieties:
  Processor Arrays: Connection Machine CM-2, Maspar MP-1, MP-2
  Vector Pipelines: IBM 9000, Cray C90, Fujitsu VP, NEC SX-2, Hitachi S820

## Slide 19: MIMD
Currently, the most common type of parallel computer. Most modern computers fall into this category.
Multiple Instruction: every processor may be executing a different instruction stream
Multiple Data: every processor may be working with a different data stream
Execution can be synchronous or asynchronous, deterministic or non-deterministic
Examples: most current supercomputers, networked parallel computer "grids" and multi-processor SMP computers - including some types of PCs.

## Slide 20: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summerizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 21: Technology Trends
Gordon Moore
Moore Law
  In 1965 he predicted that the number of components the industry would be able to place on a computer chip would double every year. In 1975, he updated his prediction to once every two years. It has become the guiding principle for the semiconductor industry to deliver ever-more-powerful chips while decreasing the cost of electronics.
  Transistor density 2x in 18-24 months (1.4-1.5x/year )
DRAM density
  1977-1997： 1.46x/year
  1997-2017： 1.34x/year
  2017-2022： 1.1x/year

## Slide 22: Gordon Moore on Moore’s law
Moore’s brief Bio
  http://www.intel.com/pressroom/kits/bios/moore.htm
Gordon Moore on Moore’s law
http://www.sichinamag.com/Article/html/2007-09/2007919032802.htm
Video on conversation with Moore
http://you.video.sina.com.cn/b/7076856-1282136212.html

## Slide 23: Technology Trends
Integrated circuit logic technoloty
  Transistor Density: incr. 35% per year, (4x every 4 years)
  Die size: 10%-20% per year
  Transistor count per chip:40-55% per year or 2x 10 to 24 months
Semiconductor DRAM
  Capacity per DRAM: 25%-40% per year (2x every 2-3 years)
  Memory speed: about 10% per year
  Might stop and may be replaced
Semiconductor Flash – standard storage device in PMDs
  Capacity per flash chip：50-60% per year （ 2x every 2 years）
  15-20 times cheaper than DRAM
Magnetic Disk tech.
  Desnsity: 30% p.y. Before 1990; 60% p.y. 1990-1996
  100 p.y. 1996-2004 ; 30% p.y. after 2004
  capacity: about 60% per year
Network
  bandwidth: 10Mb  100Mb  1Gb
  10 years 5 years
Designers often design for the next technology.

## Slide 24: Improvement of DRAM rate
AQA Edition | Year | DRAM growth | Characterization of impact on DRAM capacity
1 | 1990 | 60% / year | Quadrupling every 3 years
2 | 1996 | 60% / year | Quadrupling every 3 years
3 | 2003 | 40%-60%/ year | Quadrupling every 3 to 4 years
4 | 2007 | 40% / year | Doubling every 2 years
5 | 2011 | 25% - 40% / year | Doubling every 2 - 3 years

## Slide 25: Import Notes
A rule of thumb
  Cost decrease rate ~ density increase rate
Technology thresholds
  Technology improves continuously, an impact of this improvements can be in discrete leaps.

## Slide 26: Perf. Trends: Bandwidth over latency
Bandwidth/throughput: total amount of work done in a given time
Latency/response time: the time between the start and the completion of an event.
Rule of thumb
  Bandwidth grow rate ~ improvement in latency2
10，000X—25，000X in Bandwidth
30X—80X in latency

## Slide 27: Performance milestones in microprocessor

## Slide 28: Challenges for IC Tecnology
IC characteristic: feature size(特征尺寸）
  10 microns in 1971  0.18microns in 2001
   0.09 microns in 2006  0.032 microns in 2011
  7nm is under way.
  Rule of thumb: transistor perf. Improves linearly with decreasing feature size.
IC density improvement is both opportunity and Challenge:
  signal delay for a wire increase in proportion to the product of its resistance and capacitance.
Wire delay---major design limitation

## Slide 29: Bad prediction with big guy
“There is no reason anyone would want a computer in their home.”
    --Ken Olson, president,
    Chairman and founder of Digital Equipment Corp., 1977

## Slide 30: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power and Energy in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summerizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 31: Trends in Power
Power also provide challenges as device scaled
  first microprocessor: 1/10watt -->
  2GHz P4: 135watt
Challenges:
  distributing the power
  removing the heat
  preventing hot spot

## Slide 32: Techiques to save engery
Do nothing well----stop the clocks when cores are idle.
Dynamic Voltage – Frequency Scaling (DVFS)
  A few clock frequency and voltages
Design for typical case
  Lower power modes（LPM） –save power
  Can not access DRAM or disk when in LPM
Overlocking
  Turn off all cores but one and run at higher clok rate.
Race-to-halt
  Use a faster， less energy-efficient processor to allow the rest of the system to to into a sleep mode

## Slide 33: Compare the performance / power
Pentium® 4 Processor
August 27, 2003
@3.2 GHz core
55 Million 0.13µ transistors
1249 SPECint2000
386 Processor
May 1986
@16 MHz core
275,000 1.5µ transistors
~1.2 SPECint2000
17 Years
200x
200x/11x
1000x

## Slide 34: Power efficiency
Performance scales with area**.5
Power efficiency has dropped

## Slide 35: Two concepts
Dynamic power: power consumption in switching transistors.
  Power dynamic = ½ *Capacitive load * Voltage2 * Frequency switched
  Energy dynamic = Capacitive load * Voltage2
Static power: power consumption when a transistor is off due to power leakage
  Power static = current static * Voltage

## Slide 36: Rule of Thumb
10% reduction of voltage yields
  10% reduction in frequency
  30% reduction in power
  Less than 10% reduction in performance
Voltage | Frequency | Power | Performance
1% | 1% | 3% | 0.66%
Rule of Thumb

## Slide 37
Frequency Reduction | Power Reduction | Performance Reduction
15% | 45% | 10%
Dual core with voltage scaling
Area = 1
Voltage = 1
Freq = 1
Power = 1
Perf = 1
Area = 2
Voltage = 0.85
Freq = 0.85
Power = 1
Perf = ~1.8
A 15%
Reduction
In Voltage
Yields
SINGLE CORE
DUAL CORE
RULE OF THUMB

## Slide 38: Multiple cores deliver more performance per watt
C1
C4
C2
C3
Small
core
Big core
Cache
Cache
1
2
3
4
1
2
1
1
1
2
3
4
1
2
3
4
Power
Performance
Many core is more power efficient
Power ~ area
Single thread performance ~ area**.5

## Slide 39: Why Multicore?

## Slide 40: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summerizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 41: Major Theme: Lower Cost
Cost Trend
  Understanding cost trends of component is important for designers, since we design for tomorrow !
The impact factors for cost:
  Time----Component prices drop over time without major improvements in manufacturing technology
  Volume ----Volume decreases cost due to increases in manufacturing efficiency.
  Commodification----The competition among the suppliers of the components will decrease overall product cost.

## Slide 42: Understanding Cost Trend by Learning Curve

## Slide 43: Price of Pentium4 & PentiumM

## Slide 44: Rules of Thumb
Time: learning curve ----yield
  Twice the yield will have half the cost.(for chip, board, or a system)
Volume:
  Cost decrease about 10% for each doubling of volume.
Commodities:
  Vendor competition
  Supplier competition
  Volume increase, however limited profits.
Notes: Volume affect the cost
缩短了learning curve下拐的时间, 下降的时间与制造的系统数量部分成正比.
提高了购买和制造效率,降低成本
数量会减少开发成本,因为成本是分摊到各台计算机的.

## Slide 45: Cost of an Integrated Circuit

## Slide 46: Distribution of Cost in a System

## Slide 47: Cost vs. Price
Component costs
  Raw material cost.
Direct cost:
  Costs incurred to make a single item. Adds 20% to 40% to component cost.
Gross margin ( Indirect cost):
  Overhead not associated with a single item, i.e. R&D, marketing, manufacturing equipment, taxes, etc.
  Only 4%-12% of income are spent on R&D
Average Selling Price (ASP):
  Component cost + direct cost + indirect cost.
List price :
  Not ASP. Stores add to the ASP to get their cut. Want 50% to 75% of list price.

## Slide 48: The components of price for a $1000 PC

## Slide 49: Cost vs. Price
This gives you insight on how a design decision will affect selling price,
  i.e. changing cost by $1,000 increases selling price by $3,000 to $4,000.
Also, consider volume and price relationship:
  In general, the fewer computers that are sold, the higher the price.
  Also, a decrease in volume causes cost to increase, further increasing price.
Therefore, small changes in cost can have an unexpected large increase in price.

## Slide 50: Computer Design Engineering life cycle
User requirement
Analysis(1.2)
Evaluating Existing
Systems for Bottleneck(app.A)
Technology Trend 1.4
Power Trend 1,5
Cost Trend 1.6
Dependability 1,7
Quantitative Principles
1.9
Simulate New
Designs and
Organizations
Workloads
Implement Next
Generation System
Benchmarks(1.8)
Evaluating for energy-performance cost (1.8)
Notes: Requirement Analysis:
Market analysis: who you will sell 4-1.2
desktop, server, embedded system, HPC
Different markets has different driven motivations.
When design a desktop, it aims to obtain best price-performance.
For the servers, dependability is critical, then the scalability, and throughput.
For the embedded computer systems, price is a key factor, while real-time performance is important . And power efficiency and memory size is always under consideration.
2. Functional requirement: 4-1.3
3. Performance requirement:
4. Power
5. Unfuntional requirements: availability, dependibility 1.7
7. Cost/price

## Slide 51: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summerizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 52: Why Business Continuity ?
Lost Revenue
Know the downtime costs (per hour, day, two days...)
Number of employees impacted (x hours out * hourly rate)
Damaged Reputation
Customers
Suppliers
Financial markets
Banks
Business partners
Financial Performance
Revenue recognition
Cash flow
Lost discounts (A/P)
Payment guarantees
Credit rating
Stock price
Other Expenses
Temporary employees, equipment rental, overtime costs, extra shipping costs, travel expenses...
Direct loss
Compensatory payments
Lost future revenue
Billing losses
Investment losses
Lost Productivity

## Slide 53: Why high Dependability ?
Millions of US Dollars per Hour in Lost Revenue
6.5
3.6
2.8
2.6
2.0
1.6
1.6
1.5
1.3
1.2
1.1
Retail brokerage
Point of sale
Energy
Credit card sales authorization
Telecommunications
Call location
Manufacturing
Financial institutions
Information technology
Insurance
Retail
Source Meta Group, 2005

## Slide 54: Information Availability(5个9)
% Uptime | % Downtime | Downtime per Year | Downtime per Week
98% | 2% | 7.3 days | 3hrs 22 min
99% | 1% | 3.65 days | 1 hr 41 min
99.8% | 0.2% | 17 hrs 31 min | 20 min 10 sec
99.9% | 0.1% | 8 hrs 45 min | 10 min 5 sec
99.99% | 0.01% | 52.5 min | 1 min
99.999% | 0.001% | 5.25 min | 6 sec
99.9999% | 0.0001% | 31.5 sec | 0.6 sec

## Slide 55: Evolvement of Dependability-1
Reliability (可靠性) 1960s
  ----field of fault tolerance and system reliability
Definition
  In general, reliability (systemic def.) is the ability of a person or system to perform and maintain its functions in routine circumstances, as well as hostile or unexpected circumstances.
  The IEEE defines it as ". . . the ability of a system or component to perform its required functions under stated conditions for a specified period of time."
The Institute of Electrical and Electronics Engineers

## Slide 56: Evolvement of Dependability-2
Dependability (可信性)
  1985, Jean-Claude Laprie
    J.C. Laprie. "Dependable Computing and Fault Tolerance: Concepts and terminology," in Proc. 15th IEEE Int. Symp. on Fault-Tolerant Computing, 1985
  International Conference on dependable Systems and networks
  International Symposium on Reliable Distributed Systems
  International Symposium on Software Reliability Engineering.

## Slide 57: Definition 1 of Denpendability
Computer system dependability is The quality of the delivered service such that reliance can justifiably be placed on this service.
  J.C. Laprie. "Dependable Computing and Fault Tolerance: Concepts and terminology," in Proc. 15th IEEE Int. Symp. on Fault-Tolerant Computing, 1985
  reliability, maintainability, availability, safety, are quantitative measures corresponding to distinct perceptions of the same attribute of a system: it’s dependability
  general concept
Notes: Error, fault, failure

## Slide 58: Definition 2 of Denpendability
A. Avizienis, J.-C. Laprie and B. Randell: Fundamental Concepts of Dependability. Research Report No 1145, , April 2001
Denpendability&
Security
Notes: Error, fault, failure

## Slide 59: Related concepts
Availability(可用性) - readiness for correct service
Reliability(可靠性) - continuity of correct service
Safety(平安性?) - absence of catastrophic consequences on the user(s) and the environment
Integrity(完整性) - absence of improper system alteration
Maintainability(可维护性) - ability to undergo modifications and repairs
Confidentiality(机密性), the absence of unauthorized disclosure of information
Security(安全保障) is a composite of Confidentiality, Integrity, and Availability.

## Slide 60: Dependability(可信性)
Service level Agreements(SLA) / Service level objectives (SLO)
  Service accomplishment
  Service interruption
Failures:
  Saccomplishment Sinterruption
Restorations:
  Sinterruption Saccomplishment

## Slide 61: Measurements of Dependability
Module reliability: continuous service accomplishment ( of the time to failure )
  MTTF: Mean Time To Failure
  MTTR: Mean Time To Repair (service interruption)
  FIT: Failure In Time = 1/MTTF
  MTBF: Mean Time Between Failure = MTTF+MTTR
Module availability
  MTTF = MTTF
  MTTF + MTTR MTBF

## Slide 62: Example: disk system
Assumption:
  10 disks, 1000000 hour MTTF
  1 SCSI controller, 500000 hour MTTF
  1 power supply, 1 fan, both 200000 hour MTTF
  1 SCSI cable, 1000000 hour MTTF
Question: MTTR of the whole system
Answer:
  Failure ratesystem = 10*1/1000,000 + 1/500,000 + 1/200,000 + 1/100,000
  = 23000/1000,000,000
  MTTFsystem = 1/Failuresystem = 43500 hours ~ 5 years

## Slide 63: Way to cope with failure
Redundancy:
  Time redundancy: repeat the operation again to see if it is still in erroneous.
  Resource redundancy: have other components to take over from the one that failed.

## Slide 64: Dependability
Compare with
  Trusted computing
  Trustworthy computing
  Credibility

## Slide 65: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summerizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 66: Measuring and Reporting Performance
Comparing Machines
  Execution time (latency)
  Throughput
  MIPS - millions of instructions per second
Comparing Machines Using Sets of Programs
  Choosing which program to evaluate performance
    Benchmark Suites
  Different Means: Arithmetic, Harmonic, and Geometric Means

## Slide 67: Ddifferent perception
Performance means different things to different people, therefore its assessment is subtle
different perception
  Criteria of performance evaluation differs among users and designers
Just a piece of
cake ! Even for 50 guys
Faint ! When will
they bring me the meal?
Sorry, Lady is first !

## Slide 68: Perf. Metrics --response time
Wall-clock time
  Start the program and watch the clock -
  when the program ends, that’s the total wall-clock time
  Also called response time or elapsed time or
  Measures user perception of the system speed
Problems with wall-clock time
  What if more than one program is running on
  the same machine ?
  What if the program asks for user input ?

## Slide 69: Performance Metrics --CPU time
Measures the time the CPU is computing, (not waiting for I/O)
  Measures designer perception of the CPU speed
CPU time is further divided into:
  User time - time spent in user mode
  System time - time spent in the operating system (OS)
Unix time command reports CPU time as:
  90.7u 12.9s 2:39 65%
  90.7 user CPU seconds (in the user’s program)
  12.9 system CPU seconds (in the system calls e.g. printf)
  2 minutes, 39 seconds wall-clock time
  65% of the wall clock time was spent running on the CPU

## Slide 70: Performance Metrics --throughput
Amount of work done in a given time
  Measure administrator perception of the system perf.
We often use throughput to measure
  Number of lines of code per day
  Number bits per second transmitted over a wire
  Number of web pages served
In contrast to latency
  amount of time to produce 1 line of code
  amount of time to send 1 bit over a wire
  Amount of time spent waiting to receive web page
Often, processor performance is only quoted in terms of relative latency
  Program A ran 10 times faster than program B
But, for many apps, throughput much more important than latency
  Financial markets, government statistics (census)

## Slide 71: Response time vs. Throughput
If you improve response time, you usually improve throughput
  Replacing the processor of a computer with a faster version
you can also improve throughput without improving response time
  Adding additional processors to a system that uses multiple processors
  for separate tasks (e.g. handling of airline reservations system)

## Slide 72: Another industry Metric: MIPS
MIPS - Millions of Instructions per Second
When comparing two machines (A, B) with the same instruction set, MIPS is a fair comparison(sometimes…)
But, MIPS can be a “meaningless indicator of performance…”

## Slide 73: Ex: MIPS might be meaningless
Machine A has a special instruction for performing square root calculations. It takes 100 cycles to execute.
Machine B doesn’t have the special instruction -- must perform square root calculations in software using simple instructions (.e.g, Add, Mult, Shift) that each take 1 cycle to execute
Machine A: 1/100 MIPS = 0.01 MIPS
Machine B: 1 MIPS

## Slide 74: Another view: Power consumption and Efficiency
Critical factors for embedded systems:
  cost
  physical size
  memory
  power consumption
Fig. 1.27
  AMD ElanSC520
  AMD K6-2E
  IBM PowerPC 750CX
  NEC VR 5432
  NEC VR 4122
The NEC VR 4122 is the big
winner for its best performance/watt,
though it is the second lowest performing processor.

## Slide 75: Summary of performance metrics
Response (Execution) time
  user perception
  system performance
  the only unimpeachable measure of performance
CPU time
  designer perception
  CPU performance
Throughput
  administrator perception
MIPS
  merchant perception

## Slide 76: Choose Programs to Evaluate Performance
Ideal performance evaluation:
  A random sample of users running their programs and OS commands.
Many different types of benchmarks
  Real applications--- Scientific and engineering
  Modified (or scripted) applications--- focus on specific features
  Kernels --- critical program fragments
  Toy --- small programs, often measure very little
  Synthetic -- created to represent some aspects of a program (e.g., mix of instruction types)
  Database -- a world unto itself
  What really matters is how YOUR application performs

## Slide 77: Something about Synthetic
Synthetic benchmarks :
  Programs that try to "exercise" the system in the same way to match the average frequency of operations and operands of a large set of programs.
  Whetstone and Dhrystone.
  Similar to kernels but are NOT real programs !
  Compiler and hardware optimizations can artificially inflate performance of these benchmarks but not of real programs.
  These benchmarks don’t reward optimizations!
  SQRT(EXP(x))= e x = e x/2 = EXP(X/2)

## Slide 78: Notes on performance benchmark
Benchmarks can focus on specific aspects of a system
  floating point & integer ALU, memory system, I/O, OS
Universal benchmarks can be misleading since hardware and compiler vendors might optimize their design for ONLY these programs
The best types of benchmarks are real applications since they reflect the end-user interest
Architectures might perform well for some applications and poorly for others
Compilation can boost performance by taking advantage of architecture-specific features. Application-specific compiler optimization are becoming more popular.

## Slide 79: SPEC
SPEC - The System Performance Evaluation Cooperative
  founded in 1988 by a small number of workstation vendors who realized that the marketplace was in desperate need of realistic, standardize performance tests.
  Grown to become successful performance standardization bodies with more than 40 member companies.
  http://www.spec.org
SPEC's Philosophy
  The goal of SPEC is to ensure that the marketplace has a fair and useful set of metrics to differentiate candidate systems.
  The basic SPEC methodology is to provide the benchmarker with a standardized suite of source code based upon existing applications

## Slide 80: SPEC benchmarks： Desktop Benchmarks
CPU-intensive benchmarks
  SPEC89
  SPEC92
  SPEC95
  SPEC2000
  SPEC CPU2006 ( 12 CINT2006, 17 CFP2006)
graphics-intensive benchmarks
  SPEC2000
    SPECviewperf
      is used for benchmarking systems supporting the OpenGL graphics library
    SPECapc
      consists of applications that make extensive use of graphics.

## Slide 81: SPEC INT 95 Benchmark descriptions

## Slide 82: SPEC FP 95 Benchmark Descriptions

## Slide 83: New SPEC Int 2000 Benchmarks

## Slide 84: New SPEC FP 2000 Benchmarks

## Slide 85: SPEC benchmarks Server Benchmarks
SPECrate--processing rate of a multiprocessor
  SPEC CPU2000—throughput-oriented benchmark
  SPECrate—processing rate of a multiprocessor
  SPECSFS--file server benchmark
  SPECWeb--Web server benchmark
  Transaction-processing (TP) benchmarks
  TPC benchmark—Transaction Processing Council
    TPC-A, 1985
    TPC-C, 1992,
    TPC-H TPC-RTPC-W

## Slide 86: SPEC benchmarks Embedded Benchmarks
EDN Embedded Microprocessor Benchmark Consortium (or EEMBC, pronounced “embassy”).

## Slide 87: Running Benchmarks
Key factor: Reproducibility by other experimenters.
Details, details, and more details !!! List all assumptions and conditions of your experiments.
  i.e. program input, version of the program, version of the compiler, optimization level, OS version, main memory size, disk types, etc.
A system’s software configuration can significantly affect the performance results for a benchmark.

## Slide 88: Comparing Two Machines
Machine CPI Clock Period Avg Instruction Time (secs)
Machine A 1.2 2 ns
Machine B 2.5 1 ns
CPU Time = # of instructions executed * avg instruction time
Assume 1,000,000, 000 instructions
Machine A: 1,000,000,000 * 2.4ns = 2.4 seconds
Machine B: 1,000,000,000 * 2.5ns = 2.5 seconds
Which machine is faster? Machine A
How much faster? 2.5 / 2.4 = 1.04 times faster

## Slide 89: Comparing Performance
Often, we want to compare the performance of different machines or different programs. Why?
  To help engineers understand which is “better”
  To give marketing a “silver bullet” for the press release
  To help customers understand why they should buy <my machine>
Performance and Execution time are reciprocals
Maximizing performance means minimizing response (execution) time

## Slide 90: Common used phrases
“Performance of P1 is better than P2 ” is, for a given work load L, P1 takes less time to execute L than P2 does
performance(P1) > Performance(P2)
 Execution Time(P1, L) < Execution Time(P1, L)
“Processor X is n times fast than Y” is

## Slide 91: Comparing Performance Across Multiple Programs
  A is 10 times faster than B for program 1
  B is 10 times faster than A for program 2
  A is 20 times faster than C for program 1
  C is 50 times faster than A for program 2
  B is 2 times faster than C for program 1
  C is 5 times faster than B for program 2
Each statement above is correct…,
…but we want to know which machine is the best?

## Slide 92: Let’s Try a Simpler Example
Two machines timed on two benchmarks
  How much faster is Machine A than Machine B?
Attempt 1: ratio of run times, normalized to Machine A times
  program1: 4/2 program2 : 8/12
  Machine A ran 2 times faster on program 1, 2/3 times faster on program 2
  On average, Machine A is (2 + 2/3) /2 = 4/3 times faster than Machine B
It turns this “averaging” stuff can fool us

## Slide 93: Example: Second answer
Two machines timed on two benchmarks
  How much faster is Machine A than Machine B?
Attempt 2: ratio of run times, normalized to Machine B times
  program 1: 2/4 program 2 : 12/8
  Machine A ran program 1 in 1/2 the time and program 2 in 3/2 the time
  On average, (1/2 + 3/2) / 2 = 1
  Put another way, Machine A is 1.0 times faster than Machine B

## Slide 94: Example: Third answer
Two machines timed on two benchmarks
  How much faster is Machine A than Machine B?
Attempt 3: ratio of run times, aggregate (total sum) times,
  Machine A took 14 seconds for both programs
  Machine B took 12 seconds for both programs
  Therefore, Machine A takes 14/12 of the time of Machine B
  Put another way, Machine A is 6/7 faster than Machine B

## Slide 95: Which is Right?
Question:
  How can we get three different answers?
Solution
  Because, while they are all reasonable calculations…
  …each answers a different question
We need to be more precise in understanding and posing these performance & metric questions

## Slide 96: Arithmetic and Harmonic Mean
Total Execution Time: A Consistent Summary Measure
  Arithmetic mean is the average of the execution time that tracks total execution time.
  If performance is expressed as a rate, then the average that tracks total execution time is the harmonic mean

## Slide 97: Problems with Arithmetic Mean
Applications do not have the same probability of being run
Longer programs weigh more heavily in the average
For example, two machines timed on two benchmarks
Machine A Machine B
Program 1 2 seconds (20%) 4 seconds (20%)
Program 2 12 seconds (80%) 8 seconds (80%)
If we do arithmetic mean, Program 2 “counts more” than Program 1
  an improvement in Program 2 changes the average more than a proportional improvement in Program 1
But perhaps Program 1 is 4 times more likely to run than Program 1

## Slide 98: Weighted Execution Time
Often, one runs some programs more often than others. Therefore, we should weight the more frequently used programs’ execution time
Weighted Harmonic Mean

## Slide 99: Using a Weighted Sum or weighted average
Allows us to determine relative performance 10/7.2 = 1.38
--> Machine B is 1.38 times faster than Machine A

## Slide 100: Another Solution
Normalize run time of each program to a reference
So when we normalize A to B, and average, it looks like A & B are the same.
But when we normalize B to A, it looks like B is 33% better!

## Slide 101: Example
33744 1
W(B)1=  = 0.909
10×(1/10＋1/100)
1
W(B)2=  = 0.091
100×(1/10＋1/100)
Equal-time weighting

## Slide 102: Geometric Mean
Used for relative rate or performance numbers
Geometric mean’s nice property
  Geometric mean(Xi) Xi
  Geometric mean(Yi) Yi
=Geometric mean( )

## Slide 103: Using Geometric Mean
Drawback:
  Geometric mean does NOT predict run time
Normalizes.
  Each application now counts equally.
  Advantage: Irrelevance of the reference computer in relative performance

## Slide 104: Summary of comparing performance
Total execution time or arithmetic mean
  consistent result
  programs in the workload are NOT always run an equal number of times
Weighted arithmetic mean
  take into account the frequency of use in the workload
  solution depends on which machine is the reference.
Normalized Geometric Mean---SPEC Ratio
  consistent result, no matter which machine is the reference.
  Geometric mean does NOT predict run time
Ideal solution : Measure a real workload and weight the programs according to their frequency of execution.
What really matters is how YOUR application performs

## Slide 105: New SPEC Performance Numbers
Geometric Mean of 12 (SpecInt) and 14 (SpecFP) Benchmarks
  Performance measured against SPARC 10/40
2000 Performance Numbers (Microprocessor Report, Dec. 2000)

## Slide 106: New SPEC Performance Numbers
Geometric Mean of 12 (SpecInt) and 14 (SpecFP) Benchmarks
  Performance measured against SPARC 10/40
2001 Performance Numbers (Microprocessor Report, Aug. 2001)

## Slide 107: Topics in Chapter
1.1 Why take this course ?
1.2 Classes of computers in current computer market
1.3 Defining computer architecture and What’s the task of computer design?
1.4 Trends in Technology
1.5 Trends in power in Integrated circuits
1.6 Trends in Cost
1.7 Dependability
1.8 Measuring, Reporting and summerizing Perf.
1.9 Quantitative Principles of computer Design
1.10 Putting it altogether

## Slide 108: 1.9 Quantitative Principles
Take advantage of parallelism
Principle of Locality
Focus on the common case
Amdahl's Law
CPU Performance Equation

## Slide 109: Take advantage of parallelism
Most important methods of improving performance
Parallelism levels
  System level: use multiple processors
  Instruction level:
    Pipelining
  Operation level:
    set-associate cache
    Pipelined function unit
Any other examples ?

## Slide 110: Principle of Locality
Program Property: Programs tend to reuse data and instructions they have used recently.
Rule of thumb:
  a program spends 90% of its execution time in only 10% of the code.
Temporal locality
  Recently accessed items are likely to be accessed in the near future.
Spatial locality
  Items whose addresses are near one another tend to be referenced close together in time.
Any example ?

## Slide 111: Focus on the common case
The most important and pervasive principle of computer design.
  Power, resource allocation, performance, dependability.
  Rule of thumb: simple is fast.
  Frequent case is often simpler and can be done faster.
A fundamental law, called Amdahl’s Law, can be used to quantify this principle.

## Slide 112: Amdahl’s Law
The performance improvement to be gained from using some faster mode of execution is limited by the fraction of the time the faster mode can be used.
Example

## Slide 113: Amdahl’s law
Increasing the clock rate would not affect memory access time
Using a floating point processing unit does not speed integer ALU operations

## Slide 114: Amdahl’s law
Amdahl's law defines the speedup
If we know two factors:
  Fraction enhanced : Fraction of computation time in original machine that can be converted to take advantage of the enhancement.
  Speedup enhanced in enhanced mode : Improvement gained by enhanced execution mode:

## Slide 115: Speedup Equation
Example:
  A server system with an enhanced CPU( 10 times faster than the original one) used for Web serving. Assuming the original CPU is busy with computation 40% of the time and is waiting for I/O 60% of the time.
Answer:
  Fractionenhanced = 0.4, Speedupenhanced =10
  Speedup = 1 = 1 = 1.56
  0.6 + 0.4 0.64
  10

## Slide 116: Another Example
Implementations of floating-point (FP) square root vary significantly in performance
Two enhancement proposal
  One proposal is to enhance the FPSQR hardware and speed up this operation by a factor of 10.
  The alternative is just to try to make all FP instructions in the graphics processor run faster by a factor of 1.6;
Assuming
  FP square root (FPSQR) is responsible for 20% of the execution time of a critical graphics benchmark.
  FP instructions are responsible for a total of 50% of the execution time for the application.
  The design team believes that they do both enhancement with the same effort.
Compare these two design alternatives.

## Slide 117: Solution of the example

## Slide 118: Example for dependability-1
Given:
  Failure ratesystem = 10*1/1000,000 + 1/500,000 + 1/200,000 + 1/100,000
  10 + 2 + 5 + 5 + 1
  =-----------------------------
  1,000,000
  = 23000/1000,000,000
  So, Power failure% = 5/23 = 0.22

## Slide 119: Example for dependability-2
Reliability of the power supply can be improved via redundancy:
  200000  830,000,000 ~ 4150X 5/23
Reliability improvement
1
= ----------------------------- = 1.28
(1-0.22) + 0.22/4150

## Slide 120: What the Amdahl’s Law imply ?
If an enhancement is only usable for a fraction of task, then the total speedup will be no more than 1/ (1-F).
Serve the guide
  to how much an enhancement will improve performance
  to how to distribute resource to improve cost-performance
Useful for comparing
  the overall system performance of two alternatives,
  two CPU design alternatives
We can improve the performance by
  increasing the Fractionenhanced
  or, increasing the Speedupenhanced

## Slide 121: The CPU Performance Equation
The “Iron Law” of processor performance:
  Often it is difficult to measure the improvement in time using a new enhancement directly.
CPU Performance Equation

## Slide 122: Calculation of CPU Time
CPU time = Instruction count  CPI  Clock cycle time
Or
Architecture --> Implementation --> Realization
Compiler Designer Processor Designer Chip Designer

## Slide 123: Related technologies
CPU performance is dependent upon 3 characteristics:
  clock cycle (or rate) ( CCT )
  clock cycles per instruction ( CPI )
  instruction count. ( IC )
One difficulty: It is difficult to change one in isolation of the others.
Inst Count CPI Clock Rate
Program X
Compiler X (X)
Inst. Set. X X
Organization X X
Technology X

## Slide 124: Other format of CPU Performance Equation

## Slide 125: Example of CPUtime calculation
Suppose we have made the following measurements:
  Frequency of FP operations (other than FPSQR) = 25%
  Average CPI of FP operations = 4.0
  Average CPI of other instructions = 1.33
  Frequency of FPSQR = 2%
  CPI of FPSQR = 20
Two design alternatives
  decrease the CPI of FPSQR to 2
  decrease the average CPI of all FP operations to 2.5.
Compare these two design alternatives using the CPU performance equation.

## Slide 126: Answer to the question
Since the CPI of the overall FP enhancement is slightly lower, its performance will be marginally better.

## Slide 127: Compare the result with that from Amdahl’s law
This is the same speedup we obtained using Amdahl’s Law:

## Slide 128
Suppose that there are four types of operations in an application. After making enhancements to the original function units, each type of operation gains performance improvement as shown in the following table.
1) What’s the enhanced speedup of each operation respectively after improving?
2) What’s the overall speedup of the application respectively after only improving Op2 or Op4?
Hint: Calculate the overall speedup considering only one of the enhanced function units is used. There are 2 situations.
Operation Type | IC (total 100) | CPI before enhancement | CPI after enhancement
Op1 | 10 | 2 | 1
Op2 | 30 | 20 | 15
Op3 | 35 | 10 | 3
Op4 | 25 | 4 | 1

## Slide 129: Performance & price-performance
Factors that responsible for the wide variation in price
  Different levels of expandability
  Use of cheaper disks and cheaper memory
  Cost of CPU varies
  Software differences
  Lower-end system use PC commodity parts in fans, power supply, support chip sets
  Commoditization effect

## Slide 130: Five desktop and rack-mountable systems
1GB ECC SDRAM, 80GB disk
Expandability(可扩展性):
Sun Java worktation < Dell < HP BL25p
Cost of processor: die size, L2 cache, clock rate, cache size
Softerware difference

## Slide 131: Price-performance www.spec.org

## Slide 132: Messurements-1
For Servers
TPC-C : standard industry benchmark for OLTP
    Reasonable approximation
    Measure total system performance
    Rules of measurement are very complete
    Vendors devote significant effort
    Report both performance & price-performance

## Slide 133: Price-performance TPC-C 2005.7

## Slide 134: TPC-C & TPC-E
TPC(TransactionProcessing PerformanceCouncil)
  10 members http://www.tpc.org
TPC-C:
  benchmark for OnLine Transaction Processing
  simulates a complete environment where a population of terminal operators executes transactions against a database
TPC-E
  simulates the OLTP workload of a brokerage firm
TPC-C&TPC-E
  http://www.searchsv.com.cn/showcontent_13524.htm

## Slide 135: tpsE & tpsE/&100000

## Slide 136: Power performance for 3 servers
Best power perf

## Slide 137: Fallacies & pitfalls
Pitfall(易犯的错误):
  Falling prey to Amdahl’s Law.
    Not to try to improve some unit of small F
  A single point of failure
    An example of dependability
    Don’t forget the single fan !

## Slide 138: Fallacy1 : the cost of the processor dominates the cost of the system.

## Slide 139: Fallacy
Benchmarks remain valid indefinitely
  “Benchmarksmanship” “benchmark engineering”
The rated mean time to failure of the disks is 1200000 hours or almost 140 years, so disks practically never fail.
  Real-world MTTF is about 2-4 times worse than manufacturer’s MTTF for ATA disks, 4-8 times worse for SCSI disks
  ( ATA: AT Attachment )
  SCSI: Small Computer System Interface )
Peak performance tracks observed performance.