## Slide 1: Chapter 2
Instructions: Language of the Computer

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction
2.1 Introduction

## Slide 3: The RISC-V Instruction Set
Used as the example throughout the book
Developed at UC Berkeley as open ISA
Now managed by the RISC-V Foundation (riscv.org)
Typical of many modern ISAs
  See RISC-V Reference Data tear-out card
Similar ISAs have a large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …

## Slide 4: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c // a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours（有利于）regularity.
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware
2.2 Operations of the Computer Hardware

## Slide 7: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled RISC-V code:
add t0, g, h // temp t0 = g + h add t1, i, j // temp t1 = i + j sub f, t0, t1 // f = t0 - t1

## Slide 8: Register Operands
Arithmetic instructions use register operands
RISC-V has a 32 × 64-bit register file in RV64I.
  Use for frequently accessed data
  64-bit data is called a “doubleword”
    32 x 64-bit general purpose registers x0 to x30(应是x31?)
  32-bit data is called a “word”
RISC-V has a 32 × 32-bit register file in RV32I.
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware
c.f.的意思是比较compare
【拉丁语】 confer（比较）

## Slide 9: RISC-V Registers
x0: the constant value 0
x1: return address
x2: stack pointer
x3: global pointer
x4: thread pointer
x5 – x7, x28 – x31: temporaries
x8: frame pointer
x9, x18 – x27: saved registers
x10 – x11: function arguments/results
x12 – x17: function arguments
RISC-V-Reader-Chinese-v2p1.pdf 在P43说：

## Slide 10
x0: the constant value 0
x1: return address
x2: stack pointer
x3: global pointer
x4: thread pointer
x5 – x7, x28 – x31: temporaries
x8: frame pointer
x9, x18 – x27: saved registers
x10 – x11: function arguments/results
x12 – x17: function arguments
右边资料来自于《RISC-V手册》【RISC-V-Reader-Chinese-v2p1.pdf】 P28

## Slide 11: RISC-V register conventions
Name | Register name | Usage | Preserved On call?
x0 | 0 | The constant value 0 | n.a.
x1(ra) | 1 | Return address(link register) | yes
x2(sp) | 2 | Stack pointer | yes
x3(gp) | 3 | Global pointer | yes
x4(tp) | 4 | Thread pointer | yes
x5-x7 | 5-7 | Temporaries | no
x8-x9 | 8-9 | Saved | yes
x10-x17 | 10-17 | Arguments/results | no
x18-x27 | 18-27 | Saved | yes
x28-x31 | 28-31 | Temporaries | no
Notes: x5

## Slide 12: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in x19, x20, …, x23
Compiled RISC-V code:
add x5, x20, x21 //x5=t0 add x6, x22, x23 //x6=t1 sub x19, x5, x6

## Slide 13: 2.3 Operands of the Computer Hardware 2.3.1 Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
RISC-V does not require words to be aligned in memory
  Unlike some other ISAs

## Slide 14: Memory Operands
Memory is byte addressed
  Each address identifies an 8-bit byte
RISC-V is Little Endian
  Least-significant byte at least address of a word
  c.f. Big Endian: most-significant byte at least address

## Slide 15: Memory Operand Example
C code:
A[12] = h + A[8];
  h in x21, base address of A in x22
  Each element of array A is doubleword.
Compiled RISC-V code:
  Index 8 requires offset of 64
    8 bytes per doubleword
ld x9, 64(x22) add x9, x21, x9 sd x9, 96(x22)

## Slide 16: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 17: 2.3.2 Constant or Immediate Operands
Constant data specified in an instruction
addi x22, x22, 4
Make the common case fast（加速经常性操作）
  Small constants are common
  Immediate operand avoids a load instruction
Immediate Operands

## Slide 18: Constant or Immediate Operands
Constant or immediate Operands
  Many time a program will use a constant in an operation
    Incrementing index to point to next element of array
    Add the constant 4 to register x22
    Assuming AddrConstants4 is address pointer of constant 4
        AddrConstants4是具体的位移量，例如24
ld x9, AddrConstant4(x3) // x9=constant 4
add x22, x22, x9
  Immediate: Other method for adding constant 4 to x22
    Avoids the load instruction
    Offer versions of the instruction
    addi x22, x22, 4 // x22= x22+ 4
  Constant zero: a register x0
Design Principle 3
    Make the common case fast: (why?) Constant operands occur frequently it is very common Loading them from memory is very slow
4
….
x3
AddrConstants4

## Slide 19: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 … 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 64 bits: 0 to +18,446,774,073,709,551,615
§2.4 Signed and Unsigned Numbers
第三章已讲过，不讲
2.4 Signed and Unsigned Numbers

## Slide 20: 2’s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 … 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 64 bits: −9,223,372,036,854,775,808 to 9,223,372,036,854,775,807
2^31=2 147 483 648
第三章已讲过，不讲

## Slide 21: 2’s-Complement Signed Integers
Unsigned Binary Integers
Bit 63 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2’s complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111
第三章已讲过，不讲

## Slide 22: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 0010two
  –2 = 1111 1111 … 1101two + 1 = 1111 1111 … 1110two
第三章已讲过，不讲

## Slide 23: Sign Extension
Representing a number using more bits
  Preserve the numeric value
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110
In RISC-V instruction set
  lb: sign-extend loaded byte
  lbu: zero-extend loaded byte

## Slide 24: 2.5 Representing Instructions in the Computer
Instructions are encoded in binary
  Called machine code
RISC-V instructions
  Encoded as 32-bit instruction words
  Regularity!
§2.5 Representing Instructions in the Computer

## Slide 25: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 26: RISC-V R-format Instructions
Instruction fields
  opcode: operation code
  rd: destination register number
  funct3: 3-bit function code (additional opcode)
  rs1: the first source register number
  rs2: the second source register number
  funct7: 7-bit function code (additional opcode)
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits

## Slide 27: R-format Example
add x9,x20,x21
0000 0001 0101 1010 0000 0100 1011 0011two =
015A04B316
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0
21
20
9
0
51
0000000
10101
10100
01001
000
0110011

## Slide 28: RISC-V I-format Instructions
Immediate arithmetic and load instructions
  rs1: source or base address register number
  immediate: constant operand, or offset added to base address
    2s-complement, sign extended
Design Principle 3: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
  ld x9, 64(x22) sd x9, 96(x22)
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits

## Slide 29: RISC-V S-format Instructions
Different immediate format for store instructions
  rs1: base address register number
  rs2: source operand register number
  immediate: offset added to base address
    Split so that rs1 and rs2 fields always in the same place
rs2
rs1
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
imm[11:5]
imm[4:0]

## Slide 31: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs and produce new programs.
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 32: 2.6 Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | RISC-V
Shift left | << | << | slli
Shift right | >> | >>> | srli
Bit-by-bit AND | & | & | and, andi
Bit-by-bit OR | ¦ | ¦ | or, ori
Bit-by-bit XOR | ^ | ^ | xor, xori
Bit-by-bit NOT | ~ | ~ | 
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations

## Slide 33
来源：【RISC-V-Reader-Chinese-v2p1.pdf 】 P120

## Slide 34: Shift left/right logical Immediate
immed: how many positions to shift
Shift left logical Immediate, I-type
  Shift left and fill with 0 bits
  slli by i bits multiplies by 2i,
  slli x10,x22,3 // x10x22*23
Shift right logical
  Shift right and fill with 0 bits
  srli by i bits divides by 2i (unsigned only)
rs1
rd
funct3
opcode
6 bits
7 bits
5 bits
5 bits
3 bits
funct6
immed
6 bits

## Slide 35: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and x9,x10,x11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x11
x9
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00001100 00000000

## Slide 36: OR Operations
Set some bits to 1, leave others unchanged
or x9,x10,x11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x11
x9
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00111101 11000000

## Slide 37: XOR Operations
reverse some bits, leave others unchanged
xor x9,x10,x12 // “NOT” operation
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x12
x9
11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
11111111 11111111 11111111 11111111 11111111 11111111 11110010 00111111

## Slide 38: Conditional Branches
Branch（转移） to a labeled instruction if a condition is true
  Otherwise, continue sequentially
Branch target address must be even(偶数)
  Error: Jump to instruction address 15
  Range:-4096 ---- 4094
beq rs1, rs2, L1 ------SB类型指令
  if (rs1 == rs2) branch to instruction labeled L1
bne rs1, rs2, L1 ------SB类型指令
  if (rs1 != rs2) branch to instruction labeled L1
§2.7 Instructions for Making Decisions
2.7 Instructions for Making Decisions

## Slide 39: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, h, i, j
  x19, x20,x21,x22,x23
Compiled RISC-V code:
bne x22, x23, Else add x19, x20, x21 beq x0,x0,Exit // unconditional Else: sub x19, x20, x21 Exit: …
Assembler calculates addresses

## Slide 40
来源：【RISC-V-Reader-Chinese-v2p1.pdf】 P121
SB类型指令格式
SB类型指令中，PC 总是本指令的地址，不是下一条指令的地址

## Slide 41
来源：【RISC-V-Reader-Chinese-v2p1.pdf】 P123
SB类型指令格式

## Slide 42
书P115 有BNE指令的机器码说明，见下图，红框内机器码1100111是错的，改成1100011，依据：【RISC-V手册】（RISC-V-Reader-Chinese-v2p1.pdf）P123/总162页。 SB类型的指令（BEQ，BNE，BLT，BLTU，BGE，BGEU），指令机器码仅提供了imm[12:1]共12位，最右边应补1位0（等价于左移1位，即下面划红线文字所说的乘2），变成13位，是13位补码2进制数，范围-4096到+4094。

## Slide 43
很好的RISCV汇编器网站，能汇编成机器码
https://venus.cs61c.org/

## Slide 44
0x1000: loop: add t3, s3, s4
0x1004: bne t3, t4, Loop // 也可写作bne,t3,t4,-4 //when instruction // “bne” is executing, PC=0x1004, 上面红色的-4是字节为单 // 位的,写成-8或-2都是错！！！
offset = -4，补码表示13位offset = 1 1111 1111 11002，
去掉最低位的12位offset= 1111 1111 1110
offset 12,11,10,9,8,7,6,5,4,3,2,1
t4(X29) t3(X28)
1111111， 11101, 11100, 001, 11101, 1100011
Machine code:
1111 1101, 1110 0001, 1110 1110 0011
0xFFDE 1EE3 <==> bne t3, t4, -4
Machine code of 【bne t3, t4, Loop】

## Slide 45: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in x22, k in x24, base address of save in x25
Compiled RISC-V code:
Loop: slli x10, x22, 3 // x10x22*8 add x10, x10, x25 ld x9, 0(x10) bne x9, x24, Exit
addi x22, x22, 1 beq x0, x0, Loop Exit: …

## Slide 46
//beq x0,x0, -20 // beq x0,x0, -0x14

## Slide 47: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
Feature : every instruction in basic block should be executed sequentially
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 48: More Conditional Operations
blt rs1, rs2, L1 ------SB类型指令
  if (rs1 < rs2) branch to instruction labeled L1
bge rs1, rs2, L1 ------SB类型指令
  if (rs1 >= rs2) branch to instruction labeled L1
Example
  if (a > b) a += 1;
  a in x22, b in x23
  bge x23, x22, Exit // branch if b >= a
  addi x22, x22, 1
  Exit:

## Slide 50: Signed vs. Unsigned
Signed comparison: blt, bge
Unsigned comparison: bltu, bgeu
Example
  x22 = 1111 1111 1111 1111 1111 1111 1111 1111
  x23 = 0000 0000 0000 0000 0000 0000 0000 0001
  x22 < x23 // signed
    –1 < +1
  x22 > x23 // unsigned
    +4,294,967,295 > +1

## Slide 51: Procedure Calling
Steps required
  Place parameters in registers x10 to x17
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call (address in x1)
§2.8 Supporting Procedures in Computer Hardware
2.8 Supporting Procedures in Computer Hardware

## Slide 52: Procedure Call Instructions
Procedure call: jump and link
jal x1, ProcedureLabel ----UJ类型指令
  Address of following instruction (return address) is put into x1
  2 function
    (1). Jumps to target label: jal x0, L1
    == pseudo-instruction 【 j L1 】
    (2). call a procedure: jal x1,P1
Procedure return: jump and link register
jalr x0, 0(x1) ----------I类型指令
  Like jal, but jumps to (0 + address in x1)
  Use x0 as rd (x0 cannot be changed)
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 53
来源：【RISC-V手册】（RISC-V-Reader-Chinese-v2p1.pdf）P148-149/总162页
UJ类型指令（仅jal）格式，jalr是I类型指令

## Slide 55
bne x22, x23, Else
jal x1,Else //也可写成 jal x1,8, 这里位移量8的单位是字节， // 很容易错写成 jal x1,4 ，因为上面这条jal x1,8的指令机器码中位移量是4
beq x0,x0,Exit //上面这条jal x1,8的指令机器码中位移量是4
Else: sub x19, x20, x21
Exit: add x1,x3,x2
BEQ、JAL 所带的标号写成数值怎么写？

## Slide 56
beq x10, x0, L1 // target location：-4096 to 4094 away from this beq // instruction, 13 bit offset including appended 1-bit 0
jal x0, L1 // target location：-2^20 to 2^20-2 away from this jal // instruction, 21 bit offset including appended 1-bit 0
jalr x0, 0(x1) // target location：64-bit target PC address in X1,any // palce

## Slide 57
x0: the constant value 0
x1: return address
x2: stack pointer
x3: global pointer
x4: thread pointer
x5 – x7, x28 – x31: temporaries
x8: frame pointer
x9, x18 – x27: saved registers
x10 – x11: function arguments/results
x12 – x17: function arguments
右边资料来自于《RISC-V手册》【RISC-V-Reader-Chinese-v2p1.pdf】 P28

## Slide 58: 2.8.1 Using More Registers
Leaf Procedure: Procedures that do not call others are called leaf procedures. C code example:
long long int leaf_example ( long long int g, long long int h, long long int i, long long int j) { long long int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in x10, …, x13, f in x20(s4)
  temporaries x5(t0), x6
  Need to save x5, x6, x20 on stack
书P73

## Slide 59: Leaf Procedure Example
RISC-V code:
leaf_example:
addi sp,sp,-24
sd x5,16(sp) // x5 is t0
sd x6,8(sp) // x6 is t1
sd x20,0(sp) // x20 is s4
add x5,x10,x11
add x6,x12,x13
sub x20,x5,x6
addi x10,x20,0 //move a0,s4
ld x20,0(sp)
ld x6,8(sp)
ld x5,16(sp)
addi sp,sp,24
jalr x0,0(x1) // jr ra
Save x5, x6, x20 on stack
x5 = g + h
x6 = i + j
f = x5 – x6
//copy f to return register a0
Resore x5, x6, x20 from stack
//Return to caller

## Slide 60: Local Data on the Stack

## Slide 61: Register Usage
x5 – x7, x28 – x31: temporary registers
  Not preserved by the callee
x8 – x9, x18 – x27: saved registers
  If used, the callee saves and restores them

## Slide 62: Leaf Procedure Example
RISC-V code:
leaf_example:
addi sp,sp,-8
sd x5,16(sp) // x5 is t0
sd x6,8(sp) // x6 is t1
sd x20,0(sp) // x20 is s4
add x5,x10,x11
add x6,x12,x13
sub x20,x5,x6
addi x10,x20,0 //move a0,s4
ld x20,0(sp)
ld x6,8(sp)
ld x5,16(sp)
addi sp,sp,8
jalr x0,0(x1) // jr ra
Save x5, x6, x20 on stack
x5 = g + h
x6 = i + j
f = x5 – x6
//copy f to return register a0
Resore x5, x6, x20 from stack
//Return to caller

## Slide 63: 2.8.2 Nested Procedures
Non-Leaf Procedures: Procedures that call other procedures
For nested call, caller needs to save each following register on the stack before modifying it:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 64: Non-Leaf Procedures
Procedures that call other procedures, e.g.
  int p1(a0,a1,old-a2) // ra has the return address
    { …..
    t3=j+4
    p2(a0,a1,new-a2) // jal p2 (old ra is modified )
    K=old-a2*2 //old-a2 must be saved before call p2
    m=t3-9 // t3 must be saved before call p2
    …..}
For nested call, caller needs to save each following register on the stack before modifying it:
    Its return address
    Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 65: Saves on Stack
65
Procedure A call procedure B
Caller A saves：
  a0-a7 -- if you will set new arguments for the callee and a0-a7 will still be used after return, old arguments must be saved before the jal instruction over-writes them. Conditionally save.
  ra -- must be saved before the jal proc-B instruction over-writes this value. But it need not be saved in leaf procedure. Unconditionally save.
  t0-t9 -- if you plan to use your temps after callee return, save them. note that callees are free to use temps as they please. Conditionally save.
  You need not save s0-s11 as the callee will take care of them
Callee B saves：
  s0-s11 -- before the callee B uses such a register, it must save the old contents since the caller will usually need it on return. Unconditionally save.

## Slide 66: Non-Leaf Procedure Example
C code:
long long int fact (long long int n) { if (n < 1) return 1; else return n * fact(n - 1); }
  Argument n in x10
  Result in x10

## Slide 67
RISC-V code:
fact:
addi sp,sp,-16
sd x1,8(sp)
sd x10,0(sp)
addi x5,x10,-1
bge x5,x0,L1
addi x10,x0,1
addi sp,sp,16
jalr x0,0(x1)
L1: addi x10,x10,-1
jal x1,fact
addi x6,x10,0
ld x10,0(sp)
ld x1,8(sp)
addi sp,sp,16
mul x10,x10,x6
jalr x0,0(x1)
Save return address and n on stack
x5 = n - 1
Else, set return value to 1
n = n - 1
if n >= 1, go to L1
call fact(n-1)
Pop stack, don’t bother restoring values
Return
Restore caller’s n
Restore caller’s return address
Pop stack
return n * fact(n-1)
return
move result of fact(n - 1) to x6

## Slide 68
RISC-V code:
fact:
addi sp,sp,-16
sd ra,8(sp)
sd a0,0(sp)
addi t0,a0,-1 //x5 is t0
bge t0,x0,L1
addi a0,x0,1
addi sp,sp,16
jalr x0,0(ra) //jr ra
L1: addi a0,a0,-1
jal ra,fact
addi t1,a0,0 //mov t1,a0
ld a0,0(sp)
ld ra,8(sp)
addi sp,sp,16
mul a0,a0,t1
jalr x0,0(ra) //jr ra
Save return address and n on stack
X5=t0= n - 1
Else, set return value to 1
n = n - 1
if n >= 1, go to L1
call fact(n-1)
Pop stack, don’t bother restoring values
Return
Restore caller’s n
Restore caller’s return address
Pop stack
return n * fact(n-1)
return
move result of fact(n - 1) to t1
long long int fact (long long int n) { if (n < 1) return 1; else return n * fact(n - 1); }

## Slide 69: 2.8.3 Allocating Space for New Data on the Stack
Local data allocated by callee
  e.g., C automatic variables will be allocated in stack when registers are exhausted.
Procedure frame (activation record)
  Used by some compilers to manage stack storage
Local data
vs
global data

## Slide 70: 2.8.4 Allocating Space for New Data on the Heap
Text: program code
Static data: e.g. m, n at right example
  global variables, static variables in C, constant arrays and strings
  x3 (global pointer) initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc() in C, new in Java
Stack: automatic storage
  Such as right 【 int j[100]; 】
Address of first byte in static data is 0000 0000 1000 0000hex
int m; /* global variable */
void strcpy (char x[], char y[]) { int i,j[100];
static int n; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Memory Layout

## Slide 71: Character Data
Byte-encoded character sets
  ASCII: 128 characters
Unicode: 32-bit character set, 0-0x10FFFF
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings
§2.9 Communicating with People
2.9 Communicating with People

## Slide 73: Byte/Halfword/Word Operations
RISC-V byte/halfword/word load/store
  Load byte/halfword/word: Sign extend to 64 bits in rd
    lb rd, offset(rs1)
    lh rd, offset(rs1)
    lw rd, offset(rs1)
  Load byte/halfword/word unsigned: Zero extend to 64 bits in rd
    lbu rd, offset(rs1)
    lhu rd, offset(rs1)
    lwu rd, offset(rs1)
  Store byte/halfword/word: Store rightmost 8/16/32 bits
    sb rs2, offset(rs1)
    sh rs2, offset(rs1)
    sw rs2, offset(rs1)

## Slide 74: String Copy Example
C code:
  Null-terminated string
void strcpy (char x[], char y[]) { size_t i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }

## Slide 75: String Copy Example
RISC-V code:
strcpy: addi sp,sp,-8 // adjust stack for 1 doubleword sd x19,0(sp) // push x19 add x19,x0,x0 // i=0 L1: add x5,x19,x11 // x5 = addr of y[i] lbu x6,0(x5) // x6 = y[i] add x7,x19,x10 // x7 = addr of x[i] sb x6,0(x7) // x[i] = y[i] beq x6,x0,L2 // if y[i] == 0 then exit addi x19,x19, 1 // i = i + 1 jal x0,L1 // next iteration of loop L2: ld x19,0(sp) // restore saved x19 addi sp,sp,8 // pop 1 doubleword from stack jalr x0,0(x1) // and return
void strcpy (char x[], char y[]) { size_t i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }

## Slide 76: String Copy Example
RISC-V code:
strcpy: addi sp,sp,-8 // adjust stack for 1 doubleword sd x19,0(sp) // push x19 (x19=s3,used as i) add x19,x0,x0 // i=0 L1: add x5,x19,a1 // x5=t0= addr of y[i] lbu x6,0(x5) // x6 = y[i] add x7,x19,a0 // x7 = addr of x[i] sb x6,0(x7) // x[i] = y[i] beq x6,x0,L2 // if y[i] == 0 then exit addi x19,x19, 1 // i = i + 1 jal x0,L1 // j L1 // next iteration of loop L2: ld x19,0(sp) // restore saved x19 addi sp,sp,8 // pop 1 doubleword from stack jalr x0,0(x1) // jr ra // and return
void strcpy (char x[], char y[]) { size_t i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }

## Slide 77: String Copy Example
strcpy: // i is in x19(s3) addi sp,sp,-8
sd x19,0(sp) add x19,x0,x0 L1: add x5,x19,a1 lbu x6,0(x5) add x7,x19,a0
sb x6,0(x7) beq x6,x0,L2 addi x19,x19, 1 jal x0,L1 L2: ld x19,0(sp) addi sp,sp,8 jalr x0,0(x1)
void strcpy (char x[], char y[]) { size_t i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
For leaf procedure, we can allocate automatic variable (such as i in strcpy) to temporary register and avoid saving and restoring.
strcpy: // i is in t4 addi sp,sp,-8 sd x19,0(sp) add t4,x0,x0 L1: add x5, t4,a1 lbu x6,0(x5) add x7, t4,a0 sb x6,0(x7) beq x6,x0,L2 addi t4, t4, 1 jal x0,L1 L2: ld x19,0(sp) addi sp,sp,8 jalr x0,0(x1)
优化后省掉4条指令

## Slide 78: 2.10 RISC-V Addressing for Wide Immediates and Addresses
Most constants are small:12-bit immediate is sufficient
For the occasional 32-bit constant
lui rd, constant //U-Type instruction
  Copies 20-bit constant(补码带符号数) to bits [31:12] of rd
  Extends bit 31 to bits [63:32]
  Clears bits [11:0] of rd to 0
0000 0000 0011 1101 0000
0000 0000 0000 0000
lui x19, 976 // 0x003D0
§2.10 RISC-V Addressing for Wide Immediates and Addresses
addi x19,x19,1280 // 0x500
0000 0000 0000 0000
0000 0000 0000
0000 0000 0011 1101 0000
0000 0000 0000 0000
0000 0000 0000 0000
0101 0000 0000
Above two instructions make a 32-bit constant in x19.
2.10.1 Wide Immediate Operands

## Slide 79
lui rd, constant //U-Type instruction
  Copies 20-bit constant(补码带符号数) to bits [31:12] of rd
  Extends bit 31 to bits [63:32]
  Clears bits [11:0] of rd to 0
1001 0000 0011 1101 0000
1111 1111 1111 1111
lui x19, 0x903d0 // 0x903D0
§2.10 RISC-V Addressing for Wide Immediates and Addresses
addi x19,x19,1280 // 0x500
1111 1111 1111 1111
0000 0000 0000
1001 0000 0011 1101 0000
0101 0000 0000
Above two instructions make a 32-bit constant in x19.
1111 1111 1111 1111
1111 1111 1111 1111

## Slide 80: 2.10.2 Addressing in Branches
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
SB format:
PC-relative addressing
Target address = PC + immediate × 2，这里immediate是12位补码表示的带符号数
rs2
rs1
funct3
opcode
imm [10:5]
imm [4:1]
imm[12]
imm[11]
2.7节已讲过，不讲

## Slide 81: Jump Addressing
Jump and link (jal) target uses 20-bit immediate for larger range: PC=PC+imm*2, 这里imm是20位补码表示的带符号数，依据是第5板书P116下面这段划红线的文字
UJ format:
=============== 以下是新内容 =================
For long jumps, eg, to 32-bit absolute address 0xabcd1234
  lui: load address[31:12] to temp register, lui t0, 0xabcd1
  jalr: add address[11:0] and jump to target, jalr x0,0x234(t0)
rd
opcode
7 bits
5 bits
imm[11]
imm[20]
imm[10:1]
imm[19:12]
本页上部在2.8节已讲过，不讲

## Slide 82: 2.10.3 RISC-V Addressing Mode Summary
e.g. addi x23,x28,-240
slli x10, x22, 63
ld x26, -48(x25) 不是立即数寻址
e.g. add x23,x28, x29
e.g. ld x26, -48(x25)
sd x26, -48(x25)
e.g. beq x20,x23, exit1
jal x1, fact

## Slide 83
S-type: 4 instructions，sd, sw, sh, sb
  example：sd x28, -36(x24)
SB-type : 6 instructions， BEQ，BNE，BLT，BLTU，BGE，BGEU，
  example： bne x22, x23, exit
UJ-type: Unconditional Jump-and-link, 1 instructions，jal
  example： jal x1,fact // = [ jal ra,fact ], call a procedure or function, similar to x86 [call fact]
  example: jal x0, labal1 // Unconditionally Jump to label1, similar to x86 [jump label1], similar to MIPS [ j label1],
U-type: 2 instructions，lui, auipc. example： lui x19, 0x9a3d0
本页课件每种类型的指令数量根据书末倒数第2页（P1048/总1049）的内容得出

## Slide 84
3 I-type instructions in RV64I and RV32I (slli, srli, srai) have 6-bit funct7 and 6-bit rs2, are different from most I-type instructions listed above.

## Slide 85
书末倒数第2页（PDF文件的P1048/总1049）的内容：

## Slide 86
FIGURE 2.18 RISC-V instruction encoding.

## Slide 88: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions
§2.11 Parallelism and Instructions: Synchronization
不考或简单考

## Slide 89: Synchronization in RISC-V
Load reserved: lr.d rd,(rs1)
  Load from address in rs1 to rd
  Place reservation on memory address
Store conditional: sc.d rd,(rs1),rs2
  Store from rs2 to address in rs1
  Succeeds if location not changed since the lr.d
    Returns 0 in rd
  Fails if location is changed
    Returns non-zero value in rd
不考或简单考

## Slide 90: Synchronization in RISC-V
Example 1: atomic swap (to test/set lock variable)
  again: lr.d x10,(x20)
  sc.d x11,(x20),x23 // X11 = status
  bne x11,x0,again // branch if store failed
  addi x23,x10,0 // X23 = loaded value
Example 2: lock
  addi x12,x0,1 // copy locked value
  again: lr.d x10,(x20) // read lock
  bne x10,x0,again // check if it is 0 yet
  sc.d x11,(x20),x12 // attempt to store
  bne x11,x0,again // branch if fails
  Unlock:
  sd x0,0(x20) // free lock
不考或简单考

## Slide 91: 2.12 Translating and Starting a Program
Many compilers produce object modules directly
Static linking
§2.12 Translating and Starting a Program

## Slide 92: RISC-V programming: 下面的汇编语言源程序格式参考RISC-V汇编源程序格式书写（ RISC-V-Reader-Chinese-v2p1.pdf P41有介绍），不一定完全符合格式
92
.data
Y: .dword 0x33334444CCCCDDDD
……
.text
A: ld x10, X // procedure A
jal x1, B // call B
add x8, x9,x10
……
.data
X：.dword 0x11112222AAAABBBB
……
.text
B: sd x11, Y // procedure B
jal X1, A // call A
sub x6,x7,x8
……
File A.asm File B.asm

## Slide 93: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Header: describes the size of text and data, position of the other pieces of the object file.
Text segment: translated instructions
Static data segment: data allocated for the life of the program
Relocation info: identifies instructions and data words that depend on absolute addresses when the program is loaded into memory.
Symbol table: contains the remaining labels that are not defined, such as external references.
Debug info: for associating with source code

## Slide 94
94
.data
Y：.dword 0x33334444CCCCDDDD
……
.text
A: ld x10, X // procedure A
jal x1, B // call B
add x8, x9,x10
……
File A.asm
在windows系统中，A.OBJ 和 B.OBJ可连接成为my.exe文件
应是Y？

## Slide 95
.data
X：.dword 0x11112222AAAABBBB
……
.text
B: sd x11, Y // procedure B
jal A // call A
sub x6,x7,x8
……
File B.asm
应是X？

## Slide 96: Linking Object Modules
Produces an executable image
  1. Merges segments
  2. Determine the addresses of data labels and instruction labels
  3. Patch both the internal and external references
2.12.3 Linker

## Slide 97
-0x104 = -260
0x0fc = 252
X3 is gp

## Slide 98
assuming x3 (gp) is initialized to 1000 0000hex.
gp

## Slide 99: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space large enough for the text and data
  3. Copy text and initialized data into memory
  4. Set up arguments on stack
  5. Initialize registers (including sp, fp, gp)
  6. Jump to startup routine
    Copies arguments to x10, … and calls main()
    When main returns, syscall “exit” is executed.
2.12.4 Loader

## Slide 100: Dynamic Linking
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all referenced libraries
  Automatically picks up new library versions
2.12.5 Dynamically Linked Libraries

## Slide 101: 2.12.6 Starting a Java Program
Simple portable instruction set for the JVM
Interprets bytecodes
Compiles bytecodes of “hot” methods into native code for host machine
Java program VS Compiled C program
  the factor of 10 slowdown(慢10倍)
Java Virtual Machine 是一种解释执行程序，类似于basic程序的解释执行

## Slide 102: 2.13 A C Sort Example to Put it All Together
Illustrates use of assembly instructions for a C bubble sort function
Swap procedure (leaf)
  void swap(long long int v[], long long int k) { long long int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in x10, k in x11, temp in x5
§2.13 A C Sort Example to Put It All Together

## Slide 103: 2.13.1 The Procedure Swap
swap:
slli x6,x11,3 // reg x6 = k * 8
add x6,x10,x6 // reg x6 = v + (k * 8)
ld x5,0(x6) // reg x5 (temp) = v[k]
ld x7,8(x6) // reg x7 = v[k + 1]
sd x7,0(x6) // v[k] = reg x7
sd x5,8(x6) // v[k+1] = reg x5 (temp)
jalr x0,0(x1) // return to calling routine
  void swap(long long int v[], long long int k) { long long int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in x10, k in x11, temp in x5

## Slide 104: The Procedure Swap
swap:
slli t1, a1,3 // reg t1 = k * 8
add t1,a0,t1 // reg t1 = v+(k*8)= addr of v[k]
ld t0,0(t1) // reg t0 (temp) = v[k]
ld t2,8(t1) // reg t2 = v[k + 1]
sd t2,0(t1) // v[k] = reg t2
sd t0,8(t1) // v[k+1] = reg t0 (temp)
jr ra //ret // return to calling routine
  void swap(long long int v[], long long int k) { long long int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in a0, k in a1, temp in t0

## Slide 105: 2.13.2 The Procedure sort
Non-leaf (calls swap)
  void sort (long long int v[], size_t n)
  {
  size_t i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1;
  j >= 0 && v[j] > v[j + 1];
  j -= 1) {
  swap(v,j);
  }
  }
  }
  v in x10/a0, n in x11/a1, i in x19/s3, j in x20/s4

## Slide 106
Procedure sort
  C code
  sort ( int v[ ] , int n )
  {
  int i , j ;
  for ( i = 0 ; i < n ; i + = 1 ) {
  for ( j = i - 1 ; j >= 0 && v[j] > v[j+1] ; j- = 1 )
  swap ( v , j ) ;
  }
  }
  i=0: inner loop do nothing
  i=1: j=0, V[0]、V[1]小的上移
  i=2: j=1开始, V[1]、V[2]小的上移， V[0]、V[1]小的上移
  i=3: j=2开始, V[2]、V[3]小的上移， V[1]、V[2]小的上移， V[0]、V[1]小的上移
  ……
  i=9: j=8开始, V[8]、V[9]小的上移， V[7]、V[8]小的上移…… V[0]、V[1]小的上移
V[0]
V[1]
V[2]
……
V[n-1]
If V[0]> V[1]
V[0]
V[1]
V[2]
V[3]
V[4]
V[5]
V[6]
V[7]
V[8]
V[9]

## Slide 107
Procedure sort
  C code
  void sort (long long v[ ] , size_t n )
  {
  size_t i , j ;
  for ( i = 0 ; i < n ; i + = 1 ) {
  for ( j = i - 1 ; j >= 0 && v[j] > v[j+1] ; j -= 1 )
  swap ( v , j ) ;
  }
  }
  Register allocation for sort
  v -- x10/a0 --> x21/s5 n -- x11/a1 --> x22/s6
  i ---- x19/s3 j ---- x20/s4
  Passing parameters in sort
  Preserving registers in sort
  x1 , x19, x20, x21, x22
V[0]
V[1]
V[2]
……
V[n-1]
If V[0]> V[1]

## Slide 108
  Code for the procedure sort
    Saving registers
  sort: addi sp, sp, -40 // make room on stack for 5 registers
  sd x1, 32(sp) // save return address on stack
  sd x22, 24(sp) // save x22 on stack
  sd x21, 16(sp) // save x21 on stack
  sd x20, 8(sp) // save x20 on stack
  sd x19, 0(sp) // save x19 on stack
    Procedure body{Outer loop {Inner loop} }
    Restoring registers
    exit1: ld x19, 0(sp) // restore x19 from stack
    ld x20, 8(sp) // restore x20 from stack
    ld x21, 16(sp) // restore x21 from stack
    ld x22, 24(sp) // restore x22 from stack
    ld x1, 32(sp) // restore return address from stack
    addi sp, sp, 40 // restore stack pointer
    Procedure return
    jalr x0, 0(x1) // return to calling routine

## Slide 109
    Code for Procedure body
      Move parameters
      mv x21, x10 // copy parameter x10/a0 into x21
      mv x22, x11 // copy parameter x11/a1 into x22
      Outer loop—first for loop
    for ( i = 0 ; i < n ; i + = 1 ) {
      li x19, 0 // i = 0
  for1tst: bge x19, x22, exit1 // go to exit1 if i >= n
      ………………
      （body of first for loop is second for loop）
      ………………
  exit2: addi x19, x19, 1 # i = i + 1
  j for1tst # jump to test of outer loop
  exit1:
  v -- x10/a0 --> x21/s5 n -- x11/a1 --> x22/s6
  i ---- x19/s3 j ---- x20/s4

## Slide 110
      Inner loop-- second for loop is body of first for loop
    for ( j = i - 1 ; j >= 0 && v[j] > v[j+1] ; j- = 1 ){
      addi x20, x19, -1 // j = i - 1
for2tst: blt x20, x0, exit2 // go to exit2 if j < 0
    slli x5, x20, 3 // x5 = j * 8
    add x5, x21, x5 // x5 = the address of v[j]
    ld x6, 0(x5) // x6 = v[j]
    ld x7, 8(x5) // x7 = v[j + 1]
    ble x6, x7, exit2 // go to exit2 if v[j] <= v[j+1] // ………………
      （body of second for loop ）
    ………………
    addi x20, x20, -1 // j = j - 1
    j for2tst // jump to test of inner loop
  exit2:
  v -- x10/a0 --> x21/s5 n -- x11/a1 --> x22/s6
  i ---- x19/s3 j ---- x20/s4

## Slide 111
    body of second for loop: swap ( v , j ) ;
      Pass parameters and call
    mv x10，x21 // first swap parameter v
    mv x11，x20 // second swap parameter j
      Call function swap
    jal x1, swap
Notice: 1.Why are x10 and x11 saved? x10 is the base of the array v. x10 will be used repeatedly and might be(actually not here) changed by the procedure swap. x11 is the size of the array v. x11 will be used repeatedly and changed before the procedure swap is called. 2.Why are they not pushed to stack?
  Register variable is faster
  v -- x10/a0 --> x21/s5 n -- x11/a1 --> x22/s6
  i ---- x19/s3 j ---- x20/s4

## Slide 112
  v -- x10/a0 --> x21/s5 n -- x11/a1 --> x22/s6
  i ---- x19/s3 j ---- x20/s4

## Slide 114: Effect of Compiler Optimization
Performance = 1/Execution Time
Compiled with gcc for Pentium 4 under Linux
  O1, O2, O3 are gcc compile options
Procedure inlining（ inlining：代码嵌入）: Instead of passing arguments and invoking the code with a jal instruction, the compiler would copy the code from the swap procedure into caller.
  A method of compile optimization.
2.37=158615/66990 65690=44993*1.46
上图红圈：CPI最小不是性能最好；指令总数最小不是性能最好；

## Slide 115: Effect of Compiler Optimization
Compiled with gcc for Pentium 4 under Linux

## Slide 116
Instruction count and CPI are not good performance indicators in isolation（孤立地）
  Time (similar to Instruction count * CPI ) is the only accurate measure of program performance.
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
网上看到一篇文章说：5w数据量,快速排序的速度是冒泡的900倍

## Slide 117: Effect of Language and Algorithm

## Slide 118: 2.14 Arrays vs. Pointers
Array address calculations involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity
§2.14 Arrays versus Pointers

## Slide 119: Example: Clearing an Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
li x5,0 // i = 0 loop1: slli x6,x5,3 // x6 = i * 8 add x7,x10,x6 // x7 = address // of array[i] sd x0,0(x7) // array[i] = 0 addi x5,x5,1 // i = i + 1 blt x5,x11,loop1 // if (i<size) // go to loop1 | mv x5,x10 // p = address // of array[0] slli x6,x11,3 // x6 = size * 8 add x7,x10,x6 // x7 = address // of array[size] loop2: sd x0,0(x5) // Memory[p] = 0 addi x5,x5,8 // p = p + 8 bltu x5,x7,loop2 // if (p<&array[size]) // go to loop2

## Slide 120: Comparison of Array vs. Ptr
Multiply operation is simplified to shift
Array version requires shift to be inside loop
  Pointer version only increments pointer
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination(循环变量的去除)
  to make program clearer and safer

## Slide 121
必讲课本内容（考试覆盖范围）：
1.1--1.12；
2.1--2.14 （除了2.11）；
3.1--3.5；
4.1--4.9；
5.1--5.9；
+ 原来i/o storage内容。

## Slide 122: MIPS Instructions
MIPS: commercial predecessor to RISC-V
Similar basic set of instructions
  32-bit instructions
  32 general purpose registers, register 0 is always 0
  32 floating-point registers
  Memory accessed only by load/store instructions
    Consistent use of addressing modes for all data sizes
Different conditional branches
  For <, <=, >, >=
  RISC-V: blt, bge, bltu, bgeu
  MIPS: slt, sltu (set less than, result is 0 or 1)
    Then use beq, bne to complete the branch
§2.16 Real Stuff: MIPS Instructions

## Slide 123: Instruction Encoding

## Slide 124: The Intel x86 ISA
Evolution with backward compatibility
  8080 (1974): 8-bit microprocessor
    Accumulator, plus 3 index-register pairs
  8086 (1978): 16-bit extension to 8080
    Complex instruction set (CISC)
  8087 (1980): floating-point coprocessor
    Adds FP instructions and register stack
  80286 (1982): 24-bit addresses, MMU
    Segmented memory mapping and protection
  80386 (1985): 32-bit extension (now IA-32)
    Additional addressing modes and operations
    Paged memory mapping as well as segments
§2.17 Real Stuff: x86 Instructions

## Slide 125: The Intel x86 ISA
Further evolution…
  i486 (1989): pipelined, on-chip caches and FPU
    Compatible competitors: AMD, Cyrix, …
  Pentium (1993): superscalar, 64-bit datapath
    Later versions added MMX (Multi-Media eXtension) instructions
    The infamous FDIV bug
  Pentium Pro (1995), Pentium II (1997)
    New microarchitecture (see Colwell, The Pentium Chronicles)
  Pentium III (1999)
    Added SSE (Streaming SIMD Extensions) and associated registers
  Pentium 4 (2001)
    New microarchitecture
    Added SSE2 instructions

## Slide 126: The Intel x86 ISA
And further…
  AMD64 (2003): extended architecture to 64 bits
  EM64T – Extended Memory 64 Technology (2004)
    AMD64 adopted by Intel (with refinements)
    Added SSE3 instructions
  Intel Core (2006)
    Added SSE4 instructions, virtual machine support
  AMD64 (announced 2007): SSE5 instructions
    Intel declined to follow, instead…
  Advanced Vector Extension (announced 2008)
    Longer SSE registers, more instructions
If Intel didn’t extend with compatibility, its competitors would!
  Technical elegance ≠ market success

## Slide 127: Basic x86 Registers

## Slide 128: Basic x86 Addressing Modes
Two operands per instruction
Source/dest operand | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate
Memory addressing modes
  Address in register
  Address = Rbase + displacement
  Address = Rbase + 2scale × Rindex (scale = 0, 1, 2, or 3)
  Address = Rbase + 2scale × Rindex + displacement

## Slide 129: x86 Instruction Encoding
Variable length encoding
  Postfix bytes specify addressing mode
  Prefix bytes modify operation
    Operand length, repetition, locking, …

## Slide 130: Implementing IA-32
Complex instruction set makes implementation difficult
  Hardware translates instructions to simpler microoperations
    Simple instructions: 1–1
    Complex instructions: 1–many
  Microengine similar to RISC
  Market share makes this economically viable
Comparable performance to RISC
  Compilers avoid complex instructions

## Slide 131: Other RISC-V Instructions
Base integer instructions (RV64I)
  Those previously described, plus
  auipc rd, immed // rd = (imm<<12) + pc
    follow by jalr (adds 12-bit immed) for long jump
  slt, sltu, slti, sltui: set if less than (like MIPS)
  addw, subw, addiw: 32-bit add/sub
  sllw, srlw, srlw, slliw, srliw, sraiw: 32-bit shift
32-bit variant: RV32I
  registers are 32-bits wide, 32-bit operations
§2.18 The Rest of the RISC-V Instruction Set

## Slide 132: Instruction Set Extensions
M: integer multiply, divide, remainder
A: atomic memory operations
F: single-precision floating point
D: double-precision floating point
C: compressed instructions
  16-bit encoding for frequently used instructions

## Slide 133: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less productivity
§2.19 Fallacies and Pitfalls

## Slide 134: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accrete more instructions
x86 instruction set

## Slide 135: Pitfalls
Sequential words are not at sequential addresses
  Increment by 4, not by 1!
Keeping a pointer to an automatic variable after procedure returns
  e.g., passing pointer back via an argument
  Pointer becomes invalid when stack popped

## Slide 136: Concluding Remarks
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Good design demands good compromises
Make the common case fast
Layers of software/hardware
  Compiler, assembler, hardware
RISC-V: typical of RISC ISAs
  c.f. x86
§2.20 Concluding Remarks