## Slide 1: Chapter 5 Large and Fast: Exploiting Memory Hierarchy

## Slide 2: 5.1 Introduction
SRAM:
  value is stored on a pair of inverting gates
  very fast but takes up more space than DRAM
  (4 to 6 transistors)
附录也无此内容

## Slide 3: Memories: Review
Word Line
Bit Line
C
Sense Amp
. . .
DRAM:
  value is stored as a charge on capacitor (must be refreshed)
  very small but slower than SRAM (factor（倍数） of 5 to 10)
Write
  set wordline HIGH and Charge bitline HIGH or LOW
Read
  Bit line is precharged to a voltage halfway between HIGH and LOW, and then the word line is set HIGH(晶体管基集为高时，
  集电极与发射极导通).
  Depending on the charge in the capacitor, the precharged bitline is pulled slightly higher or lower.
  Sense Amplifier Detects change
  RISCV教材附录 第A-63页有介绍

## Slide 4: DRAM logical organization (256 Mbit) 1位数据读出
Column mutiplexer
Sense
Amps & I/O
Memory
Array
(16,384×16,384)
A0…A1
3
14
Data in
D
Q
Word Line
Storage
Cell
Data out
Row Decoder
…
Bit Line
14
14bit col. Addr. Reg.
14bit row addr Reg
16384 bit col. data Reg.
CAS（列选通）
RAS（行选通）
RAS: Row Access Strobe, CAS: Column Access Strobe

## Slide 5: DRAM logical organization (256 Mbit) 1位数据写入
上图未画出：有一个列解码器（14输入），列解码器有16384根输出线，每个输出线用于16384个三态门的控制线，这16384个三态门的输入连在一起，作为bit line的1位输入数据，这16384个三态门的输出作为memory array的列输入（其中1根为高或低，其余为高阻态）。
Column decoder
16384个3态门
Memory
Array
(16,384×16,384)
A0…A1
3
14
Data in
D
Q
Word Line
Storage
Cell
Data out
Row Decoder
…
Bit Line
14
14bit col. Addr. Reg.
14bit row addr Reg
16384 根3态门的控制线
CAS（列选通）
RAS（行选通）
control
input
output

## Slide 6: Locality---- two important concepts
1. temporal locality (locality in time):
  If an item is referenced, it will tend to be referenced again soon.
2. spatial locality (locality in space):
  If an item is referenced, items whose addresses are close by will tend to be referenced soon.
As we know, these principles actually exists in most programs.
  Why does code have locality?
Our initial focus: two levels (upper, lower)
  block: minimum unit of data (block) for transfers

## Slide 7: Solutions
Build a memory hierarchy
M
e
m
o
r
y
C
P
U
M
e
m
o
r
y
S
i
z
e
C
o
s
t
(
$
/
b
i
t
)
S
p
e
e
d
S
m
a
l
l
e
s
t
B
i
g
g
e
s
t
H
i
g
h
e
s
t
L
o
w
e
s
t
F
a
s
t
e
s
t
S
l
o
w
e
s
t
M
e
m
o
r
y
processor
Data are transferred
upper
Block (aka line, 见RISCV书P368): unit of copying between memory and cache
  May be multiple words

## Slide 8: Some important concepts
Hit: The CPU accesses the upper level，data requested is in the upper level，succeeds.
Miss: The CPU accesses the upper level， data requested is not in the upper level，fails.
Hit time:
  The time to access the upper level of the memory hierarchy, which includes the time needed to determine whether the access is a hit or a miss.
miss penalty:
  The time to replace a block in the upper level with the corresponding block from the lower level
  发生缺失时，访问1次内存的时间=hit_time + miss_penalty

## Slide 9: Exploiting Memory Hierarchy
  Hierarchies bases on memories of different speeds and size
  more close to CPU the level is, faster the one is.
  more close to CPU the level is, smaller the one is.
  more close to CPU the level is, more expensive
Levels in the memory hierarchy
Increasing distance from the CPU
Size of the memory at each level
size

## Slide 10
Disk is normally the bottom of the hierarchy
Some systems use tape or file server in LAN as the next level below disk.
Design goal:
  the processor has an access time of level 1 of the hierarchy
  the processor has a memory as large as level n.
Exploited Memory Hierarchy
  Cache: SRAM and DRAM (main memory)
    The solution focuses on speed
  Virtual Memory: DRAM and DISK
    The solution focuses on size

## Slide 11: 5.2 Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
1 second=10^3 millisecond=10^6 us(micro second)
=10^9 ns(nanosecond)
Ideal memory Hierarchy
  Access time of SRAM
  Capacity and cost/GB of disk
§5.2 Memory Technologies

## Slide 12: DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge, The charge can be kept for several milliseconds.
  Must periodically be refreshed
    This consumes 1% to 2% of the active cycles of the DRAM
    Performed on a DRAM “row”: refreshing an entire row (which shares a word line) with a read cycle followed immediately by a write cycle.

## Slide 13
刷新与行地址有关。刷新时一行行进行的，必须在刷新周期内，由专用的刷新电路来完成对基本单元电路的逐行刷新，才能保证DRAM内的信息不丢失。通常有三种方式刷新：集中刷新、分散刷新和异步刷新。
DRAM 制造商的一些资料中显示，内存至少要每64ms刷新一次，这也就意味着内存有1％的时间要用来刷新。
内存的刷新关键 在于当对内存单元进行读取操作时保持内存的内容不变，所以DRAM单元每次读取操作之后都要进行刷新：执行一次回写操作，因为读取操作也会破坏内存中的电 荷，也就是说对于内存中存储的数据是具有破坏性的。

## Slide 14
下图1条DRAM内存条有8片chip（市场上也有9片或4片的）。
例子：1个chip内有4个bank，每个bank内有8个array（8个array决定了位宽是8bit），一个特定地址的数据只在其中1个bank中，1个bank的容量是64K*8bit（256 row * 256 column * 8bit），则这个chip有256k*8bit，位宽8bit。
  Chip的位宽由array数量决定，无关bank数量，增加chip内的bank数只会增加容量，不增加位宽。
  输入地址时，地址译码电路会选择其中的一个bank
  读数据的bank内地址是0xA1B4，clk1输入row-addr=0xA1,每个array读出1个row的256位存到row buffer（256 bits latches），8个array同时读出同1个row的256*8位存到row buffer， 接着clk2输入col-addr=0xB4, 会读出row buffer 内column-addr是0xB4处的8bit（对应bank内地址0xA1B4 ），row-addr不变 ，clk3和clk4输入col-addr=0xB5,0xB6, 依次读出0xA1B5处的8bit， 0xA1B6处的8bit。
  When the row is in the buffer, it can be transferred by successive column addresses at whatever the width of the DRAM is (typically 4, 8, or 16 bits in DDR3).  在上例中，When the row is in the buffer, it can be transferred by successive column addresses at 8bit.
ftp: \课-计算机组成\电子书及补充读物\DRAM \DRAM的结构原理剖析-CSDN博客-210525.docx 很有用

## Slide 15
Modern DRAMs are organized in banks, typically four for DDR3.
Sending a PRE (precharge) command opens or closes a bank.
  Memory addr: [bank-addr ] [row-addr] [column-addr],
    E.g. : 24-bit address [2-bit] [11-bit] [11-bit]
  Each bank consists of a series of rows. 这里的row不同于上个PPT页的array。
A row address is sent with an Act (activate), which causes the row to transfer to a buffer.
When the row is in the buffer, it can be transferred by successive column addresses at whatever the width of the DRAM is (typically 4, 8, or 16 bits in DDR3) or by specifying a block transfer and the starting address.
FIGURE 5.4 Internal organization of a DRAM.
Internal organization of a DRAM

## Slide 16: Advanced DRAM Organization
Bits in a DRAM are organized as a rectangular array
  DRAM accesses an entire row
  Burst mode: supply successive words from a row with reduced latency
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
  Example of Burst mode

## Slide 17: DRAM Generations
Year | Capacity | $/GB
1980 | 64Kbit | $1500000
1983 | 256Kbit | $500000
1985 | 1Mbit | $200000
1989 | 4Mbit | $50000
1992 | 16Mbit | $15000
1996 | 64Mbit | $10000
1998 | 128Mbit | $4000
2000 | 256Mbit | $1000
2004 | 512Mbit | $250
2007 | 1Gbit | $50

## Slide 18: DRAM Performance Factors
Row buffer
  Allows several words to be read and refreshed in parallel
Synchronous DRAM (SDRAM)
  DRAMs added clocks
  Allows for consecutive accesses in bursts without needing to send each address
  Improves bandwidth
DRAM banking（不讲）
  Allows simultaneous access to multiple DRAMs
  Improves bandwidth

## Slide 19: Increasing Memory Bandwidth
4-word wide memory
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  Bandwidth = 16 bytes / 17 cycles = 0.94 B/cycle
4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 B/cycle
书上无，不讲

## Slide 20: Flash Storage
Nonvolatile semiconductor storage
  100× – 1000× faster than disk
  Smaller, lower power, more robust
  But more $/GB (between disk and DRAM)

## Slide 21: Flash Types
NOR flash: bit cell like a NOR gate
NAND flash: bit cell like a NAND gate
Flash bits wears out after 1000’s of writes
  Wear levelling(磨损均衡化): remap data to less used blocks

## Slide 22: Disk Storage
Nonvolatile, rotating magnetic storage

## Slide 23: Disk Sectors and Access
Each sector records
  Sector ID
  Data (512/1024/2048/4096 bytes, 4096 bytes proposed)
  Error correcting code (ECC) or Error checking code
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads
  Rotational latency
  Data transfer
  Controller overhead

## Slide 24: Disk Access Example
Given
  512B sector, 15,000 rpm(round per minute), 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk(no queuing delay )
Average read time
  4ms seek time
  + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms
书上无，不讲

## Slide 25: Disk Performance Issues
Manufacturers quote （报告） average seek time
  Based on all possible seeks
  Locality and OS scheduling lead to smaller actual average seek times
Disk drives include caches
  Prefetch sectors in anticipation of access
  Avoid seek and rotational delay

## Slide 26: 5.3 Cache Memory
Cache
  Also known as “Cache Memory”, initially all entries are empty.
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches
Figure 5.7 The cache: word Xn is not initially in the cache.
Two issues:
  How do we know if a data item is in the cache?
  If it is, how do we find it?
P80有三种cache的介绍

## Slide 27: Direct Mapped Cache
Where can a block be placed in the upper level (cache)?
Algorithm: Index is the cache block address, it is
  (memory block address) modulo (the number of blocks in the cache)
The cache has 2n blocks, index is equal to the lowest n bits of memory block address. Here n=3.
8 Block of cache
5 bit memory block address
index

## Slide 28: The basics of Cache
For each item of data at the memory, there is exactly one location in the cache where it might be.
  e.g., lots of items at the lower level(memory) share locations in the upper level(cache)

## Slide 29: 5.3.1 Accessing a Cache
How do we know which particular memory block is stored in a cache location?
  Store memory block address as well as the data
  Actually, only need the high-order bits (tag)
    memory block address = { tag, index}
    e.g. memory block address =10011,tag=10,index=011
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
a. The initial state of the cache after power-on |  |  | 
What if there is no data in a location?
  V (Valid bit): 1 = present, 0 = not present
  Initially all of V are 0
Tags and Valid Bits

## Slide 30: Accessing a cache---how do we find it?
32-bit or 64-bit memory address
Index=(memory block address) modulo (the number of blocks in the cache)
e.g. 011 = 10011 % 1000 （binary） , or 3=19 % 8
Byte offset
Index
TAG
Block address MOD Numbers of Cache Block
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
a. The initial state of the cache after power-on |  |  | 
V:valid bit
FIGURE 5.9

## Slide 31: Access sequence: figure b,c,d,e, f,g,h,i
Access sequence of Mem Block address (red address indicates hit)：
10110,11010,10110,11010, 10000,00011,10000,10010
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
b. After handling a miss of address(10110) |  |  | 
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
c. After handling a miss of address(11010) |  |  | 
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
d. After handling a hit of address(10110) |  |  | 
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
e. After handling a hit of address(11010) |  |  | 
FIGURE 5.9

## Slide 32: Access sequence
10110,11010,10110,11010, 10000,00011,10000,10010
Index | V | Tag | Data
000 | Y | (10)2 | Memory(10000)
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
f. After handling a miss of address(10000) |  |  | 
Index | V | Tag | Data
000 | Y | (10)2 | Memory(10000)
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | Y | (00)2 | Memory(00011)
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
g. After handling a miss of address(00011) |  |  | 
Index | V | Tag | Data
000 | Y | (10)2 | Memory(10000)
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | Y | (00)2 | Memory(00011)
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
h. After handling a hit of address(10000) |  |  | 
Index | V | Tag | Data
000 | Y | (10)2 | Memory(10000)
001 | N |  | 
010 | Y | (11)→ (10)2 | Memory(10010)
011 | Y | (00)2 | Memory(00011)
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
i. After handling a miss of address(10010) |  |  | 
FIGURE 5.9

## Slide 33: Direct Mapped Cache construction
1 block includes only 1 word (4 byte) here
What kind of locality are we taking advantage of?
temporal
2
Answer for two issues:
  How do we know if a data item is in the cache?
  If it is, how do we find it?
32-bit memory address

## Slide 34: Direct Mapped Cache construction
1 block includes only 1 word (4 byte)
64-bit memory address
Answer for two issues:
  How do we know if a data item is in the cache?
  If it is, how do we find it?

## Slide 35: How many total number of bits needed for a cache in direct-mapped cache?
64-bit address, n bits index, The block size is 2m words (2m+2 bytes)
The cache size is 2n blocks
The data size in a block: 2m words, 2m+2 bytes, 2m+5 bits
  Address structure: m bits are used for the word within the block, and 2 bits are used for the byte part of the address
The size of the tag field is 64 − (n + m + 2).
The total bits in a direct-mapped cache is
  2n ×(block size + tag size + valid field size)
  = 2n ×[2m+5 + 64 − (n + m + 2) + 1] = 2n ×[2m+5 + 63 − n − m)]
64-bits address:

## Slide 36: How many total number of bits needed for a cache in direct-mapped cache?
32-bit address, n bits index, The block size is 2m words (2m+2 bytes)
The cache size is 2n blocks
The data size in a block: 2m words, 2m+2 bytes, 2m+5 bits
  m bits are used for the word within the block, and two bits are used for the byte part of the address
The size of the tag field is 32 − (n + m + 2).
The total bits in a direct-mapped cache is
  2n ×(block size + tag size + valid field size)
  = 2n ×[2m+5 + 32 − (n + m + 2) + 1] = 2n ×[2m+5 + 31 − n − m)]
32-bits address:
32位版本，不讲

## Slide 37: Bits in Cache
Example
How many total bits are required for a direct-mapped cache (16KB of data and 4-word blocks)? assuming a 64-bit address.
Answer
One block=4 words = 16 bytes
Number of blocks = 16K ÷ 16 = 210 blocks, index bits n=10
The data size in a block: 22 words, m=2
The size of the tag field: 64 − (n + m + 2) = 50 bits
Data bits of 1 block =4×32=128 bits
The total bits in cache is
  2n ×(block size + tag size + valid field size)
  = 1024×[128 + 50+ 1] = 179 Kbits
  The total bytes =179/8 KiB = 22.4 KiB =1.4*16 KiB
  It is about 1.4 times of the data

## Slide 38: Bits in Cache
Example
How many total bits are required for a direct-mapped cache (16KB of data and 4-word blocks)? assuming a 64-bit address.
Answer
One block=4 words = 16 bytes
Number of blocks = 16K ÷ 16 = 210 blocks, index bits n=10
The data size in a block: 22 words, m=2
The size of the tag field: 64 − (n + m + 2) = 50 bits
Data bits of 1 block =4×32=128 bits
The total bits in cache is
  Total data size + 2n ×(tag size + valid field size)
  = 16K*8 + 1024×[50+ 1] = 128K+51K = 179 Kbits
本PPT页的方法与上页有区别（但篮框内基本相同），是更好的方法

## Slide 39: Mapping an Address to Multiword Cache Block
Example
Consider a cache with 64 blocks and a block size of 16 bytes.
What cache block number does byte address 1200 map to?
Answer： Cache block number =
(memory Block address) modulo (Number of cache blocks)
Where the memory Block address is
So cache block number =75 modulo 64 =11,
cache block number is also known as cache block address .
The start and end byte address of the block where address 1200 is located in:
Byte address
Bytes per block
1200
16
=
= 75
Byte address
Bytes per block
×Byte per block -----
Byte address
Bytes per block
×Byte per block
+( Byte per block-1)
1200 ----- 1215
Here:
Tag
Index
Offset
0
3
4
9
10
63
4 bits
6 bits
54 bits

## Slide 40: Block Size Considerations
Larger blocks with many bytes should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger block size  fewer block number
    More competition（很多内存块争着要进入cache）  a block will be moved out from cache before many of its words are accessed
Larger blocks, larger miss penalty
  Fetch more bytes from Memory when miss occurs.
  Can override(消除) benefit of reduced miss rate
  Early restart and critical-word-first can help
    early restart: resume execution as soon as the requested word of the block （e.g. the 2# word in 8-word block） is returned, no wait for entire block (i.e. no wait for 3#--8# words) to be loaded.
    critical-word-first: Organize the memory, the requested word is transferred first. The remainder is then transferred, starting from the next word after the requested one and wrapping around to the beginning of the block.

## Slide 41: Larger blocks exploit spatial locality
Taking advantage of spatial locality to lower miss rates with many word in the block:
direct-mapped cache
FIGURE A-1

## Slide 42
Figure 5.11 Miss rate versus block size. 4 caches: 4K, 16K, 64K, 256K bytes
The miss rate goes up if block size is too large relative to the cache size.
Each line represents a cache of different size： 4K, 16K, 64K, 256K bytes.
following figure data are based on SPEC92. SPEC92是在SPEC89的10个基准程序基础上再增加了4个测试整数运算性能的程序和8个测试浮点数性能的程序,分别称之为SPECint92(共8个程序)和SPECfP92(共14个程序)

## Slide 43: 5.3.2 Handling Cache Misses
  Read hits: this is what we want !
  Read misses, two kinds of misses:
    instruction cache miss
    data cache miss
  a cache miss creates a instruction pipeline stall
  we stall the entire processor, essentially freezing the contents of the temporary and programmer-visible registers
    meanwhile we wait for memory.
  in contrast to an exception or interrupt: saving the state of all registers.
  assume in-order processors ( not out-of-order processors) stalls on cache misses in this section.
Handling Cache reads hit and read Miss

## Slide 44
Steps of instruction cache read miss operation
  for instruction cache miss, we stall the CPU, fetch block from memory, deliver to cache, restart CPU read.
    Step-1 Send the original PC value [(current PC)-4] to the memory address.
      Reason of (current PC)-4 : at the end of 1# cycle (IF stage) in pipeline, PC <-- PC+4, after the begin of 2# cycle (ID stage), we fetch memory block, but [current PC] is ([original PC]+4)
    Step-2 Instruct main memory to read a block and wait, this takes multiple clock cycles ( e,g, 100 cycles).
    Step-3 Write the cache entry: put the data from memory into the data portion of the entry, write the upper bits of the address (from the ALU) into the tag field, and set valid bit to 1.
    Step-4. Restart the instruction execution at the first step, which will refetch the instruction again, this time finding it in the cache.
Above approach can be extended to handle data misses
  But some differences exists.

## Slide 45: 5.3.3 Handling Writes
  2 kinds of caches
  write-through cache: when cache writes hit, cache system write the data into cache and memory
    The latest data is in memory. But makes writes take longer
      e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles，no write buffer
      Effective CPI =( N+N*10%*100)/N = 1 + 0.1×100 = 11
  write-back cache: when cache writes hit, cache system only writes data into cache, don't write into memory.
    The latest data is in cache
    Memory data may be obsolete, when a cache block is removed from cache, it should be written back to memory.

## Slide 46
Write stall ---When the CPU must wait for writes to complete during write through
Write buffers
  A small cache that can hold a few values waiting to go to main memory.
    补充：each buffer entry contains data and its memory address.
  To avoid stalling on writes, many CPUs use a write buffer.
    A write buffer includes one or several entries
    Each entry contains data (1 byte or 1 word or 1 double-word) and its memory address(依据：书P434 Figure 5.32)
    After putting data into write buffer, CPU continues subsequent cycle or instruction immediately
      Only stalls on write if write buffer is already full
  This buffer helps when writes are clustered.
  It does not entirely eliminate stalls since it is possible for the buffer to be full if the write burst is larger than the buffer.

## Slide 47: Write buffers
write
buffer
CPU
in out
DRAM
(or lower mem)
Write Buffer

## Slide 48
Write hits: Difference Strategy for write-back and write-through cache
  Write-back cache (Causing Inconsistent)
    Write the data into only the data cache, Fast
    Write back cache block to memory when the block is replaced.
    A write-back scheme is more complex to implement than write-through.
    write-back Improves performance, especially when processors can generate writes as fast as (or faster than) the writes can be handled by main memory;
  Write-through cache ( Ensuring Consistent)
    Write operation always update the memory
    It is slower because of writing memory, solution: using write buffer

## Slide 49
Options of write misses in write-through caches
  Write allocate（写分配）
    Allocate a cache block（在direct mapped cache中，不需要分配，可选的cache entry是唯一的，但在其它2种cache中，有多个cache entry可选，需要分配一个） , load memory data into cache, then write data in cache
  No write allocate (aka Write around)
    The data is only written to main memory, not written into the cache. Don’t fetch a memory block to cache.
    Reason： programs often write a whole block before reading it (e.g., initialization). 这时把一个block从内存搬到cache是白费力气，因为block内的所有字都是只写不读（至少在初始化后的一段较长时间内不读取）。
None of Write-allocate and No-write-allocate exist in write-back caches
aka: also known as
本页内容在英文教材PDF文件的P386 “Elaboration”

## Slide 50
3 steps for Write misses :
  Only for write-back cache: if the cache block is dirty, write it back to memory. Write-through cache无本步骤.
    dirty: cache block has been modified after load from memory
  First read the entire block into cache from memory
    the word (or double words) that SW/SD instruction writes need not be moved into cache because it will be updated immediately.
  Then write a word (for SW instr.) or double word (for SD instr.) into:
    Only cache (for write-back cache)
    Only memory (for write-through cache with no write allocate )
    both cache and memory (for write-through cache with write allocate ).
aka: also known as

## Slide 51: Write-through scheme VS write-back scheme
When data is written into the cache (executing a SW(Store Word) or SD instruction), is the data also written to main memory?
  write-through cache
    yes
    Can always discard cached data, the latest data is in memory
    Cache control bit: only a valid bit
    memory always have latest data
    advantage: Read misses don't result in writing memory, memory hierarchy is consistent and it is simple to implement.
  write-back cache
    no
    Can’t just discard cached data, we have to write it back to memory
    Cache control bits: valid and dirty bits
    Less access to memory, since data often overwritten multiple times
    advantage : Writings occur at speed of cache, writing main memory happens less frequently when multiple writing occur to the same block.

## Slide 52: Cache总结（SW指令）
以cache写hit时采用write back(方案A)和write through（方案B）为中心，分别有2种cache系统：
  系统A： cache写hit时采用write back(方案A)
  系统B： cache写hit时采用write through（方案B）
SW（store word）指令执行时的操作
  系统A：cache写hit时，采用write back只写cache （化1个cycle）;
    cache写miss时，依次完成（1）如果cache dirty先把cache的1个block写回内存（可使用write buffer加快速度，估计化1个cycle），如果cache不dirty则不写回内存（不花时间）。（2）把内存的1个block读入cache（可能化100 cycle）；（3） 写1个字到cache（化1个cycle），不写内存;

## Slide 53: Cache总结（SW指令）
SW（store word）指令执行时的操作，SD指令与此类似
  系统B-方案B1： write through with “Write allocate”.
    Cache写hit时，既写cache又写内存，写内存时使用write buffer加快速度;
    Cache写miss时，（1）把内存的1个block读入cache （可能化100 cycle） ，原cache内容直接丢弃；（2）同时写1个字到cache （化1个cycle）和内存（最快时化1个cycle） ，写内存时使用write buffer加快速度（但连续多条SW指令可能引起Write Stall--写停顿，下同）;
  系统B-方案B2： write through with “No write allocate” (Write around)
    Cache写hit时，与B1相同: 既写cache又写内存，写内存时使用write buffer加快速度;
    cache写miss时，采用“No write allocate”，不读内存的1个block到cache中 ，不写cache只写内存(写1个字到内存)，写内存时使用write buffer加快速度，最快时化1个cycle ;

## Slide 54
Consider a write miss in a write-through cache.
Options of write misses in write-through caches
  Write allocate（写分配）
    Allocate a cache block（在direct mapped cache中，不需要分配，可选的cache entry是唯一的，但在其它2种cache中，有多个cache entry可选，需要分配一个） , load 1 memory block into cache, then write 1 word or double word in cache
  No write allocate (aka Write around)
    The data is only written to main memory, not written into the cache. Don’t fetch a memory block to cache.
aka: also known as
5.3.3 Elaboration(详述): write misses in write- through caches
内容重复，不讲

## Slide 55: 5.3.3 Elaboration(详述): write operation of write-through cache
Suppose write-through cache (with write-allocate?) is used.
Step 1 in write-through cache: we write the data into the cache while reading the tag;
  If the tag matches, i.e. write hits ,write is finished in one cycle
    correct block has been updated, the processor can continue normally.
    Lkj补充：write operation: write a word or double words into memory, i.e. execute a SW or SD instruction .
  if the tag mismatches, then a miss occurs.
    the overwriting of the block in the cache is not catastrophic.
      Since memory has the correct value.
    Step 2: usually a memory block will be copied into cache with 10-100 cycle.
    Step 3: write a word or double words into memory (or both memory and cache).

## Slide 56: 5.3.3 Elaboration: write miss operation of write-back cache
Suppose write-back cache is used.
A write-back scheme is more complex to implement than write-through
When write miss occurs
  Step1:write the dirty block back to memory with 10-100 cycle
    If write-back buffer is used, this 10-100 cycle will decrease to minimum of 1 cycle.
    If dirty-bit is 0, step1 can be omitted.
  Step 2: a memory block will be copied into cache with 10-100 cycle.
  Step 3: write a word or double words in cache.
Overwriting cache block prior to hit tests is not allowed
  This would destroy the cache block (which is not backed up in memory)
  Although this is allowed for a write-through cache

## Slide 57: 5.3.3 Elaboration: write hit operation of write-back cache
When cache write hits, Method 1 : memory-stores may be finished in 2 cycles
  a cycle to check for a hit
  followed by a cycle to actually perform the write
When cache write hits, Method 2 : memory-stores may be finished using 1 normal cache cycle plus 1 unused cache cycle
  因为pipeline操作，本方法实际只消耗1个（不是2个）周期
  A store buffer must be used to hold data
  The processor lookups cache, and places the data into store buffer in 1 normal cache cycle.
    This take only one normal cache cycle based on pipeline.
    Now cache is hit, the new data in store buffer are written into cache on the next unused cache cycle.
    Here the new data is word for SW(Store Word), or double word for SD (Store Double-word), .

## Slide 58: 5.3.3 Elaboration: write-back caches also uses write buffers
Many write-back caches also include write buffers (here also called write-back buffer )
  to reduce the miss penalty
  when a miss occurs and a modified block is replaces.
    the modified block is moved to a write-back buffer while the requested block is read from memory.
    The cache block in write-back buffer is later written back to memory.

## Slide 59: 5.3.3 Elaboration: write-back caches also uses write buffers
Many write-back caches also include write buffers (here also called write-back buffer )
  to reduce the miss penalty
  when a miss occurs and a modified block is replaces.
    the modified block is moved to a write-back buffer while the requested block is read from memory.
    The cache block in write-back buffer is later written back to memory.
本页与上页内容全同，仅用于格式刷的黑字体模板来源

## Slide 60: 5.3.4 An Example Cache: The Intrinsity FastMATH Processor
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle simultaneously
Split cache: separate I-cache (Instruction cache) and D-cache (Data cache)
  Each 16KB: 256 blocks × 16 words/block,8-bit index, 18-bit tag, 18=32-8-6
  The processor can request both an instruction word and a data word on every clock.
  D-cache: write-through or write-back
In practice, to eliminate the multiplexor, caches use a separate large RAM for the data and a smaller RAM for the tags
SPEC2000 miss rates
  I-cache: 0.4%,D-cache: 11.4%, Weighted average: 3.2%

## Slide 61: Example: Intrinsity FastMATH
  16 words per block here

## Slide 62: 5.4 Measuring and Improving Cache Performance
We use CPU time to measure cache performance.
CPU time= (CPU execution clock cycles + Memory-stall clock cycles) ×Clock cycle time
Memory-stall clock cycles =Read-stall cycles + Write-stall cycles
For Read-stall:
Read-stall cycles = ×Read miss rate ×Read miss penalty
For a write-through plus write buffer scheme:
Write-stall cycles= ×Write miss rate ×Write miss penalty
+ Write buffer stalls
If the “write buffer stalls” are small, we can safely ignore them .
Reads
Program
Writes
Program

## Slide 63: Combine the reads and writes
In most write-through cache organizations, the read and write miss penalties are the same（假定用前面讲的B1方案，不用B2方案）
  the time to fetch the block from memory.
If we neglect the write buffer stalls, we get the following equation:
Memory-stall clock cycles ＝
× Miss rate × Miss penalty
We can also write this as:
Memory-stall clock cycles ＝
The above Instructions is the number of memory access instructions.
Memory accesses
Program
Instructions
Program
Misses
Instructions
×Miss penalty
×

## Slide 64: Calculating cache performance
Assume:
Instruction cache miss rate 2%
  data cache miss rate 4%
  CPI without any memory stalls 2
  miss penalty 100 cycles
  The Load & stores are 36% of instructions
Question: How faster a processor would run with a perfect cache?
Answer: (下面的单位都是cycles)
  Suppose total instruction count is I.
Instruction miss cycles = I×2%×100 =2.00I
Data miss cycles = I×36%×4%×100 =1.44I
Total memory-stall cycles= 2.00I+ 1.44I =3.44 I
CPI with stall = (total cycles for perfect cache + total memory-stalls) / I
= (2*I + 3.44 *I )/ I = 5.44
Total memory-stall cycles / Total cycles = 3.44 I/5.44I= 63%

## Slide 65: How faster a processor for ideal
What happens if the processor is made faster?
Assume CPI reduces from 2 to 1
Total cycles = total cycles for perfect cache + total memory-stalls
=1*I+3.44*I = 4.44I
CPU time with stalls
CPU time with perfect cache
I×CPIstall×Clock cycle
I×CPIperfect×Clock cycle
CPIstall
CPIperfect
5.44
2
=
=
=
CPU time with stalls
CPU time with perfect cache
I * CPIstall
I * CPIperfect
4.44
1
=
=
=4.44
=2.72
3.44
5.44
3.44
4.44
=63% to
=77%
Total memory-stall cycles / Total cycles = 3.44 I/4.44I= 77%
Total memory-stall cycles / Total cycles
from

## Slide 66: Calculating cache performance with Increased Clock Rate
Suppose we increase the performance of the computer in the previous example：doubling CPU clock rate ，while memory access time does not change.
Question : How much faster will the computer be with the faster clock to slow clock?
Answer
Total miss cycles per instruction = (2%×200) + 36%×(4%×200)=6.88
CPI with cache misses = 2 + 6.88 =8.88
Performance with fast clock
Performance with slow clock
Execution time with slow clock
Execution time with fast clock
I×CPIslow clock×Clock cycle
I×CPIfast clock×Clock cycle/2
5.44
8.88×1/2
=
=1.23
=
=
This, the computer with the faster clock is about 1.2 times faster rather than 2 time faster.
I: Instruction Count
本页内容书上无，不讲

## Slide 67: Average Access Time Per Instruction
Hit time is also important for performance
  Increasing the cache size will cause a bigger cache access time.
AMAT(Average Memory Access Time): the average time Per Instruction to access memory considering hit time, miss penalty, and miss rate.
  N Instructions
  Total time of memory access: N * hit-time + N * Miss-rate * Miss-penalty
  AMAT = (N * hit-time + N * Miss-rate * Miss-penalty) / N
  = hit-time + Miss-rate * Miss-penalty
  = Time for a hit + Miss rate × Miss penalty
Example: CPU with 1ns clock, hit time = 1 cycle(5-stage pipeline 在数据和指令访问都hit时每条指令的内存访问平均花一个cycle), miss penalty = 20 cycles, miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 68: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 69: Average Access Time Per Access
Hit time is also important for performance
  Increasing the cache size will cause a bigger cache access time.
AMAT(Average Memory Access Time): the average time Per access to access memory considering hit time, miss penalty, and miss rate.
  N memory access
  Total time of memory access: N * hit-time + N * Miss-rate * Miss-penalty
  AMAT = (N * hit-time + N * Miss-rate * Miss-penalty) / N
  = hit-time + Miss-rate * Miss-penalty
  = Time for a hit + Miss rate × Miss penalty
Example: CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns, 这里AMAT指指令内存的每次平均访问时间
    2 cycles per instruction
本书不用 AMAT per access

## Slide 70: 说明：本页PPT从另一角度计算 Average Memory Access time per access，最终结果（红色的公式） 与上页PPT相同
Average Memory Access time = (total-hit-time + total-miss-time) / I
=[I * hit rate * Cache time + I * miss rate *(Cache time + Miss_penalty) ] / I
= 99% * 5 + (100%-99%) * 45 =5.5ns
150605标注：这里 I=number of total memory access, Miss penalty=40ns，
hit rate=99%, miss rate =1%
发生缺失的单条指令花时间= Cache time +Miss_penalty=5+40=45ns
Average Memory Access time
= [ I * hit rate * Cache time + I * miss rate *(Cache time + Miss_penalty) ] / I
= [ I * (hit rate + miss rate )* Cache time + I * miss rate * Miss_penalty) ] / I
= [ I * Cache time + I * miss rate * Miss_penalty) ] / I
= Cache time + miss rate * Miss_penalty
Note: (hit rate + miss rate ) =100%
不讲，本书不用 AMAT per access

## Slide 71
Risc-V 第5版 P394上面的这段文字，红线画出的instruction 是否应写成 access 才正确？
Answer: 不用改

## Slide 72: Performance Summary
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls spend more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 73: The disadvantage of a direct-mapped cache
If the CPU requires the following memory units sequentially: word 0,word 8 and word 0. Word 0 and word 8 both are mapped to cache block 0, so the third access will be a miss.
  Suppose each block contains 1 word.
But obviously, if one memory block can be placed in any cache block , the miss can be avoided. So, there is possibility that the miss rate can be improved.
0
0
0
0
1
0
0
1
0
1
0
1
0
0
1
0
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
0
0
C
a
c
h
e
M
e
m
o
r
y
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1

## Slide 74
Direct mapped
  Block can only go in one place in the cache
    Memory-block-address MOD Number-of-blocks-in-cache
Fully associative ：Block can go anywhere in cache.
Set associative
  Block can go in one of a set in the cache.
  A set is a group of blocks in the cache.
    Memory-Block-address MOD Number-of-sets-in-the-cache
  If each set has n blocks, the cache is said to be n-way set associative.
Note that direct mapped is the same as 1-way set associative, and fully associative is m-way set-associative (for a cache with m blocks).

## Slide 75: Figure 8-32 Block Placement

## Slide 76: Q2: Block Identification
Every row of cache has an address tag that stores the main memory address of the data stored in the block.
When checking the cache, the processor will compare the requested memory address to the cache tag -- if the two are equal, then there is a cache hit and the data is present in the cache
Often, each cache block also has a valid bit that tells if the contents of the cache block are valid
不讲

## Slide 77: The basics of a set-associative cache Decreasing miss ratio with associativity
A set-associative cache is divided into some sets. A set contains several blocks.
A memory block is mapped to a set in the cache through a mapping algorithm.
  The memory block can be placed in any block in the corresponding set.
The mapping algorithm is:
Set number (Index) =
(Memory block number) modulo (Number of sets in the cache)
If a set has only one block, this set-associative cache is actually a direct-mapped cache.
If a set-associative cache has only one set, this set-associative cache is called a fully-associative cache.

## Slide 78: The Format of the Physical Memory Address
The Index field selects
  The set, in case of a set-associative cache
  The block, in case of a direct-mapped cache
  Has as many bits as log2(#sets) for set-associative caches, or log2(#blocks) for direct-mapped caches
The Byte Offset field selects
  The byte within the block
  Has as many bits as log2(size of block), here the size of block is total bytes in a block.
The Tag is used to find the matching block within the cache
  Has as many bits as Address_size – Index_size – Byte_Offset_Size

## Slide 79: An eight-block cache configured as variety-way

## Slide 80: Set Associative Cache Organization
Total 256 sets

## Slide 81: Miss rate versus set-associativity
Assume: there are three small caches, each consisting of four one-word blocks.
One cache is direct-mapped,
the second is two-way set associative
and the third is fully associative.
Question: Given the following sequence of block addresses: 0,8,0,6,8, find the number of misses for each cache organization.
Answer: for direct-mapped 5 misses
Memory block | Hit or miss | Contents after each reference |  |  | 
 |  | Set 0 | Set 1 | Set 2 | Set 3
 |  | Block 0 | Block 1 | Block 2 | Block 3
0 | Miss | M[0] |  |  | 
8 | Miss | M[8] |  |  | 
0 | Miss | M[0] |  |  | 
6 | Miss | M[0] |  | M[6] | 
8 | Miss | M[8] |  | M[6] | 

## Slide 82
Second, for the two-way set associative cache. 4 misses
Memory block | Hit or miss | Contents after each reference |  |  | 
 |  | Set 0 |  | Set 1 | 
 |  | Block 0 | Block 1 | Block 2 | Block 3
0 | Miss | M[0] |  |  | 
8 | Miss | M[0] | M[8] |  | 
0 | Hit | M[0] | M[8] |  | 
6 | Miss | M[0] | M[6] |  | 
8 | Miss | M[8] | M[6] |  | 
Memory block | Hit or miss | Contents after each reference |  |  | 
 |  | Only one set |  |  | 
 |  | Block 0 | Block 1 | Block 2 | Block 3
0 | Miss | M[0] |  |  | 
8 | Miss | M[0] | M[8] |  | 
0 | Hit | M[0] | M[8] |  | 
6 | Miss | M[0] | M[8] | M[6] | 
8 | Hit | M[0] | M[8] | M[6] | 
Finally, for the fully associative cache. 3 misses

## Slide 83: How much of a reduction in the miss rate is achieved by associativity?
The data cache miss rates for organization like the Intrinsity FastMATH processor for SPEC2000 benchmarks with associativity varying from one-way to eight-way .
Data cache organization is 64KB data cache and 16-word block
Associativity | Data miss rate
1 | 10.3%
2 | 8.6%
4 | 8.3%
8 | 8.1%

## Slide 84: Size of tags versus set associativity
Assume
  Cache size is 4K Block
  Block size is 4 words
  Physical address is 32bits
Question
Find the total number of set and total number of tag bits for variety associativity
Answer
Offset size (Byte) = 16= 24 4 bits for byte-offset Number of memory block = 232÷24=228 28 bits for memory Block # Number of cache block = 212 12 bits for cache Block #
For direct-mapped
Bits of index = 12 bits
bits of Tag = (28-12) ×4K=16×4K=64 Kbits
32-bits address:
4 bits

## Slide 85
For two-way associative
Number of cache set = 212 ÷ 2= 211
Bits of index =11 bits
Bits of Tag = (28-11) ×4K=17×4K=68 Kbits
For four-way associative
Number of cache set = 212 ÷ 4= 210
Bits of index =10 bits
Bits of Tag = (28-10) ×4K=18×4K=72 Kbits
For full associative
Number of cache set = 1
Bits of index = 0 bits
Bits of Tag = (28-0) ×4K=112 Kbits
 | Direct | 2-way | 4-way | Fully
Index(bit) | 12 | 11 | 10 | 0
Tag(bit) | 16 | 17 | 18 | 28

## Slide 86
In a direct-mapped cache, there is only one block that can be replaced
In set-associative and fully-associative caches, there are N blocks (where N is the degree of associativity
Choosing which block to replace

## Slide 87: Strategy of block Replacement
Several different replacement policies can be used
  Random replacement - randomly pick any block
    Easy to implement in hardware, just requires a random number generator
    Spreads allocation uniformly(均衡地) across cache
    May evict a block that is about to be accessed
  Least-recently used (LRU) - pick the block in the set which was least recently accessed
    Assumed more recently accessed blocks more likely to be referenced again
    This requires extra bits in the cache to keep track of accesses.
  First in,first out(FIFO)-Choose a block from the set which was first came into the cache

## Slide 88: 5.4.3 Choosing which block to replace
In an associative cache, we must decide which block to replace when a miss happens and the corresponding set is full.
The most commonly used scheme is least recently used (LRU), which we used in the previous example. In an LRU scheme, the block replaced is the one that has been unused for the longest time.
For a two-way set associative cache, the LRU can be implemented easily. We could keep a single bit in each set. We set the bit whenever a specific block in the set is referenced, and reset the bit whenever another block is referenced.
As associativity increases, implementing LRU gets harder.

## Slide 89: 5.4.4 Decreasing miss penalty with multilevel caches
Add a second level cache:
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  Part1: With just primary cache, CPI of 1.0 on a 5GHz machine with a 2% miss rate, 100ns DRAM access
  Miss penalty to main memory is
  The CPI with one level of caching
Total CPI = 1.0 + Memory-stall cycles per instruction
    =( 1.0 *I+ 2%*I × 500 ) / I = 1.0 + 2% × 500 = 11.0
  Part2: Adding 2nd level cache with 5ns access time, decreases miss rate to 0.5%（That is，for n instructions( not n memory accesses)，total 0.5%*n access to DRAM， total 2%*n access to the 2nd level cache ）
  Suppose: no double miss (both instruction cache and data cache miss ) occurs during each one-instruction execution.(书上没说，但这条很重要)
100ns
0.2
= 500 clock cycles
5ns
0.2
= 25 clock cycles=Miss penalty of 2nd level cache
本页及后4页PPT来自MIPS教材，非本书内容
不讲

## Slide 90
The CPI with Two level of cache with 0.5% miss rate for main memory
Total CPI = 1.0 + Primary stalls per instruction + Secondary stalls per instruction
= 1 + 2% ×25 + 0.5% × 500
= 1.0 + 0. 5 +2.5 = 4.0
The processor with secondary cache is faster, the faster factor(倍数) is
Using multilevel caches:
  try and optimize the hit time on the 1st level cache
  try and optimize the miss rate on the 2nd level cache
11.0
4.0
=2.8
不讲

## Slide 91
while L1 cache hit test is operating, we process L1 cache data fetching simultaneously, these 2 operations begin at the same time and cost same time.
L2 cache operates so.
Fig. Total time of an instruction reading memory with both miss of L1 and L2 cache: 526 cycles
不讲

## Slide 92: Decreasing miss penalty with multilevel caches
Total N instructions (e.g. N=10000, 4000 memory access instructions, 6000 other instructions such as ADD、SUB、AND、BEQ、J……, total memory access number: 14000(not N) )
  N*98% instructions without any miss penalty, time A=N*98%*H1 cycle
  N*2% instructions with miss of first level cache, time: B+C= N*2%*(H1+H2) + N*0.5% *M2
    N*1.5% access with hit of 2nd level cache, time B=N*1.5% *(H1+H2)
    N*0.5% access with miss of 2nd level cache, Time C= N*0.5% *(H1+H2+M2)
  3 kinds of access time
    H1: 1 cycle, access none of 2nd level cache and DRAM
    H2: 25 cycles to access 2nd level cache
    M2: 500 cycles, miss penalty to access 2nd level cache (i.e. time to access DRAM)
Total time of N instructions: A+B+C
  = N*98%*H1 + N*2%*(H1+H2) + N*0.5% *M2
  = N*H1 + N*2%*H2 + N*0.5% *M2 = N*(1+2%*25+0.5%*500) = 4*N
average CPI=4N/N=4
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  CPI of 1.0 on a 5GHz machine with a 2% miss rate, 100ns DRAM access
  Adding 2nd level cache with 5ns access time decreases miss rate to 0.5%（That is，for n memory access instructions ，total 0.5%*n access to RAM， total 2%*n access to the 2nd level cache ）
Miss penalty to main memory is
Miss penalty to 2nd level cache is
不讲

## Slide 93: Decreasing miss penalty with multilevel caches
Total N instructions (e.g. N=10000, 4000 memory access instructions, 6000 other instructions such as ADD、SUB、AND、BEQ、J……, total memory access number: 14000(not N) )
  N*98% accesses without any miss penalty, time A=N*98%*H1 cycle
  N*2% accesses with miss of first level cache, time: B+C= N*2%*(H1+H2) + N*0.5% *M2
    N*1.5% instructions with hit of 2nd level cache, time B=N*1.5% *(H1+H2)
    N*0.5% instructions with miss of 2nd level cache, Time C= N*0.5% *(H1+H2+M2)
  3 kinds of access time
    H1: 1 cycle, hit time to access first level cache
    H2: 25 cycles, hit time to access 2nd level cache
    M2: 500 cycles, miss penalty to access 2nd level cache (time to access DRAM)
Total time of N instructions: A+B+C
  = N*98%*H1 + N*2%*(H1+H2) + N*0.5% *M2
  = N*H1 + N*2%*H2 + N*0.5% *M2 = N*(1+2%*25+0.5%*500) = 4*N
average CPI=4N/N=4
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  CPI of 1.0 on a 5GHz machine with a 2% miss rate, 100ns DRAM access
  Adding 2nd level cache with 5ns access time decreases miss rate to 0.5%（That is，for n memory access instructions ，total 0.5%*n access to RAM， total 2%*n access to the 2nd level cache ）
Miss penalty to main memory is
Miss penalty to 2nd level cache is
本页是一种错误的解题思路，要引起注意
不讲

## Slide 94: 5.4.4 Decreasing miss penalty with multilevel caches
Add a second level cache:
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  Part1: With just primary cache, CPI of 1.0 on a 4GHz machine with a 2% miss rate, 100ns DRAM access
  Miss penalty to main memory is
  The CPI with one level of caching
Total CPI = 1.0 + Memory-stall cycles per instruction
    =( 1.0 *I+ 2%*I × 400 ) / I = 1.0 + 2% × 400 = 9
    I: total instruction number
  Part2: Adding L-2 cache with 5ns access time, decreases miss rate to 0.5%（That is，for n instructions( not n memory accesses)，total 0.5%*n access to DRAM， total 2%*n access to the 2nd level cache ）
  Suppose: no double miss (both instruction cache and data cache miss ) occurs during each one-instruction execution.(书上没说,补充)
100ns
0.25
= 400 clock cycles
5ns
0.25
= 20 clock cycles=Miss penalty of 2nd level cache
同RISC-V教材

## Slide 95
Note: miss rate is the miss rate per instruction, not the miss rate per access.
The CPI with Two level of cache with 0.5% miss rate for main memory
Total CPI = 1.0 + Primary stalls per instruction + Secondary stalls per instruction
= 1 + 2% ×20 + 0.5% × 400
= 1.0 + 0. 4 +2 = 3.4
The processor with secondary cache is faster, performance ratio is
Using multilevel caches:
  try and optimize the hit time on the 1st level cache
  try and optimize the miss rate on the 2nd level cache
9.0
3.4
=2.6

## Slide 96: Direct-mapped Cache Example (1-word Blocks)
总结和回顾
不讲

## Slide 97: Fully-Associative Cache example (1-word Blocks)
Assume cache has 4 blocks
总结和回顾
不讲

## Slide 98: 2-Way Set-Associative Cache
Assume cache has 4 blocks and each block is 1 word
2 blocks per set, hence 2 sets per cache
总结和回顾
不讲

## Slide 99: Deep concept in Cache
Four Questions for Memory Hierarchy Designers
Caching is a general concept used in processors, operating systems, file systems, and applications.
There are Four Questions for Memory Hierarchy Designers
Q1: Where can a block be placed in the upper level?
(Block placement)
  Fully Associative, Set Associative, Direct Mapped
Q2: How is a block found if it is in the upper level? (Block identification)
  Use Tag
Q3: Which block should be replaced on a miss? (Block replacement)
  Random, LRU,FIFO
Q4: What happens on a write? (Write strategy)
  Write Back or [Write Through (with Write Buffer)]
总结和回顾
不讲

## Slide 100: 5.4.5 Decreasing Software Optimization via Blocking 因课时限制，本小节上课不讲，自学 5.5 Dependable Memory Hierarchy 在下一章【Chapter 8 Storage, Networks and Other Peripherals】（来源于第三版教材）讲 5.6 Virtual Machines 因课时限制，本小节上课不讲，自学

## Slide 101: 5.7 Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM （Virtual Memory）“block” is called a page
  如果虚拟地址的长度（位数）足够长，磁盘划出的用于虚拟内存的磁盘空间大小（字节数）为B，物理内存大小（字节数）为A，则用户可用的虚拟内存大小为A+B
§5.7 Virtual Memory

## Slide 102: 5.7 Virtual Memory
Main memory can act as a cache for the secondary storage (disk)
Advantages:
  illusion of having more physical memory
  program relocation
  protection
Virtual addr.
Physical addr.

## Slide 103: Pages: virtual memory blocks
Page faults: the data is not in memory, retrieve it from disk
  huge miss penalty, thus pages should be fairly large (e.g., 4KB)
  reducing page faults is important (LRU is worth the price)
  can handle the faults in software instead of hardware
  using write-through is too expensive so we use write back

## Slide 104: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS exception processing program
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms

## Slide 105: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table start address in physical memory
If page is present in memory
  PTE (Page Table Entry) stores the physical page number
  Plus other status bits (referenced, dirty, …)
    Reference bit (aka use bit) in PTE is set to 1 on each access to corresponding page, periodically cleared to 0 by OS
    Dirty bit in PTE is initialized to 0, set to 1 when any byte of the page is written
    Valid bit
      0: the page is present in disk, and a page fault occurs.
      1: the page is present in main memory
  Plus other page protection bits (writable, non-kernel process readable, …)
If page is not present in memory
  PTE can refer to location in swap space on disk

## Slide 106: Mapping Pages to Storage
valid bit
0: the page is present in disk, and a page fault occurs.
1: the page is present in main memory

## Slide 107: 5.7.1 Placing a page and finding it again ----Page Tables
Virtual memory systems use fully associative mapping method

## Slide 108: 5.7.2 Page faults
When the OS creates a process, it usually creates the space on disk for all the pages of a process.
When a page fault occurs, the OS will be given control through exception mechanism.
The OS will find the page in the disk by the page table.
Next, the OS will bring the requested page into main memory. If all the pages in main memory are in use, the OS will use LRU strategy to choose a page to replace
It is possible that part of the page table is moved into data cache (依据：书P435第8行）
Virtual page

## Slide 109: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE is set to 1 on access to page
  Reference bit is periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Write through is impractical
  Use write-back
  Dirty bit in PTE is set to 1 when page is written
5.7.4 What about writes?

## Slide 110: 5.7.5 Making Address Translation Fast----TLB
Fast Translation Using a TLB
TLB (Translation-Lookaside Buffer)：A cache for address translations, more accurate to call it a translation cache, 中文常称为【快表】
Address translation requires extra memory references
  One to access the page table in memory
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called Translation Look-aside Buffer (TLB), it make translation faster.
  Typical: 16–512 entries, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate, 4–8 bytes each TLB entry
  cache block size: size of 1-2 TLB entry
  TLB Misses could be handled by hardware or software
Lookaside:后备，旁视

## Slide 111: 5.7.5 Making Address Translation Fast----TLB
Virtual page number in TLB acts as tag in cache
TLB一般都是fully-associative cache，极少数采用set-associative cache

## Slide 112: TLB Misses (virtual page number Not found in TLB)
When TLB Misses, 2 cases
  If page is in memory
    Load the PTE from memory and retry
    Could be handled in hardware
    Or in software
      Raise a special exception
  If page is not in memory (page fault)
    page fault exception happens, OS handles fetching the page and updating the page table
    Then restart the faulting instruction (e.g. LD,SD,LW,SW…)

## Slide 113: TLB Miss Handler
TLB miss indicates
  Page present in memory, but PTE not in TLB
  Or page not present in memory
TLB Miss Handler in Intrinsity FastMATH do:
  Hardware saves the virtual page number of the reference into a special register
  Generates an exception which handles the miss in software.
  Exception handler (software) do:
    Use virtual page number to find entry in page table
    If the PTE have a valid physical address: Copies PTE (page table entry) in memory to TLB, restarts the instruction, get physical address in TLB.
    If the PTE does not have a valid physical address, page fault will occur

## Slide 114: Page Fault Exception Handler
Use faulting virtual address to find PTE
Locate page on disk
Choose page to replace
  If dirty, write to disk first
Read page into memory and update page table
Copy updated PTE into TLB (补充）
Re-execute faulting instruction (e.g. LW, LD, SD……)
本页PPT书上好像没有

## Slide 115: 5.7.6 The Intrinsity FastMATH TLB An real example: the Intrinsity FastMATH
both virtual page number and physical page number are 20 bits
The TLB contains 16 entries, mixed with instruction PTE and data PTE
Each TLB entry is 64 bits wide
  a 20-bit tag (i.e. virtual page number)
  a 20-bit physical page number
  a valid bit, a dirty bit…...
Its cache is direct mapped cache
Like most MIPS systems, it uses software to handle TLB misses. A TLB miss exception takes about 13 clock cycles, assuming
  the exception code is in instruction cache
  the page table entry (PTE) is in data cache.

## Slide 116
Used in Intrinsity FastMATH Memory Hierarchy

## Slide 117: TLBs and caches scheme in Intrinsity FastMATH CPU adopting write-through with write allocate for cache
全图
FIGURE 5.32 Processing a read or a write-through in the Intrinsity FastMATH TLB and cache

## Slide 118: TLBs and caches
放大后的局部图

## Slide 119: TLBs and caches
放大后的局部图

## Slide 120
Our virtual memory and cache systems work together as a hierarchy:
  data cannot be in the cache unless it is present in main memory.
When OS migrate every page from main memory to secondary memory（disk）
  It flushes all contents of this page from cache.
  It modifies the page table entry and clears TLB entry of this page to indicate the page migrated to disk.
5.7.7 Integrating Virtual Memory, TLBs, and Caches

## Slide 121: Possible combinations of Event
Three different types of misses: TLB miss, page Fault, cache miss
Page table Miss: =[page fault], page is in disk;
Page table Hit: page is in memory

## Slide 122
The most important function of virtual memory
  to allow sharing of a memory area by multiple processes
  providing memory protection among these processes, (including OS process)
to implement protection in the virtual memory, the hardware must provide 3 functions:
  Support at least two modes
    user process mode
    supervisor process mode
      operating system process = supervisor process = kernel process = executive process.
  Provide information of the process state: user/supervisor mode bit, the page table pointer, the TLB.
    a user process can read but not write these information.
    OS uses special instructions (only available in supervisor mode) to write these information
5.7.8 Implementing Protection with Virtual Memory

## Slide 123
  the processor can go from user mode to supervisor mode, and vice versa.
    The first direction is finished by a system call exception (instruction ECALL in RISC-V)
      It transfers control to a dedicated location in supervisor code space.
    Like other exception, PC is saved in the SEPC (supervisor exception program counter), and the processor enters supervisor mode.
    To return to user mode from the exception, use the supervisor exception return (instruction SRET)
补充知识（非本书内容，[操作系统]课）
  每一个进程都拥有一个自己的页表，每一个进程的PCB（Process Control Block,进程控制块）中有指针指向本进程的页表。
  当进程切换时，比如现在是进程1运行，TLB中放的是进程1的相关数据的地址，突然切换到进程2，TLB中原有的数据不是进程2相关的，此时TLB刷新数据有两种办法:
    全部刷新：很简单，但花销大，很多不必刷新的数据也刷新，增加了花销
    部分刷新：根据标志位，刷新需要刷新的数据，不需要刷新的被保留。

## Slide 124
storing the page tables in OS address space, the OS can change the page tables
  a user process can not change page tables
  process A can not change any page table mapping.
  process A can not map its virtual page to physical page of process B
  protecting data of process B from reading or writing by process A;
To allow another process P1 to read a page owned by process P2,
  P2 asks OS to create a page table entry mapping virtual page of P1 to P2’s physical page that P2 wants to share.
  The OS use the write protection bit to prevent P1 from writing the data.
5.7.8 Implementing Protection with Virtual Memory

## Slide 125: Modern Systems
Very complicated memory systems: