## Slide 1: Chapt 2-1: Memory hierarchy
Memory hierarchy
The basic of cache
Organization of main memory
1

## Slide 2: Chapter B & 2: Memory Hierarchy
Memory Hierarchy ABC
How to improve Cache performance
Memory Organization
Virtual Memory

## Slide 3: 2.1 Introduction
Why do designers need to know about memory technology?
  Processor performance is usually limited by memory bandwidth
  As IC densities increase, lots of memory will fit on processor chip
Application requirements:
  Unlimited amounts of memory
  Faster memory, higher bandwidth
  Lower price per byte
  If for embedded systems: lower power comsumption
These requirements are contradictory.
  The bigger, more difficult to make it fast
  The faster, more expensive
  The faster will consume much more power.

## Slide 4: Memory Technologies
Random Access Memories
  DRAM: Dynamic Random Access Memory
    High density, low power, cheap, slow
    Dynamic: needs to be “refreshed” regularly
  SRAM: Static Random Access Memory
    Low density, high power, expensive, fast
    Static: content will last “forever”(until lose power)
What gets used where?
  Main memory is DRAM: you need it big, so you need it cheap
  CPU cache memory is SRAM: you need it fast, so it’s more expensive, so it’s smaller than you would usually want due to resource limitations
Relative performance
  Size: DRAM/SRAM: 4-8x bigger for DRAM
  Cost/Cycle time: SRAM/DRAM: 8-16x faster, more $$$ for SRAM

## Slide 5: Memory Hierarchy: a natural Solution
How can we provide a memory with small access time, big capacity and lower price ?
The first principle: make the common case fast !
  What is the common case ?
Recall: the principle of locality of reference !
  Program access a relatively small portion of the address space at any instant of time.
  Ok, we should make these accesses more quickly.
  We can hold the recently accessed items in a fast memory.
Yeah: Smaller memories will be faster !
  We can use more expensive and smaller memories to hold the most recently used items.
  The cost and power impact is lessoned for small size.

## Slide 6: What is Memory Hierarchy ?
Memory hierarchy is organized into several levels:
  Each smaller, faster, and more expensive per byte than the next lower level.
  Temporal Locality (Locality in Time):
   Keep most recently accessed data items closer to the processor
  Spatial Locality (Locality in Space):
   Move blocks consists of contiguous words to the faster levels
Notes: Y-axis is performance
X-axis is time
Latency
Cliché:
Not e that x86 didn’t have cache on chip until 1989

## Slide 7: Memory Hierarchy
The goal:To provide a memory system with cost most almost as low as the cheapest level of memory and speed almost as fast as the fastest level.
Control
Datapath
Secondary
Storage
(Disk)
Processor
Registers
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
On-Chip
Cache
Fastest
Slowest
Smallest
Biggest
Highest
Lowest
Speed:
Size:
Cost:
Compiler
Hardware
Operating System

## Slide 8: Levels of the Memory Hierarchy
CPU Registers
500 Bytes
<250 ps
Cache
K Bytes
1-10ns
1-0.1 cents/bit
Main Memory
1G Bytes
100ns- 150ns
$.0001-.00001 cents /bit
Disk
T Bytes, 10 ms (10-5-10-6 cents/bit
Capacity
Access Time
Cost
Tape
infinite
sec-min
10-8
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Xfer Unit
prog./compiler
1-8 bytes
cache cntl
8-128 bytes
OS
512-4K bytes
user/operator
Mbytes
Upper Level
Lower Level
faster
Larger

## Slide 9: Who Cares About the Memory Hierarchy?
1980: no cache in µproc; 2001: 2-level cache on chip (1989 first Intel µproc with a cache on chip)
DRAM
7%/yr.
DRAM
µProc
20%/yr.
CPU
Processor-Memory
Performance Gap: (grows 50% / year)
“Moore’s Law”
“Less’ Law?”
µProc
52%/yr.
µProc
25%/yr.

## Slide 10: Different concerns for desktops, servers, and embedded computers
Desktop computers:
  primarily running one application for single user
  concerned more with average latency from the memory hierarchy.
Servers computers:
  May have hundreds of users running potentially
  dozens of applications simultaneously.
  concerned about memory bandwidth.
Embedded computers:
  Used for real-time applications, so worst-case performance is a focus
  Power and battery life, may NOT choose hardware optimizations
  Running only one application using very simple OS, so protection role of memory is often diminished.
Notes: 1st generation
Latency 1/2
but Clock rate 3X and IPC is 3X
Now move to other 1/2 of industry

## Slide 11: Memory Hierarchy Terminology
Hit: data appears in some block in the faster level (Block X)
  Hit Rate the fraction of memory access found in the faster level
  Hit Time: Time to access the faster level which consists of
    Memory access time + Time to determine hit/miss
Miss: data needs to be retrieve from a block in the slower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level +
    Time to deliver the block to the processor
Hit Time << Miss Penalty
Slower Level
Memory
Faster Level
Memory
To Processor
From Processor
Block X
Block Y

## Slide 12: Review of the ABCs of Caches
36 terms of Cache
Cache Virtual memory
data cache Instruction cache unified cache
block page tag field
Block address index field block offset
full associative set associative direct mapped
n-way set associative set address trace
misses per instruction Memory stall cycles miss penalty
Valid bit dirty bit locality
cache hit hit time
cache miss miss rate page fault
Write through write back write allocate
random replacememt least-recently used no-write allocate
Average memory access time write buffer write stall

## Slide 13: What is a cache?
Small, fast storage used to improve average access time to slow memory.
In computer architecture, almost everything is a cache!
  Registers “a cache” on variables – software managed
  First-level cache a cache on second-level cache
  Second-level cache a cache on memory
  Memory a cache on disk (virtual memory)
  TLB a cache on page table
  Branch-prediction a cache on prediction information?

## Slide 14: Four Questions for Memory Hierarchy Designers
Q1: Where can a block be placed in the upper level?
(Block placement)
  Fully Associative, Set Associative, Direct Mapped
Q2: How is a block found if it is in the upper level? (Block identification)
  Tag/Block
Q3: Which block should be replaced on a miss? (Block replacement)
  Random, LRU,FIFO
Q4: What happens on a write? (Write strategy)
  Write Back or Write Through (with Write Buffer)

## Slide 15: Q1: Block Placement
Direct mapped
  Block can only go in one place in the cache
Usually (address) MOD (Number of blocks in cache)
Fully associative
  Block can go anywhere in cache.
Set associative
  Block can go in one of a set of places in the cache.
  A set is a group of blocks in the cache.
  (Block address) MOD (Number of sets in the cache)
  If sets have n blocks, the cache is said to be n-way set associative.
Note that direct mapped is the same as 1-way set associative, and fully associative is m-way set-associative (for a cache with m blocks).

## Slide 16: 8-32 Block Placement

## Slide 17: Q2: Block Identification
Every block has an address tag that stores the main memory address of the data stored in the block.
When checking the cache, the processor will compare the requested memory address to the cache tag -- if the two are equal, then there is a cache hit and the data is present in the cache
Often, each cache block also has a valid bit that tells if the contents of the cache block are valid

## Slide 18: The Format of the Physical Address
The Index field selects
  The set, in case of a set-associative cache
  The block, in case of a direct-mapped cache
The Byte Offset field selects
  The byte within the block
  Has as many bits as log2(size of block)
The Tag is used to find the matching block within a set or in the cache
  Has as many bits as
  (AddressSize) – (IndexSize) – (ByteOffsetSize)

## Slide 19: Direct-mapped Cache Example (1-word Blocks)

## Slide 20: Fully-Associative Cache example (1-word Blocks)
Assume cache has 4 blocks

## Slide 21: 2-Way Set-Associative Cache
Assume cache has 4 blocks and each block is 1 word
2 blocks per set, hence 2 sets per cache
index

## Slide 22: Example: set associate cache
Memory size: 4G, Cache 8K, 2-way set associate

## Slide 23: Q3: Block Replacement
In a direct-mapped cache, there is only one block that can be replaced
In set-associative and fully-associative caches, there are N blocks (where N is the degree of associativity

## Slide 24: Strategy of block Replacement
Random replacement - randomly pick any block
  Easy to implement in hardware, just requires a random number generator
  Spreads allocation uniformly across cache
  May evict a block that is about to be accessed
Least-recently used (LRU) - pick the block in the set which was least recently accessed
  Assumed more recently accessed blocks more likely to be referenced again
  This requires extra bits in the cache to keep track of accesses.
First in,first out(FIFO)-Choose a block from the set which was first came into the cache

## Slide 25: Implementation of Replacement
Psedo LRU
Example:
V NV
A 1 0
B 0 1
C 0 0
D 0 0
When Miss:
Kick out the Victim,
Make the NextVictim to be Victim,
and select one from the left two blocks to be the NextVictim

## Slide 26: Another psedo LRU
3 bit for a set ( 4-way )
One bit for which is the LRU in AB
One bit for which is the LRU in CD
One bit for which is the LRU in AB / CD

## Slide 27: Q4: Write Strategy
When data is written into the cache (on a store), is the data also written to main memory?
write-through : The information is written to both the block in the cache and to the block in the slower memory
    Cache control bit: only a valid bit
    memory (or other processors) always have latest data
    Always combined with write buffers so that don’t wait for slow memory
write-back:The information is written only to the block in the cache. The modified cache block is written to main memory only when it is replaced
    Cache control bits: both valid and dirty bits
    much lower bandwidth, since No writes to slow memory for repeated write accesses

## Slide 28: Pros and Cons for write strategy
Write-through adv:
  Read misses don't result in writes,
  memory hierarchy is consistent and it is simple to implement.
Write back adv:
  Writes occur at speed of cache
  main memory bandwidth is smaller when multiple writes occur to the same block.
Notes: 可能是write back和write through比需要的内存带宽降低 ，因为基本都写cache里了
(上面两个方法的对比）

## Slide 29: Write stall
Write stall ---When the CPU must wait for writes to complete during write through
Write buffers
  A small cache that can hold a few values waiting to go to main memory,to avoid stalling on writes
  This buffer helps when writes are clustered.
  It does not entirely eliminate stalls since it is possible for the buffer to fill if the burst is larger than the buffer.

## Slide 30: Write Through via Buffering
Processor writes data into the cache and the write buffer
Memory controller writes contents of the buffer to memory
Increased write frequency can cause saturation of write buffer
If CPU cycle time too fast and/or too many store instr. in a row:
  Store buffer will overflow no matter how big you make it
  The CPU Cycle Time get closer to DRAM Write Cycle Time
Write buffer saturation can be handled by installing a second level (L2) cache
Processor
Cache
Write Buffer
DRAM
Processor
Cache
Write Buffer
DRAM
L2
Cache

## Slide 31: Write buffers
write
buffer
CPU
in out
DRAM
(or lower mem)
Write Buffer

## Slide 32: Write policy when misses
If a miss occurs on a write (the block is not present), there are two options.
Write allocate
    The block is loaded into the cache on a miss before anything else occurs.
Write around (no write allocate)
    The block is only written to main memory
    It is not stored in the cache.
In general, write-back caches use write-allocate , and write-through caches use write-around .

## Slide 33: Example
Assume a fully associative wtrie-back cache with many cache entries that starts empty.below is a sequence of five memory operations(the address is in square brackets):
  1 write Mem[100];
  2 write Mem[100];
  3 Read Mem[200];
  4 write Mem[200];
  5 write Mem[100];
What are the number of hits and misses when using no-write allocate versus write allocate?
Answer :
for no-write allocate misses: 1,2,3,5
hit : 4
for write allocate misses: 1,3
hit : 2,4,5

## Slide 34: Split vs. unified caches
Unified cache
  All memory requests go through a single cache.
  This requires less hardware, but also has lower hit rate
Split I & D cache
  A separate cache is used for instructions and data.
  This uses additional hardware, though there are some simplifications (the I cache is read-only).
Proc
Unified
Cache-1
Unified
Cache-2
Proc
I-Cache-1
D-Cache-1
Unified
Cache-2

## Slide 35: Split vs. mixed cache
Miss per 1000 instructions for 2-way associate cache.
Average miss rate = Inst%  MRinst. + Data% MRdata
Split : remove the misses due to conflicts between inst. blocks and data blocks , but has fixed cache space for both instructions and data.

## Slide 36: Example:Alpha 21264 data cache

## Slide 37: Superviser cache / User cache
Instruction Cache
Supervisor/ User Space Bit
    1: Supervisor access only
    0: Supervisor / User access

## Slide 38: Procedure for Cache Accessing
Step2 Index selection , Reading the two tags from cache.
Step1 Cache is divided into 2 fields: the 38 bit block address and the 6-bit block offset(64=26and 38+6=44).
Step3 the two tags are compared and the winner is selected.Tag contains the valid bit, otherwise the results of the comparion are ignored.
Step4 If one tag does match, CPU loads the proper data from the cache, otherwise from main memory.
The 21264 allows 3 clock cycles for these four steps,so the instructions in the following 2 clock cycles would wait if they tried to use the result of the load.