## Slide 1: Ch2-2 How to improve cache performance (cont.)

## Slide 2: 5.3 Cache performance
CPU Execution time=
=(CPU clock cycles + Memory stall cycles)×Clock cycle time
  CPIExecution includes ALU and Memory instructions

## Slide 3: Average Memory Access Time
Average Memory Access Time＝
Whole accesses time
All memory accesses in program
Accesses time on hitting+ Accesses time on miss
All memory accesses in program
＝
＝ Hit time + (Miss Rate × Miss Penalty)

## Slide 4: Cache performance metrics
Miss rate
  Independent of the speed of hardware.
Average memory access time (AMAT)
  Better than miss rate , but
  Indirect measure of performance
CPUtime

## Slide 5: Ex1: Impact on Performance
Suppose a processor executes at
  Clock Rate = 200 MHz (5 ns per cycle), Ideal (no misses) CPI = 1.1
  50% arith/logic, 30% ld/st, 20% control
Suppose that 10% of memory operations get 50 cycle miss penalty
Suppose that 1% of instructions get same miss penalty
Calculate the AMAT and real CPI.
Answer:
AMAT=(1/1.3)x[1.1+0.01x50]+(0.3/1.3)x[1.1+0.1x50]
=2.64
CPI = ideal CPI + average stalls per instruction
= 1.1(cycles/ins) + [ 0.30(DataMops/ins) x 0.10(miss/DataMop) x 50 (cycle/miss)] + 1(InstMop/ins) x 0.01 (miss/InstMop) x 50 (cycle/miss)] = (1.1 + 1.5 + .5) cycle/ins = 3.1
= ideal CPI + (AMAT - HitTime) x AccessOp/ins
= 1.1 + (2.64 – 1.1) x (1 + 0.3) = 3.1
Notes: Average stalls per instruction = (AMAT – HitTime) x access times/ins

## Slide 6: Ex2: Impact on Performance
Assume : Ideal CPI=1 (no misses)
L/S’s structure . 50% of instructions are data accesses
Miss penalty is 25 clock cycles
Miss rate is 2%
How faster would the computer be if all instructions were cache hits?
Answer: first compute the performance for always hits:
CPUexecution time =(CPU clock cycles+memory stall cycles)×clock cycle
=(IC ×CPI+0) ×Clock cycle
=IC ×1.0 ×clock cycle

## Slide 7: Answer for example 2 (cont.)
Now for the computer with the real cache,first compute memory stall cycles:
The performance ratio is the inverse of the execution times
CPU execution time cache 1.75 ×IC ×Clock cycle
CPU execution time 1.0 × IC ×clock cycle
The computer with no cache misses is 1.75 time faster.
＝
The total performance is thus:
CPU execution time cache =(IC ×1.0+IC ×0.75) ×Clock cycle
=1.75 ×IC ×Clock cycle

## Slide 8: Ex3: Impact on Performance
Assume : unified caches: 32K unified cache
Split cache: 16K D-cache and 16K I-cache
36% of the instructions are data transfer instructions
A hit takes 1 colck cycle
The miss penalty is 100 clock cycles
A load/store take 1 extra clock cycle on a unified cache
Write-through with a write-buffer
and ignore stalls due to the write buffer
What is the average memory access time in each case?

## Slide 9: MR for Uni.cache & split cache
Miss per 1000 instructions for 2-way associate cache.

## Slide 10: Answer for example 3
Answer : first let’s convert misses per 1000 instructions into miss rate.
Misses
/1000 instruction
Memory accesses/instruction
Miss rate=
Since every instruction access has exactly one memory access to fetch the instruction, according as Figure 5.8 the instruction miss rate is
Since 36% of the instructions are data transfers, according as Figure 5.8 the data miss rate is
Miss rate 16KB instruction＝
3.82/1000
1.0
＝0.0038
Miss rate 16KB data＝
40.9/1000
0.36
＝0.1136

## Slide 11: Answer for example 3 (cont.)
Basing on Figure 2.32 on page 138 there is 74% instruction references in split cache. The average miss rate for the split cache is:
(74%×0.0038)+(26% × 0.1136)=0.0323
Thus ,a 32KB unified cache has a slightly lower effective miss rate than two 16KB caches.
Form Figure 5.8 The unified miss rate needs to account for instruction and data accesses:
Miss rate 32KB unified＝
43.3/1000
1.00+0.36
＝0.0318

## Slide 12: Answer for Example3 (cont.)
Therefore,the time for each organization is
Average memory access timesplit
=74%×(1+0.0038×100)+ 26%×(1+0.1136×100)
=(74%×1.38)+(26%×12.36)=1.021+3.214=4.25
Average memory access timeunified
=74%×(1+0.0318×100)+ 26%×(1+1+0.0318×100)
=(74%×4.18)+(26%×5.18)=3.093+1.347=4.40
The average memory access time can be divided into instruction and data accesses:

## Slide 13: Ex4: Impact on Performance
Assume: in-order execution computer, such as the Ultra SPARC Ⅲ.
  Miss penalty: 100 clock cycles
  Miss rate : 2%
  Memory references Per instruction: 1.5
  Average cache misses per 1000 instructions: 30
  CPI ＝1.0(ignoring memory stalls)
What is the impact on performance when behavior of the cache is included (Calculate the impact using both misses per instruction and miss rate.)?

## Slide 14: Answer for example 4
Answer : The performance, including cache misses, is
CPU time with cache ＝
＝IC×(1.0+(30/1000×100)) × Clock cycle time
＝IC × 4.00 × Clock cycle time
Now caculating performance using miss rate:
CPU time with cache ＝
＝IC×(1.0+(1.5×2%×100)) × Clock cycle time
＝IC × 4.00 × Clock cycle time

## Slide 15: Answer for example 4 (cont.)
The clock cycles time and instruction count are the same, with or without a cache. Thus, CPU time increases fourfold, with CPI from 1.00 a “perfect cache” to 4.00 with a cache that can miss.
Without any memory hierarchy at all the CPI would increase again to 1.0+100×1.5 or 151—factor of almost 40 time longer than a system with a cache.

## Slide 16: Cache misses have a double-barreled impact on a CPU
The lower the CPIexecution, the higher the relative impact of a fix number of cache miss clock cycle.
When calculating CPI, the cache miss penalty is measured in CPU clock cycles for a miss. Therefore, even if memory hierarchies for two computers are identical, the CPU with the higher clock rate has a larger number of clock cycles per miss and hence a higher memory portion of CPI.

## Slide 17: Ex5: Impact on Performance
Assume: CPI=2 (perfect cache) clock cycle time＝1.0 ns
  MPI(memory reference per instruction)＝1.5
  Size of both caches is 64K and size of both block is 64 bytes
  One cache is direct mapped and other is two-way set associative. the former has miss rate of 1.4%, the latter has miss rate 1.0%
  The selection multiplexor forces CPU clock cycle time to be stretched 1.25 times
  Miss penalty is 75ns,and hit time is 1 clock cycle
What is the impact of two diffect cache organizations on performance of CPU (first,calculate the average memory access time and then CPU performance.)?

## Slide 18: Answer for example 5
Answer : Average memory access time is
Average memory access time＝Hit time+Miss rate×miss penalty
Thus, the time for each organization is
Average memory access time1-way＝1.0+(0.014×75)＝2.05 ns
Average memory access time2-way＝1.0×1.25 +(0.01 ×75)
＝2.00 ns
The average memory access time is better for the 2-way set-associative cache.

## Slide 19: Answer for example 5 (cont.)
CPU performance is
Substituting 75 ns for (miss penalty×Clock cycle time), the performance of each cache organization is
CPU time1-way＝IC×(2×1.0+(1.5 ×0.014 ×75))＝3.58 ×IC
CPU time2-way＝IC×(2×1.0×1.25+(1.5 ×0.010 ×75))＝3.63 ×IC

## Slide 20: Answer for example 5 (cont.)
Relative performance is
In contrast to the results of average memory access time, the direct-mapped leads to slighly better average performance. Since CPU time is our bottom-line evaluation.

## Slide 21: Miss penalty and Out-of-order Execution Processors
How do you define “miss penalty”?
Is it the full latency of the miss to memory, or
is it just the “exposed” or nonoverlapped latency when the processor must stall?
To In-order processor, there is out of question, but here is out of the question.
Refine memory stalls to lead to a new definition of miss penalty as nonoverlapped latency :

## Slide 22: Two definition
Length of memory latency –What to consider as the start and the end of a memory operation in an out-of-order processor.
Length of latency overlapped—What is the start of overlap with the processor(or equivalently, when do we say a memory operation is stalling the processor)

## Slide 23: Ex6: Performance on out-of-order processor
Assume: 30% of the 75 ns (52.5) miss penalty can be overlapped; Another parameters are same with example 5 (above example)
What is the impact of performance for out-of-order (OOO) CPU in direct-mapped cache?
Answer: Average memory access time for the OOO computer is:
Average memory access time1-way,OOO＝1.0*1.25+(0.014×52.5)
＝1.99 ns
The performance of the OOO cache is:
CPU time1-way,OOO＝IC×(2×1.0 *1.25+ (1.5×0.014×52.5))
＝3.60 ×IC
Hence, despite a much slower clock cycle time and the higher miss rate of a direct-mapped cache, the OOO computer can be slightly faster if it can hide 30% of the miss penalty.
Notes: OOO的PC reg前要加选择器选择执行哪条指令

## Slide 25: How to Improve Cache Performance?
1. Reduce the time to hit in the cache.--4
——small and simple caches, avoiding address translation, way prediction , and trace caches
2. Increase cache bandwidth .--3
—— pipelined cache access, multibanked caches, non-blocking caches,
3. Reduce the miss penalty--4
——multilevel caches, critical word first, read miss prior to writes, merging write buffers, and victim caches
4. Reduce the miss rate--4
——larger block size, large cache size, higher associativity,and compiler optimizations
5. Reduce the miss penalty and miss rate via parallelism--2
——hardware prefetching,and compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 26: 1st Hit Time Reduction Technique: Small and Simple Caches
Using small and Direct-mapped cache
The less hardware that is necessary to implement a cache, the shorter the critical path through the hardware.
Direct-mapped is faster than set associative for both reads and writes.
Fitting the cache on the chip with the CPU is also very important for fast access times.

## Slide 27: Hit time varies with size and associativity

## Slide 28: 2nd Hit Time Reduction Technique: Way Prediction
Way Prediction (Pentium 4 )
  Extra bits are kept in the cache to predict the way,or block within set of the next cache access.
  If the predictor is correct, the instruction cache latency is 1 clock clock cycle.
  If not,it tries the other block, changes the way predictor, and has a latency of 1 extra clock cycles.
  Simulation using SPEC95 suggested set prediction accuracy is excess of 85%, so way prediction saves pipeline stage in more than 85% of the instruction fetches.

## Slide 29: 3rd Hit Time Reduction Technique: Avoiding Address Translation during Indexing of the Cache
Page table is a large data structure in memory
TWO memory accesses for every load, store, or instruction fetch!!!
Virtually addressed cache?
  synonym problem
Cache the address translations?
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data

## Slide 30: TLBs
A way to speed up translation is to use a special cache of recently used page table entries -- this has many names, but the most frequently used is Translation Lookaside Buffer or TLB
Virtual Address Physical Address Dirty Ref Valid Access
Really just a cache on the page table mappings
TLB access time comparable to cache access time
(much less than main memory access time)

## Slide 31: Translation Look-Aside Buffers
Just like any other cache, the TLB can be organized as fully associative, set associative, or direct mapped
TLBs are usually small, typically not more than 128 - 256 entries even on high end machines. This permits fully associative lookup on these machines. Most mid-range machines use small n-way set associative organizations.
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
20 t
t
1/2 t
Translation
with a TLB

## Slide 32: Fast hits by Avoiding Address Translation
CPU
TB
$
MEM
VA
PA
PA
Conventional
Organization
CPU
$
TB
MEM
VA
VA
PA
Virtually Addressed Cache
Translate only on miss
Synonym Problem
VA
Tags
CPU
$
TB
MEM
VA
PA
Tags
PA
Virtual indexed, Physically tagged
Overlap $ access
with VA translation:
requires $ index to
remain invariant
across translation
L2 $

## Slide 33: Virtual Addressed Cache
Send virtual address to cache? Called Virtually Addressed Cache or
just Virtual Cache (vs. Physical Cache)
Every time process is switched logically must flush the cache; otherwise get false hits
  Cost is time to flush + “compulsory” misses from empty cache
  Add process identifier tag that identifies process as well as address within process: can’t get a hit if wrong process
Any Problems ?

## Slide 34: Virtual cache

## Slide 36: Dealing with aliases
Dealing with aliases (synonyms); Two different virtual addresses map to same physical address
NO aliasing! What are the implications?
HW antialiasing: guarantees every cache block has unique address
    verify on miss (rather than on every hit)
    cache set size <= page size ?
    what if it gets larger?
How can SW simplify the problem? (called page coloring)
  I/O must interact with cache, so need virtual address

## Slide 37: Aliases problem with Virtual cache
If the index and offset bits of two aliases are forced to be
the same, then the aliases address will map to the same block in cache.

## Slide 38: Overlap address translation and cache access (Virtual indexed, physically tagged)
Any limitation ?

## Slide 39: What’s the limitation?
IF it’s direct map cache, then
Cache size = 2index * 2blockoffset <= 2 pageoffset
How to solve this problem?
Use higher association. Say it’s a 4 way, then cache size can reach 4 times 2pageoffset with change nothing in index or tag or offset.

## Slide 40: Example: Virtual indexed, physically tagged cache
VPN: 30bits 8bits 5bits
=
=
VA
V D 25 bits 256 bits
V D 25 bits 256 bits
bank0
bank1
0
0
255
255
V D 30 bits 25 bits
=
=
=
=
VPN PPN
Cache
PPN：25bits
index block offset
TLB
Virtual address wide = 43 bits, Memory physical address wide = 38 bits, Page size = 8KB.
Cache capacity =16KB. If a virtually indexed and physically tagged cache is used.
And the cache is 2-way associative write back cache with 32 byte block size.

## Slide 41: 4th Hit Time Reduction Technique: Trace caches
Find a dynamic sequence of instructions including taken branches to load into a cache block.
The block determined by CPU instead of by memory layout.
Complicated address mapping mechanism

## Slide 42: Why Trace Cache ?
Bring N instructions per cycle
  No I-cache misses
  No prediction miss
  No packet breaks !
  Because branch in each 5 instruction, so cache can only provide a packet in one cycle.

## Slide 43: What’s Trace ?
Trace: dynamic instruction sequence
When instructions ( operations ) retire from the pipeline, pack the instruction segments into TRACE, and store them in the TRACE cache, including the branch instructions.
Though branch instruction may go a different target, but most times the next operation sequential will just be the same as the last sequential. ( locality )

## Slide 44: Whose propose ?
Peleg Weiser (1994) in Intel corporation
Patel / Patt ( 1996)
Rotenberg / J. Smith (1996)
Paper: ISCA’98

## Slide 45: Trace in CPU

## Slide 46: Instruction segment

## Slide 47: Pentium 4: trace cache, 12 instr./per cycle

## Slide 48: How to Improve Cache Performance?
1. Reduce the time to hit in the cache.--4
——small and simple caches, avoiding address translation, way prediction , and trace caches
2. Increase cache bandwidth .--3
—— pipelined cache access, multibanked caches, non-blocking caches,
3. Reduce the miss penalty--4
——multilevel caches, critical word first, read miss prior to writes, merging write buffers, and victim caches
4. Reduce the miss rate--4
——larger block size, large cache size, higher associativity,and compiler optimizations
5. Reduce the miss penalty and miss rate via parallelism--2
——hardware prefetching,and compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 49: 1st Increasing cache bandwidth: Pipelined Caches
Hit in multiple cycles,
giving fast clock cycle time
What problems for instruction pipeline ?

## Slide 50: 2nd Increasing cache bandwidth: Nonblocking Caches
A nonblocking(Lockup-free cache) cache,allows The cache to continues to supply hits while processing read misses ( hit under miss , hit under multiple miss ).
Complex caches can even have multiple outstanding misses ( miss under miss ). It will further lower effective miss penalty
Nonblocking, in conjunction with out-of-order execution, can allow the CPU to continue executing instructions after a data cache miss.
What’s the precondition ?

## Slide 51: Performance of Nonblocking cache

## Slide 52: 3nd Increasing cache bandwidth: Multibanked Caches
Cache is divided into independent banks that can support simultaneous accesses like interleaved memory banks.
  E.g.,T1 (“Niagara”) L2 has 4 banks
Banking works best when accesses naturally spread themselves across banks  mapping of addresses to banks affects behavior of memory system
Simple mapping that works well is “sequential interleaving”

## Slide 53
Single banked two bank two bank two bank
consecutive interleaving group interleaving

## Slide 54: Summary: Increase Cache Bandwidth
  1. Increase bandwidth via pipelined cache access
  2. Increase bandwidth via multibanked caches,
  3. Increase bandwidth via non-blocking caches,

## Slide 55: How to Improve Cache Performance?
1. Reduce the time to hit in the cache.--4
——small and simple caches, avoiding address translation, way prediction , and trace caches
2. Increase cache bandwidth .--3
—— pipelined cache access, multibanked caches, non-blocking caches,
3. Reduce the miss penalty--4
——multilevel caches, critical word first, read miss prior to writes, merging write buffers, and victim caches
4. Reduce the miss rate--4
——larger block size, large cache size, higher associativity,and compiler optimizations
5. Reduce the miss penalty and miss rate via parallelism--2
——hardware prefetching, compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 56: 1st Miss Penalty Reduction Technique: Multilevel Caches
This method focuses on the interface between the cache and main memory.
Add an second-level cache between main memory and a small, fast first-level cache, to make the cache fast and large.
The smaller first-level cache is fast enough to match the clock cycle time of the fast CPU and to fit on the chip with the CPU, thereby lessening the hits time.
The second-level cache can be large enough to capture many memory accesses that would go to main memory, thereby lessening the effective miss penalty.

## Slide 57: Parameter about Multilevel cache
The performance of a two-level cache is calculated in a similar way to the performance for a single level cache.
L2 Equations
AMAT = Hit TimeL1 + Miss RateL1 x Miss PenaltyL1
Miss PenaltyL1 = Hit TimeL2 + Miss RateL2 x Miss PenaltyL2
AMAT = Hit TimeL1 +
Miss RateL1 x (Hit TimeL2 + Miss RateL2 * Miss PenaltyL2)
So the miss penalty for level 1 is calculated using the hit time, miss rate, and miss penalty for the level 2 cache.

## Slide 58: Two conceptions for two-level cache
Definitions:
  Local miss rate— misses in this cache divided by the total number of memory accesses to this cache (Miss rateL2)
  Global miss rate—misses in this cache divided by the total number of memory accesses generated by the CPU
Using the terms above, the global miss for the first-level cache is stall just Miss rateL1, but for the second-level cache it is :

## Slide 59: 2nd Miss Penalty Reduction Technique: Critical Word First and Early Restart
Don’t wait for full block to be loaded before restarting CPU
  Critical Word First—Request the missed word first from memory and send it to the CPU as soon as it arrives; let the CPU continue execution while filling the rest of the words in the block. Also called wrapped fetch and requested word first
  Early restart—As soon as the requested word of the block arrives, send it to the CPU and let the CPU continue execution
Generally useful only in large blocks,
Spatial locality => tend to want next sequential word, so not clear if benefit by early restart

## Slide 60: Example: Critical Word First
Assume:
cache block＝64-byte
L2: take 11 CLK to get the critical 8 bytes,(AMD Athlon)
and then 2 CLK per 8 byte to fetch the rest of the
block
There will be no other accesses to rest of the block
Calculate the average miss penalty for critical word first.
Then assuming the following instructions read data sequentially 8 bytes at a time from the rest of the block
Compare the times with and without critical word first.

## Slide 61: 3rd Miss Penalty Reduction Technique: Giving Priority to Read Misses over Writes
If a system has a write buffer, writes can be delayed to come after reads.
The system must, however, be careful to check the write buffer to see if the value being read is about to be written.

## Slide 62: Write buffer
Write-back want buffer to hold displaced blocks
  Read miss replacing dirty block
  Normal: Write dirty block to memory, and then do the read
  Instead copy the dirty block to a write buffer, then do the read, and then do the write
  CPU stall less since restarts as soon as do read
Write-through want write buffers => RAW conflicts with main memory reads on cache misses
  If simply wait for write buffer to empty, might increase read miss penalty (old MIPS 1000 by 50% )
  Check write buffer contents before read; if no conflicts, let the memory access continue

## Slide 63: 4th Miss Penalty Reduction Technique: Merging write Buffer
One word writes replaces with multiword writes, and it improves buffers’s efficiency.
In write-through ,When write misses if the buffer contains other modified blocks,the addresses can be checked to see if the address of this new data matches the address of a valid write buffer entry.If so,the new data are combined with that entry.
The optimization also reduces stalls due to the write buffer being full.

## Slide 64: Write merging

## Slide 65: Miss Penalty Reduction Technique: Victim Caches
A victim cache is a small (usually, but not necessarily) fully-associative cache that holds a few of the most recently replaced blocks or victims from the main cache.
This cache is checked on a miss data before going to next lower-level memory(main memory).
  to see if they have the desired item
  If found, the victim block and the cache block are swapped.
  The AMD Athlon has a victim caches (write buffer for write back blocks ) with 8 entries.

## Slide 66: The Victim Cache

## Slide 67: How to combine victim Cache ?
How to combine fast hit time of direct mapped yet still avoid conflict misses?
Add buffer to place data discarded from cache
Jouppi [1990]: 4-entry victim cache removed 20% to 95% of conflicts for a 4 KB direct mapped data cache
Used in Alpha, HP machines
To Next Lower Level In
Hierarchy
DATA
TAGS
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator

## Slide 68: Summary: Miss Penalty Reduction
  1. Reduce penalty via Multilevel Caches
  2. Reduce penalty via Critical Word First
  3. Reduce penalty via Read Misses over Writes
  4. Reducing penalty via Merging write Buffer

## Slide 70: How to Improve Cache Performance?
1. Reduce the time to hit in the cache.--4
——small and simple caches, avoiding address translation, way prediction , and trace caches
2. Increase cache bandwidth .--3
—— pipelined cache access, multibanked caches, non-blocking caches,
3. Reduce the miss penalty--4
——multilevel caches, critical word first, read miss prior to writes, merging write buffers, and victim caches
4. Reduce the miss rate--4
——larger block size, large cache size, higher associativity,and compiler optimizations
5. Reduce the miss penalty and miss rate via parallelism--2
——hardware prefetching,and compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 71: Where misses come from?
Classifying Misses: 3 Cs
  Compulsory—The first access to a block is not in the cache, so the block must be brought into the cache. Also called cold start misses or first reference misses. (Misses in even an Infinite Cache)
  Capacity—If the cache cannot contain all the blocks needed during execution of a program, capacity misses will occur due to blocks being discarded and later retrieved. (Misses in Fully Associative Size X Cache)
  Conflict—If block-placement strategy is set associative or direct mapped, conflict misses (in addition to compulsory & capacity misses) will occur because a block can be discarded and later retrieved if too many blocks map to its set. Also called collision misses or interference misses. (Misses in N-way Associative, Size X Cache)
4th “C”:
  Coherence - Misses caused by cache coherence.
Notes: Intuitive Model by Mark Hill

## Slide 72: 3Cs Absolute Miss Rate (SPEC92)

## Slide 73: 3Cs Relative Miss Rate
Flaws: for fixed block size
Good: insight => invention

## Slide 74: Reducing Cache Miss Rate
To reduce cache miss rate, we have to eliminate some of the misses due to the three C's.
We cannot reduce capacity misses much except by making the cache larger.
We can, however, reduce the conflict misses and compulsory misses in several ways:

## Slide 75: Cache Organization?
Assume total cache size not changed:
What happens if:
Change Block Size:
Change Associativity:
3) Change Compiler:
Which of 3Cs is obviously affected?
Notes: Ask which affected?
Block size
1) Compulsory
2) More subtle, will change mapping

## Slide 76: 1st Miss Rate Reduction Technique: Larger Block Size (fixed size&assoc)
Larger blocks decrease the compulsory miss rate by taking advantage of spatial locality.
Drawback--curve is U-shaped
  However, they may increase the miss penalty by requiring more data to be fetched per miss.
  In addition, they will almost certainly increase conflict misses since fewer blocks can be stored in the cache.
  And maybe even capacity misses in small caches
Trade-off
  Trying to minimize both the miss rate and the miss penalty.
  The selection of block size depends on both the latency and bandwidth of lower-level memory

## Slide 77: Miss Rate relates Block size
Block size | Cache size |  |  | 
 | 4K | 16K | 64K | 256K
16 | 8.57% | 3.94% | 2.04% | 1.09%
32 | 7.24% | 2.87% | 1.35% | 0.70%
64 | 7.00% | 2.64% | 1.06% | 0.51%
128 | 7.78% | 2.77% | 1.02% | 0.49%
256 | 9.51% | 3.29% | 1.15% | 0.49%

## Slide 78: Performance curve is U-shaped
Reduced
compulsory
misses
Increased
Conflict
Misses
What else drives up block size?

## Slide 79: Example: Larger Block Size (C-26)
Assume: memory takes 80 clock cycles of overhead and then delivers 16 bytes every 2 cycles.
1 clock cycle hit time independent of block size.
Which block size has the smallest AMAT for each size in Fig.5.17 ?
Answer:
  AMAT16-byte block, 4KB = 1+(8.57%*82)=8.027
  AMAT256-byte block, 256KB= 1+(0.49%*112)=1.549

## Slide 80: 2nd Miss Rate Reduction Technique: Larger Caches
rule of thumb: 2 x size => 25% cut in miss rate
What does it reduce ?
Cache Size

## Slide 81: Pro. Vs. cons for large caches
Pro.
  Reduce capacity misses
Con.
  Longer hit time, Higher cost, AMAT curve is U-shaped
Popular in off-chip caches
Block size | Miss penalty | Cache size |  |  | 
 |  | 4K | 16K | 64K | 256K
16 | 82 | 8.027 | 4.231 | 2.673 | 1.894
32 | 84 | 7.082 | 3.411 | 2.134 | 1.588
64 | 88 | 7.160 | 3.323 | 1.933 | 1.449
128 | 96 | 8.469 | 3.659 | 1.979 | 1.470
256 | 112 | 11.651 | 4.685 | 2.288 | 1.549

## Slide 82: 3rd Miss Rate Reduction Technique: Higher Associativity
Conflict misses can be a problem for caches with low associativity (especially direct-mapped).
With higher associativity decreasing Conflict misses to improve miss rate
cache rule of thumb
2:1 rule of thumb a direct-mapped cache of size N has the same miss rate as a 2-way set-associative cache of size N/2.
Eight-way set associative is for practical purposes as effective in reducing misses for these sized cache as fully associative.

## Slide 83: Associativity
Conflict
2:1 rule of thumb

## Slide 84: Associativity vs Cycle Time
Beware: Execution time is only final measure!
Why is cycle time tied to hit time?
Will Clock Cycle time increase?
  Hill [1988] suggested hit time for 2-way vs. 1-way external cache +10%, internal + 2%
  suggested big and dumb caches

## Slide 85: Avg. Memory Access Time vs. Miss Rate (P430)
Example: assume CCT = 1.36 for 2-way, 1.44 for 4-way, 1.52 for 8-way vs. CCT direct mapped
Cache Size Associativity
(KB) 1-way 2-way 4-way 8-way
4 3.44 3.25 3.22 3.28
8 2.69 2.58 2.55 2.62
16 2.33 2.40 2.46 2.53
32 2.06 2.30 2.37 2.45
64 1.92 2.24 2.18 2.25
128 1.52 1.84 1.92 2.00
256 1.32 1.66 1.74 1.82
512 1.20 1.55 1.59 1.66
(Red means A.M.A.T. not improved by more associativity)

## Slide 86: 4th Miss Rate Reduction Technique: Way Prediction and Pseudo-Associative Cache
Using two Technique reduces conflict misses and yet maintains hit speed of direct-mapped cache
  Predictive bit - Pseudo-Associative
Way Prediction (Alpha 21264 )
  Extra bits are kept in the cache to predict the way,or block within set of the next cache access.
  If the predictor is correct, the instruction cache latency is 1 clock clock cycle.
  If not,it tries the other block, changes the way predictor, and has a latency of 3 clock cycles.
  Simulation using SPEC95 suggested set prediction accuracy is excess of 85%, so way prediction saves pipeline stage in more than 85% of the instruction fetches.

## Slide 87: Pseudo-Associative Cache (column associative)
How to combine fast hit time of Direct Mapped and have the lower conflict misses of 2-way SA cache?
Divide cache: on a miss, check other half of cache to see if there, if so have a pseudo-hit (slow hit)
Drawback: CPU pipeline is hard if hit takes 1 or 2 cycles
  Better for caches not tied directly to processor (L2)
  Used in MIPS R1000 L2 cache, similar in UltraSPARC
Time
Hit Time
Pseudo Hit Time
Miss Penalty

## Slide 88: Pseudo-Associative Cache

## Slide 89: 4th Miss Rate Reduction Technique: Compiler Optimizations
The techniques reduces miss rates without any hardware changes and reorders instruction sequence with compiler.
Instructions
  Reorder procedures in memory so as to reduce conflict misses
  Profiling to look at conflicts(using tools they developed)
Data
  Merging Arrays: improve spatial locality by single array of compound elements vs. 2 arrays
  Loop Interchange: change nesting of loops to access data in order stored in memory
  Loop Fusion: Combine 2 independent loops that have same looping and some variables overlap
  Blocking: Improve temporal locality by accessing “blocks” of data repeatedly vs. going down whole columns or rows

## Slide 90: Merging Arrays
Combining independent matrices into a single compound array.
Improving spatial locality
Example
  /*before*/
  Int val[SIZE];
  Int key[SIZE];
  /*after*/
  Struct merge{
  int val;
  int key;
  }
  Struct merge merged_array[SIZE]

## Slide 91: b. Loop Interchange
/* Before */
for (k = 0; k < 100; k = k+1)
for (j = 0; j < 100; j = j+1)
for (i = 0; i < 5000; i = i+1)
x[i][j] = 2 * x[i][j];
/* After */
for (k = 0; k < 100; k = k+1)
for (i = 0; i < 5000; i = i+1)
for (j = 0; j < 100; j = j+1)
x[i][j] = 2 * x[i][j];
Sequential accesses instead of striding through memory every 100 words;
By switching the order in which loops execute, misses can be reduced due to improvements in spatial locality.

## Slide 92: c. Loop fusion
By fusion the code into a single loop, the data that are fetched into the cache can be used repeatedly before being swapped out.
Imporving the temporal locality
Example:
/*before*/ /*after*/
For (i=0; i<N; i=i+1) For (i=0; i<N; i=i+1)
For (i=0; j<N; j=i+1) For (j=0; j<N; j=i+1)
a[i][j]=1/b[i][j]*c[i][j]; {
For (i=0; i<N; i=i+1)
a[i][j]=1/b[i][j]*c[i][j];
For (j=0; j<N; j=j+1) d[i][j]=a[i][j]*c[i][j];
d[i][j]=a[i][j]*c[i][j]; }

## Slide 93: d. Unoptimized Matrix Multiplication
/* Before */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
{r = 0;
for (k = 0; k < N; k = k+1)
r = r + y[i][k]*z[k][j];
x[i][j] = r;
};
Two Inner Loops:
  Write N elements of 1 row of X[ ]
  Read N elements of 1 row of Y[ ] repeatedly
  Read all NxN elements of Z[ ]
Capacity Misses a function of N & Cache Size:
  2N3 + N2 => (assuming no conflict; otherwise …)
Idea: compute on BxB submatrix that fits
y[1][k]
z[k][j]
x[1][j]
((N+N)N+N)N=2N3 + N2
Accessed For N3 operations

## Slide 94: Blocking optimized Matrix Multiplication
Matrix multiplication is
performed by multiplying the
submatrices first.
/* After */
for (jj = 0; jj < N; jj = jj+B)
for (kk = 0; kk < N; kk = kk+B)
for (i = 0; i < N; i = i+1)
for (j = jj; j < min(jj+B-1,N); j = j+1)
{r = 0;
for (k = kk; k < min(kk+B-1,N); k = k+1)
r = r + y[i][k]*z[k][j];
x[i][j] = x[i][j] + r;
};
Y benefits from spatial locality
Z benefits from temporal locality
Capacity Misses from 2N3 + N2 to N3/B+2N2
BN
B×B
BN
(BN+BN)+B2)×(N/B)2=2N3/B + N2
Accessed For N3 operations
B called Blocking Factor

## Slide 95: Reducing Conflict Misses by Blocking
Conflict misses in caches not FA vs. Blocking size
  Lam et al [1991] a blocking factor of 24 had a fifth the misses vs. 48 despite both fit in cache

## Slide 96: Summary of Compiler Optimizations to Reduce Cache Misses (by hand)

## Slide 97: Summary: Miss Rate Reduction
3 Cs: Compulsory, Capacity, Conflict
  1. Larger cache
  2. Reduce Misses via Larger Block Size
  3. Reduce Misses via Higher Associativity
  4. Reducing Misses by Compiler Optimizations
  5. Pseudo associative cache

## Slide 98: How to Improve Cache Performance?
1. Reduce the time to hit in the cache.--4
——small and simple caches, avoiding address translation, way prediction , and trace caches
2. Increase cache bandwidth .--3
—— pipelined cache access, multibanked caches, non-blocking caches,
3. Reduce the miss penalty--4
——multilevel caches, critical word first, read miss prior to writes, merging write buffers, and victim caches
4. Reduce the miss rate--4
——larger block size, large cache size, higher associativity,and compiler optimizations
5. Reduce the miss penalty and miss rate via parallelism--2
——hardware prefetching,and compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 99: 1st Miss Penalty/Rate Reduction Technique: Hardware Prefetching of Inst.and data
The act of getting data from memory before it is actually needed by the CPU.
This reduces compulsory misses by retrieving the data before it is requested.
Of course, this may increase other misses by removing useful blocks from the cache.
  Thus, many caches hold prefetched blocks in a special buffer until they are actually needed.
E.g., Instruction Prefetching
  Alpha 21064 fetches 2 blocks on a miss
  Extra block placed in “stream buffer”
  On miss check stream buffer
Prefetching relies on having extra memory bandwidth that can be used without penalty

## Slide 100: 2nd Miss Penalty/Rate Reduction Technique: Compiler-controlled prefetch
The compiler inserts prefetch instructions to request the data before they are needed
Data Prefetch Load data into register (HP PA-RISC loads)
  Cache Prefetch: load into cache (MIPS IV, PowerPC, SPARC v. 9)
  Special prefetching instructions cannot cause faults; a form of speculative execution
Prefetching comes in two flavors:
  Binding prefetch: Requests load directly into register.
    Must be correct address and register!
  Non-Binding prefetch: Load into cache.
    Can be incorrect. Faults?
Issuing Prefetch Instructions takes time
  Is cost of prefetch issues < savings in reduced misses?
  Higher superscalar reduces difficulty of issue bandwidth

## Slide 101: Example (P307): Compiler-controlled prefetch
for( i=0; i <3; i = i +1)
for( j=0; j<100; j=j+1)
a[i][j] = b[j][0] * b[j+1][0];
16B/block， 8B/element， 2elements/block
A[i][j]: 3*100 the even value of j will miss,
the odd values will hit, total 150 misses
B[i][j]：101*3 the same elements are accessed for each iteration of i
j=0 B[0][0]、B[1][0] 2
j=1 B[1][0]、B[2][0] 1
total 2+99=101 misses

## Slide 102: Example cont.: Compiler-controlled prefetch
For (j=0; j<100; j=j+1){
Prefetch(b[j+7][0]);
prefetch(a[0][j+7]);
a[0][j]=b[j][0]*b [j+1][0];}; 7 misses for b
4 misses for a
For (I=1; I<3; I=I+1)
For (j=0; j<100; j=j+1){
prefetch(a[i][j+7]);
a[i][j]=b[j][0]*b [j+1][0];};4 misses for a[1][j]
4 misses for a[2][j]
Total: 19 misses
save 232 cache misses at the price of 400 prefetch instructions.

## Slide 103
End.