## Slide 1: Ch3-1 ILP: Dynamic Scheduling
ILP Concept
Dynamic scheduling

## Slide 2: Chapter 3
ILP: Concepts and Challenge
Basic compiler Techniques for exposing ILP
Overcoming Data Hazards with Dynamic Scheduling
Reducing Branch Costs with Dynamic Hardwre Prediction
HP instruction Delivery & Multiple Issue
Hardware-based Speculation
Thread-level Parallelism
Notes: 数据冲突、分支预测、投机执行、线程级并行

## Slide 3: Recall from Pipelining Review
Pipeline CPI = Ideal pipeline CPI + Structural Stalls + Data Hazard Stalls + Control Stalls
  Ideal pipeline CPI: measure of the maximum performance attainable by the implementation
  Structural hazards: HW cannot support this combination of instructions
  Data hazards: Instruction depends on result of prior instruction still in the pipeline
  Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps)

## Slide 4: Ideas to Reduce Stalls
Ch3
ChG
ChC

## Slide 5: What is Instruction-Level Parallelism ?
Instruction-level parallelism
  The potential overlap among instructions
Basic Block ILP is quite small
  Basic Block: a straight-line code sequence with no branches in except to the entry and no branches out except at the exit
  average dynamic branch frequency 15% to 25% => 4 to 7 instructions execute between a pair of branches
  Plus instructions in BB likely to depend on each other
Notes: Pipeline优化针对于basic block，而basic block大小只有4到7个指令，并且bb内指令间都有依赖，很难用pipeline优化

## Slide 6: Instruction-Level Parallelism (ILP)
To obtain substantial performance enhancements, we must exploit ILP across multiple basic blocks
Simplest: loop-level parallelism to exploit parallelism among iterations of a loop
  Vector is one way
  If not vector, then either dynamic via branch prediction or static via loop unrolling by compiler

## Slide 7: Recall: Types of data hazards
Consider two instructions, A and B. A occurs before B.
RAW( Read after write) true dependence
  Instruction A writes Rx，instruction B reads Rx
WAW(Write after write) output dependence
  Instruction A writes Rx，instruction B writes Rx
WAR( Write after read) anti-denpendence
  Instruction A reads Rx，instruction B writes Rx
Hazards are named according to the ordering that MUST be preserved by the pipeline
Notes: 区分dependence和hazards

## Slide 8: True Data Dependence and Hazards
True Data Dependence:
  InstrJ is data dependent on InstrI InstrJ tries to read operand before InstrI writes it
  or InstrJ is data dependent on InstrK which is dependent on InstrI
Caused by a “True Dependence” (compiler term)
If true dependence caused a hazard in the pipeline, called a Read After Write (RAW) hazard
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 9: True Data Dependence and Hazards
Dependences are a property of programs
Presence of dependence indicates potential for a hazard, but actual hazard and length of any stall is a property of the pipeline
Importance of the data dependencies
  indicates the possibility of a hazard
  determines order in which results must be calculated
  sets an upper bound on how much parallelism can possibly be exploited
Notes: 两种解决思路，一种硬件一种软件

## Slide 10: Name Dependence 1:Anti-dependence
Name dependence: when 2 instructions use same register or memory location, called a name, but no flow of data between the instructions associated with that name;
InstrJ writes operand before InstrI reads it called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”
If anti-dependence caused a hazard in the pipeline, called a Write After Read (WAR) hazard
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 11: Name Dependence 2: Output dependence
InstrJ writes operand before InstrI writes it.
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”
If anti-dependence caused a hazard in the pipeline, called a Write After Write (WAW) hazard
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 12: ILP and Data Hazards
HW/SW must preserve program order: order instructions would execute in if executed sequentially 1 at a time as determined by original source program
HW/SW goal: exploit parallelism by preserving program order only where it affects the outcome of the program
Instructions involved in a name dependence can execute simultaneously if name used in instructions is changed so instructions do not conflict
  Register renaming resolves name dependence for regs
  Either by compiler or by HW

## Slide 13: Control Dependencies
Every instruction is control dependent on some set of branches, and, in general, these control dependencies must be preserved to preserve program order
  if p1 {
  S1;
  };
  if p2 {
  S2;
  }
S1 is control dependent on p1, and S2 is control dependent on p2 but not on p1.

## Slide 14: Control Dependence Ignored
Control dependence need not be preserved
  willing to execute instructions that should not have been executed, thereby violating the control dependences, if can do so without affecting correctness of the program
Instead, 2 properties critical to program correctness are exception behavior and data flow

## Slide 15: Exception Behavior
Preserving exception behavior
=> any changes in instruction execution order must not change how exceptions are raised in program
(=> no new exceptions)
  Example: DADDU R2,R3,R4 BEQZ R2,L1 LW R1,0(R2) L1: ……
Problem with moving LW before BEQZ?

## Slide 16: Data Flow
Data flow: actual flow of data values among instructions that produce results and those that consume them
  branches make flow dynamic, determine which instruction is supplier of data
Example:
  DADDU R1,R2,R3 BEQZ R4,L DSUBU R1,R5,R6 L: … OR R7,R1,R8
OR depends on DADDU or DSUBU? Must preserve data flow on execution

## Slide 17: A short summary
ILP
  The potential overlap among instructions
Reduce stalls from
  Structural hazards
  Data hazards
  Control hazards
To keep the program correctness, we should
  Preserving Data flow
  Preserving exception behavior

## Slide 18: Lecture for ILP: Software approaches
Basic Compiler Technique for Exposing ILP
  Loop unrolling
Static Branch Prediction
Static multiple Issue: VLIW
Advanced Compilor Support for Exposing and Exploiting ILP
  Software pipelining
  Global Code scheduling
Hardware Support for Exposing More Parallelism at compile time
  Conditional or Predicated instructions
  Compiler speculation with hardware support

## Slide 19: FP Loop: Where are the Hazards?
Loop: LD F0,0(R1) ;F0=vector element
ADDD F4,F0,F2 ;add scalar from F2
SD 0(R1),F4 ;store result
SUBI R1,R1,8 ;decrement pointer 8B (DW)
BNEZ R1,Loop ;branch R1!=zero
NOP ;delayed branch slot
Instruction Instruction Execution Latency producing result using result in cycles in cycles
FP ALU op Another FP ALU op 4 3
FP ALU op Store double 4 2
Load double FP ALU op 1 1
Load double Store double 1 0
Integer op Integer op 1 0
Where are the stalls?
Notes: 首先通过编译器指令调度解决问题，最基本的流水线，只是增加了FP指令

## Slide 20: Specification for the latency
ALU F1, -,- : IF ID FD FD FD FD WB
ALU -, F1,-: IF ID s s s FD FD FD FD WB
ALU: IF ID FD FD FD FD WB
SW: IF ID s s EX DM
LW F1, - : IF ID EX DM WB
SW: F1, 8(R1): IF ID EX DM WB
MEM/WB.LDMR --DM input port

## Slide 21: Reducing stalls from scheduling in BB and delayed branch
Loop: LD F0, 0(R1)
ADDD F4, F0, F2
SD 0(R1), F4
SUBI R1, R1, #8
BNEZ R1, Loop
F D X M W
F D s A1 A2 A3 A4 W
F s D s s X M W
F s s D X M W
F s D X M W
10 CC DS F
Loop: LD F0, 0(R1)
SUBI R1, R1,#8
ADDD F4, F0, F2
BNEZ R1, Loop
SD +8(R1), F4
F D X M W
F D X M W
F DA1A2A3A4W
F D X M W
F D s X M W
6 CC F s D X M W
第二次循环体开始
分支指令停顿一个周期，用于delay slot

## Slide 22: Unroll Loop Four Times (straightforward way)
Rewrite loop to minimize stalls?
1 Loop: LD F0,0(R1)
2 ADDD F4,F0,F2
3 SD 0(R1),F4 ;drop SUBI & BNEZ
4 LD F6,-8(R1)
5 ADDD F8,F6,F2
6 SD -8(R1),F8 ;drop SUBI & BNEZ
7 LD F10,-16(R1)
8 ADDD F12,F10,F2
9 SD -16(R1),F12
10 LD F14,-24(R1)
11 ADDD F16,F14,F2
12 SUBI R1,R1,#32 ;alter to 4*8
13 SD +8(R1),F16
14 BNEZ R1,LOOP
NOP
14 + 3 x (1+2) +1 +1 +1= 26 clock cycles, or 6.5 per iteration
Assumes R1 is multiple of 4
1 cycle stall
2 cycles stall
1 cycle stall
1 cycle stall(waiting for F16
1 cycle control stall

## Slide 23: Unrolled Loop That Minimizes Stalls
What assumptions made when moved code?
  OK to move store past SUBI even though changes register
  OK to move loads before stores: get right data?
  When is it safe for compiler to do such changes?
1 Loop: LD F0,0(R1)
2 LD F6,-8(R1)
3 LD F10,-16(R1)
4 LD F14,-24(R1)
5 ADDD F4,F0,F2
6 ADDD F8,F6,F2
7 ADDD F12,F10,F2
8 ADDD F16,F14,F2
9 SD 0(R1),F4
10 SD -8(R1),F8
11 SUBI R1,R1,#32
12 SD +16(R1),F12
13 BNEZ R1,LOOP
14 SD 8(R1),F16 8-32 = -24
14 clock cycles, or 3.5 per iteration

## Slide 24: Ideas to Reduce Stalls
Ch3
ChG
ChC

## Slide 25: Why Dynamic Scheduling ?
Example1 :
  DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F12,F8,F14
Example2: Structure Hazard
    DIVD F2,F2,F4
    ADDD F10,F0,F8 ; FP ADDer unpipelined
    ADDD F12, F0,F4
    MULD F16, F14, F4
Problem: instruction (SUBD, MULD) stalled
due to irrelevent forward instructions.
Notes: 动态调度，动态调度和

## Slide 26: HW Schemes: Dynamic scheduling
Key idea: Allow instructions behind stall to proceed
Enables out-of-order execution and allows out-of-order completion
Will distinguish when an instruction begins execution and when it completes execution; between 2 times, the instruction is in execution
In a dynamically scheduled pipeline, all instructions pass through issue stage in order (in-order issue)

## Slide 27: Adv. Of Dynamic Scheduling
Handles cases when dependences unknown at compile time
  (e.g., because they may involve a memory reference)
It simplifies the compiler
Allows code that compiled for one pipeline to run efficiently on a different pipeline
Hardware speculation, a technique with significant performance advantages, that builds on dynamic scheduling

## Slide 28: Dynamic Scheduling Step 1
Simple pipeline had 1 stage to check both structural and data hazards: Instruction Decode (ID), also called Instruction Issue
Split the ID pipe stage of simple 5-stage pipeline into 2 stages:
Issue—Decode instructions, check for structural hazards
Read operands—Wait until no data hazards, then read operands

## Slide 29: Dynamic Scheduling with a Scoreboard
Scoreboarding
  Named after CDC6600 scoreboard
  Allowing instructions to execute out of order when there are sufficient resources and no data dependences.
  In-order issue
  Out-of order completion
  Executing an instruction as early as possible

## Slide 30: Basic structure of a pipelined processor with a scoreboard

## Slide 31: CDC6600 –First Supercomputer top1 1964-1969

## Slide 32: The pipeline stages with scoreboard
The Five stages: IF, ID, EX, MEM, WB
  IF: the same for all instructions
  ID: split into two stages: issue and read operands
  EX: no change
  MEM: omitted for only concentrating on the FP operations
  WB: no change
So, the stages are: IF, IS, RO, EX,WB.
Another way to lookat missing MEM ?

## Slide 33: Pipeline supports multiple outstanding FP operations
IF
ID
M1
M2
M3
M4
M5
M6
M7
A1
A2
A3
A4
WB
EX
MEM
DIV

## Slide 34: Scoreboard Pipeline stage description
Issue: a instruction is issued when
  The functional unit is available and
  No other active instruction has the same destination register.
  Avoid strutural hazard and WAW hazard
Read Operands (RO)
  The read operation is delayed until both the operands are available.
  This means that no previously issued but ncompleted instruction has the operand as its destination.
  This resolves RAW hazards dynamically
Execution (EX)
  Notify the scoreboard when completed so the functional unit can be reused.
Write result (WB)
  The scoreboard checks for WAR hazards and stalls the completing instruction if necessary.

## Slide 35: The scoreboard algorithm
Scoreboard-takes full responsibility for instruction issue and execution
  Create the dependence records
  Decide when to fetch the operand
  Decide when to enter execution
  Decide when the result can be written into the register file
Three data structure
  Instruction status:
    which of the four steps the instruction is in
  Functional unit status: buzy,op,Fi, Fj,Fk,Qj,Qk ,Rj,Rk
  Register result status:
    which functional unit will write that register

## Slide 36: Example: Instruction status
LD F6, 34(R2)
LD F2, 45(R3)
MULTD F0, F2, F4
SUBD F8, F6, F2
DIVD F10, F0, F6
ADDD F6, F8, F2

## Slide 37: Example: Function unit status and Register status

## Slide 38: Scoreboard Example
Clock cycle counter
Instruction stream
Busy：用于描述功能部件硬件资源的占用情况 Op：说明运行时所用的是哪一个功能部件 Fi：目标寄存器 Fj, Fk：源操作数或寄存器 Qj, Qk：是否有某个功能单元占用源寄存器Fj或Fk。 Rj, Rk：用于标识源寄存器是否准备好。

## Slide 39: Scoreboard Cycle 1
Clock cycle counter
Instruction stream

## Slide 40: Scoreboard Cycle 2
Clock cycle counter
Instruction stream

## Slide 41: Scoreboard Cycle 3
Clock cycle counter
Instruction stream

## Slide 42: Scoreboard Cycle 4
Clock cycle counter
Instruction stream

## Slide 43: Scoreboard Cycle 5
Clock cycle counter
Instruction stream

## Slide 44: Scoreboard Cycle 6
Clock cycle counter
Instruction stream

## Slide 45: Scoreboard Cycle 7
Clock cycle counter
Instruction stream

## Slide 46: Scoreboard Cycle 8
Clock cycle counter
Instruction stream

## Slide 47: Scoreboard Cycle 9
Clock cycle counter
Instruction stream

## Slide 48: Scoreboard Cycle 10
Clock cycle counter
Instruction stream

## Slide 49: Scoreboard Cycle 11
Clock cycle counter
Instruction stream

## Slide 50: Scoreboard Cycle 12
Clock cycle counter
Instruction stream

## Slide 51: Scoreboard Cycle 15
Clock cycle counter
Instruction stream

## Slide 52: Scoreboard Cycle 16
Instruction stream

## Slide 53: Scoreboard Cycle 17
Instruction stream

## Slide 54: Scoreboard Cycle 18
Instruction stream

## Slide 55: Scoreboard Cycle 19
Instruction stream

## Slide 56: Limitations of Scoreboard-1
ILP
  If we can't find independent instructions to execute, scoreboard (or any dynamic scheduling scheme for that matter) helps very little.
Size of the "issued" queue
  This determines how far ahead the CPU can look for instructions to execute in parallel.
  It's called the window.
  For now, we assume that a window can not span a branch.
  In other words, the window includes instructions only within basic blocks.

## Slide 57: Limitations of Scoreboard-2
Number, types, and speed of the functional units
  This determines how often a structural hazard results in stall.
The presence of anti-dependences and output dependences
  WAR and WAW hazards limit the scoreboard more than RAW hazards, lead to WAR and WAW stalls.
  RAW hazards are problems for any technique.
  But WAR and WAW hazards can be solved in ways other than scoreboards.

## Slide 58: Dynamic Scheduling with Tomasulo’s Algorithm
For IBM 360/91 (before caches!)
Goal: High Performance without special compilers
Small number of floating point registers (4 in 360) prevented interesting compiler scheduling of operations
  This led Tomasulo to try to figure out how to get more effective registers — renaming in hardware!
Why Study 1966 Computer?
The descendants of this have flourished!
  Alpha 21264, HP 8000, MIPS 10000, Pentium III, PowerPC 604, …

## Slide 59: Tomasulo Algorithm
Control & buffers distributed with Function Units (FU)
  FU buffers called “reservation stations”; have pending operands
Registers in instructions replaced by values or pointers to reservation stations(RS); called register renaming ;
  avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations compilers can’t
Results to FU from RS, not through registers, over Common Data Bus that broadcasts results to all FUs
Load and Stores treated as FUs with RSs as well
Integer instructions can go past branches, allowing FP ops beyond basic block in FP queue

## Slide 60: Tomasulo Organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
From Intruction unit
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 61: Reservation Station Components
Reservation station:
Op: Operation to perform in the unit
Vj, Vk: Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: Qj,Qk=0 => ready
  Store buffers only have Qi for RS producing result
A: hold info. for memory address calculation
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 62: Three Stages of Tomasulo Algorithm
Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
Execute—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available

## Slide 63: Data path
Normal data bus: data + destination (“go to” bus) 点对点
Common data bus: data + source (“come from” bus) 广播
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast
Example speed: 3 clocks for Fl .pt. +,-; 10 for * ; 40 clks for /

## Slide 64: 状态切换规则表

## Slide 65: Tomasulo Example
Clock cycle counter
FU count
down
Instruction stream
3 Load/Buffers
3 FP Adder R.S.
2 FP Mult R.S.
LD/ST专门保留站

## Slide 66: Tomasulo Example Cycle 1

## Slide 67: Tomasulo Example Cycle 2
Note: Can have multiple loads outstanding

## Slide 68: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations; MULT issued
Load1 completing; what is waiting for Load1?

## Slide 69: Tomasulo Example Cycle 4
Load2 completing; what is waiting for Load2?

## Slide 70: Tomasulo Example Cycle 5
Timer starts down for Add1, Mult1

## Slide 71: Tomasulo Example Cycle 6
Issue ADDD here despite name dependency on F6?

## Slide 72: Tomasulo Example Cycle 7

## Slide 73: Tomasulo Example Cycle 8
Add1 (SUBD) completing; what is waiting for it?

## Slide 74: Tomasulo Example Cycle 9

## Slide 75: Tomasulo Example Cycle 10

## Slide 76: Tomasulo Example Cycle 11

## Slide 77: Tomasulo Example Cycle 12
Add2 (ADDD) completing; what is waiting for it?

## Slide 78: Tomasulo Example Cycle 13
All simple operation are end here.

## Slide 79: Tomasulo Example Cycle 14

## Slide 80: Tomasulo Example Cycle 15
Mult1 (MULTD) completing; what is waiting for it?

## Slide 81: Tomasulo Example Cycle 16
Just waiting for Mult2 (DIVD) to complete

## Slide 82: Tomasulo Example Cycle 17

## Slide 83: Tomasulo Example Cycle 55

## Slide 84: Tomasulo Example Cycle 56
Mult2 (DIVD) is completing; what is waiting for it?

## Slide 85: Tomasulo Example Cycle 57
Once again: In-order issue, out-of-order execution and out-of-order completion.

## Slide 86: Tomasulo’s scheme offers 2 major advantages
The distribution of the hazard detection logic
  distributed reservation stations and the CDB
  If multiple instructions waiting on single result, & each instruction has other operand, then instructions can be released simultaneously by broadcast on CDB
  If a centralized register file were used, the units would have to read their results from the registers when register buses are available.
The elimination of stalls for WAW and WAR hazards

## Slide 87: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264, IBM PPC 620 in CA:AQA 2/e, but not in silicon!
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc stores
Non-precise interrupts!
  We will address this later

## Slide 88: Tomasulo overlap iterations of loops
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling).
Reservation stations
  Permit instruction issue to advance past integer control flow operations
  Also buffer old values of registers - totally avoiding the WAR stall that we saw in the scoreboard.
Other perspective: Tomasulo building data flow dependency graph on the fly.

## Slide 89: Tomasulo Loop Example
Loop: LD F0 0 R1
MULTD F4 F0 F2
SD F4 0 R1
SUBI R1 R1 #8
BNEZ R1 Loop
Assume Multiply takes 4 clocks
Assume first load takes 8 clocks (cache miss), second load takes 1 clock (hit)
To be clear, will show clocks for SUBI, BNEZ
Reality: integer instructions ahead

## Slide 90: Loop Example

## Slide 91: Loop Example Cycle 1

## Slide 92: Loop Example Cycle 2

## Slide 93: Loop Example Cycle 3
Implicit renaming sets up “DataFlow” graph

## Slide 94: Loop Example Cycle 4
Dispatching SUBI Instruction

## Slide 95: Loop Example Cycle 5
And, BNEZ instruction

## Slide 96: Loop Example Cycle 6
Notice that F0 never sees Load from location 80

## Slide 97: Loop Example Cycle 7
Register file completely detached from computation
First and Second iteration completely overlapped

## Slide 98: Loop Example Cycle 8

## Slide 99: Loop Example Cycle 9
Load1 completing: who is waiting?
Note: Dispatching SUBI

## Slide 100: Loop Example Cycle 10
Load2 completing: who is waiting?
Note: Dispatching BNEZ

## Slide 101: Loop Example Cycle 11
Next load in sequence

## Slide 102: Loop Example Cycle 12
Why not issue third multiply?

## Slide 103: Loop Example Cycle 13

## Slide 104: Loop Example Cycle 14
Mult1 completing. Who is waiting?

## Slide 105: Loop Example Cycle 15
Mult2 completing. Who is waiting?

## Slide 106: Loop Example Cycle 16

## Slide 107: Loop Example Cycle 17

## Slide 108: Loop Example Cycle 18

## Slide 109: Loop Example Cycle 19

## Slide 110: Loop Example Cycle 20

## Slide 111: Summary of Tomasulo Algorithm
Reservations stations: implicit register renaming to larger set of registers + buffering source operands
  Prevents registers as bottleneck
  Avoids WAR, WAW hazards of Scoreboard
  Allows loop unrolling in HW
Not limited to basic blocks
  (integer units gets ahead, beyond branches)
Lasting Contributions
  Dynamic scheduling
  Register renaming
  Load/store disambiguation
360/91 descendants are Pentium III; PowerPC 604; MIPS R10000; HP-PA 8000; Alpha 21264

## Slide 112: What about Precise Interrupts?
Tomasulo had: In-order issue, out-of-order execution, and out-of-order completion
Need to “fix” the out-of-order completion aspect so that we can find precise breakpoint in instruction stream.
 Speculation，Reorder buffer ! (later )

## Slide 113: Scoreboard vs. Tomasulo
特点
  Multiple multiplier, etc. Funcs
  Issue in order, Complete OOO
  IF Issue, Ro
  4 stages pipeline
  Scoreboare centralized control
缺点
  Stall when WAW, WAR
  特点
    Fewer Func, unpipelined
    Issue in order, Complete OOO
    FP op. queue, Reservation station, LD/ST buffer, CDB
    3 stages pipeline
    Reg. RenameNo WAW, WAR
    Reduce structural hazard
    RAW detection decentralized—reservation
    CDB forwarding path
Can Scoreboard avoid WAW, WAR with Reg. Rename?

## Slide 114: Scoreboard Pipeline stage description
Issue: a instruction is issued when
  The functional unit is available and
  No other active instruction has the same destination register.
  Avoid strutural hazard and WAW hazard
Read Operands (RD)
  The read operation is delayed until both the operands are available.
  This means that no previously issued but ncompleted instruction has the operand as its destination.
  This resolves RAW hazards dynamically
Execution (EX)
  Notify the scoreboard when completed so the functional unit can be reused.
Write result (WB)
  The scoreboard checks for WAR hazards and stalls the completing instruction if necessary.

## Slide 115: The scoreboard algorithm
Scoreboard-takes full responsibility for instruction issue and execution
  Create the dependence records
  Decide when to fetch the operand
  Decide when to enter execution
  Decide when the result can be written into the register file
Three data structure
  Instruction status:
    which of the four steps the instruction is in
  Functional unit status: buzy,op,Fi, Fj,Fk,Qj,Qk ,Rj,Rk
  Register result status:
    which functional unit will write that register

## Slide 116: Explicit Register Renaming
Make use of a physical register file that is larger than number of registers specified by ISA
Key insight: Allocate a new physical destination register for every instruction that writes
  Very similar to a compiler transformation called Static Single Assignment (SSA) form — but in hardware!
  Removes all chance of WAR or WAW hazards
  Like Tomasulo, good for allowing full out-of-order completion
  Like hardware-based dynamic compilation?
Mechanism? Keep a translation table:
  ISA register  physical register mapping
  When register written, replace entry with new register from freelist.
  Physical register becomes free when not used by any active instructions

## Slide 117: Advantages of Explicit Renaming
Decouples renaming from scheduling:
  Pipeline can be exactly like “standard” MIPS pipeline (perhaps with multiple operations issued per cycle)
  Or, pipeline could be Tomasulo-like or a scoreboard, etc.
  Standard forwarding or bypassing could be used
Allows data to be fetched from single register file
  No need to bypass values from reservation station or reorder buffer
  This can be important for balancing pipeline

## Slide 118: Adv. Explicit Renaming (cont.)
Many processors use a variant of this technique:
  R10000, Alpha 21264, HP PA8000
Another way to get precise interrupt points:
  All that needs to be “undone” for precise break point is to undo the table mappings
  Provides an interesting mix between reorder buffer and future file
    Results are written immediately back to register file
    Registers names are “freed” in program order (by ROB)
What’s Future File ?

## Slide 119: Explicit Renaming Support Includes:
Rapid access to a table of translations
A physical register file that has more registers than specified by the ISA
Ability to figure out which physical registers are free.
  No free registers  stall on issue
Thus, register renaming doesn’t require reservation stations. However:
  Many modern architectures use explicit register renaming + Tomasulo-like reservation stations to control execution.
Two Questions:
  How do we manage the “free list”?
  How does Explicit Register Renaming mix with Precise Interupts?

## Slide 120: Explicit register renaming: (R1000 Style)
Physical register file larger than ISA register file
On issue, each instruction that modifies a register is allocated new physical register from freelist
Done?
Oldest
Newest
P0
P2
P4
F6
F8
P10
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P32
P34
P36
P38

P60
P62
Current Map Table
Freelist
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 121: Explicit register renaming: (R1000 Style)
Note that physical register P0 is “dead” (or not “live”) past the point of this load.
  When we go to commit the load, we free up
F0
P0
LD P32,10(R2)
N
Done?
Oldest
Newest
P32
P2
P4
F6
F8
P10
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P34
P36
P38
P40

P60
P62
Current Map Table
Freelist
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 122: Explicit register renaming: (R1000 Style)
F10
F0
P10
P0
ADDD P34,P4,P32
LD P32,10(R2)
N
N
Done?
Oldest
Newest
P32
P2
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P36
P38
P40
P42

P60
P62
Current Map Table
Freelist
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 123: Explicit register renaming: (R1000 Style)
--
--
F2
F10
F0
P2
P10
P0
BNE P36,<…>
N
DIVD P36,P34,P6
ADDD P34,P4,P32
LD P32,10(R2)
N
N
N
Done?
Oldest
Newest
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Current Map Table
Freelist
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Checkpoint at BNE instruction
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 124: Explicit register renaming: (R1000 Style)
--
F0
F4
--
F2
F10
F0
P32
P4
P2
P10
P0
ST 0(R3),P40
ADDD P40,P38,P6
Y
Y
LD P38,0(R3)
Y
BNE P36,<…>
N
DIVD P36,P34,P6
ADDD P34,P4,P32
LD P32,10(R2)
N
y
y
Done?
Oldest
Newest
P40
P36
P38
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P42
P44
P48
P50

P0
P10
Current Map Table
Freelist
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Checkpoint at BNE instruction
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 125: Explicit register renaming: (R1000 Style)
F2
F10
F0
P2
P10
P0
DIVD P36,P34,P6
ADDD P34,P4,P32
LD P32,10(R2)
N
y
y
Done?
Oldest
Newest
Current Map Table
Freelist
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Checkpoint at BNE instruction
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Speculation error fixed by restoring map table and freelist
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 126: Can we use explicit register renaming with scoreboard?
Rename
Table
Functional Units
Registers
FP Mult
FP Mult
FP Divide
FP Add
Integer
Memory
SCOREBOARD

## Slide 127: Four Stages of Scoreboard Control With Explicit Renaming
Issue—decode instructions & check for structural hazards & allocate new physical register for result
  Instructions issued in program order (for hazard checking)
  Don’t issue if no free physical registers
  Don’t issue if structural hazard
Read operands—wait until no hazards, read operands
  All real dependencies (RAW hazards) resolved in this stage, since we wait for instructions to write back data.
Execution—operate on operands
  The functional unit begins execution upon receiving operands. When the result is ready, it notifies the scoreboard
Write result—finish execution
Note: No checks for WAR or WAW hazards!

## Slide 128: Scoreboard With Explicit Renaming
Initialized Rename Table

## Slide 129: Renamed Scoreboard 1
Each instruction allocates free register
Similar to single-assignment compiler transformation

## Slide 130: Renamed Scoreboard 2

## Slide 131: Renamed Scoreboard 3

## Slide 132: Renamed Scoreboard 4
Next step Int1 will write result, where need
the value?

## Slide 133: Renamed Scoreboard 5
Next step Int2 will write result, where need
the value?

## Slide 134: Renamed Scoreboard 6
Why ADDD not issue ? Structure hazard ! Adder is occupied by with SUBD.

## Slide 135: Renamed Scoreboard 7

## Slide 136: Renamed Scoreboard 8
Next step Adder will complete execution

## Slide 137: Renamed Scoreboard 9
Next step Adder will write result, where need the value?

## Slide 138: Renamed Scoreboard 10
Adder is cleared, so ADDD can be issued next cycle.

## Slide 139: Renamed Scoreboard 11
WAR Hazard gone!
Notice that P32 not listed in Rename Table
  Still live. Must not be reallocated by accident
WAR dependence

## Slide 140: Renamed Scoreboard 12

## Slide 141: Renamed Scoreboard 13

## Slide 142: Renamed Scoreboard 14

## Slide 143: Renamed Scoreboard 15

## Slide 144: Renamed Scoreboard 16

## Slide 145: Renamed Scoreboard 17

## Slide 146: Renamed Scoreboard 18

## Slide 147: Renamed Scoreboard 19

## Slide 148: Summary #2
Explicit Renaming: more physical registers than needed by ISA.
  Separates renaming from scheduling
    Opens up lots of options for resolving RAW hazards
  Rename table: tracks current association between architectural registers and physical registers
  Potentially complicated rename table management