## Slide 1: Ch3-2 ILP: Branch Prediction

## Slide 2: Review
Structural Hazard
  Separate/replicate function unit, fully-pipelined function units
Data Hazard
  RAW: double-bump, forwarding path, simple compiler scheduling
  WAR, WAW: implicit register renaming
Control Hazard
  Resolve branch asap, Flushing, Predict-not-taken, Predict-taken, Delayed-Branch

## Slide 3: Control Hazard (example PA-25)
Flushing: stall until the branch is resolved.
  Stall X cycles if delay slots=x
Predict-not-taken:
  Hardware takes all branches as not-taken, compiler need to put frequent case in the not-taken branch
  Stall 0 cycles if not-taken, stall X cycles if taken
Predict-taken:
  Hardware takes all branches as taken, can go forward only when get the branch target . Compiler need to put frequent case in the taken branch
  Stall y cycles waiting for branch target; stall X cycles if not taken.
Delayed Branch:

## Slide 4: Static branch prediction
Stall for control hazards
= f (branch frequency, prediction accuracy, misprediction penalty )
Predict according to statistics: (predict taken)
  Mispredition: 9% ~ 59%, average 34%

## Slide 5: Predict based on profile information
  Average misprediction rate 9% for FP programs,
  Average misprediction rate 15% for integer programs

## Slide 6: Dynamic Hardware Prediction --reducing branch costs
1-bit Branch-Prediction Buffer
2-bit Branch-Prediction Buffer
Correlating Branch Prediction Buffer
Tournament Branch Predictor
Branch Target Buffer
Integrated Instruction Fetch Units
Return Address Predictors

## Slide 7: 1、1-bit Branch-Prediction Buffer
Performance = ƒ(accuracy, cost of misprediction)
Branch History Table: Lower bits of PC address index table of 1-bit values
  Says whether or not branch taken last time
  No address check (saves HW, but may not be right branch)
Problem: in a loop, 1-bit BHT will cause 2 mispredictions (avg 2/n iterations before exit):进入和退出各错一次
  Only (n-2)/n accuracy even if loop (n-1)/n of the time
  0111……1110111… …1110111……1110111…
1
1
0
PC 低位

## Slide 8: 2、2-bit Branch-Prediction Buffer
Solution: 2-bit scheme where change prediction only if get misprediction twice:
  (Jim Smith, 1981, A study of branch prediction strategies)
Red: stop, not taken
Blue: go, taken
Adds hysteresis to decision making process
  01111111……111110111111…1110111111
T
T
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
T
NT
T
NT
NT

## Slide 9: An alternative 2-bit predictor
It can be implemented using a 2-bit counter
T
T
NT
Predict Taken
Surely
Predict Not
Taken
Predict Taken
Predict Not
Taken surely
T
NT
T
NT
NT

## Slide 10: Generalize the 2-bit predictor to n-bit predictor
N-bit counter ( 0<x<2n-1)
Predict taken X >= 2n-1
Predict untaken X < 2n-1
Counter + 1 when a taken branch
Counter – 1 when a not taken branch
Most system rely on 2-bit predictor rather than n-bit predictor.

## Slide 11: Accuracy of the 2-bit predictor
4096 entries, 2-bit predictor
SPEC89
Accuracy : 99%~82%
Misprediction: 1%~18%
一个entry代表一个分支指令

## Slide 12: How about unlimited entries ?

## Slide 13: How to improve accuracy ?
Analysize the branch behavior
IF ( aa == 2)
aa = 0;
IF ( bb == 2)
bb = 0;
IF (aa == bb ) {
……
}
SUBI R3, R1, #2
BNEZ R3, L1 ; br.b1 (aa!=2)
ADD R1, R0, R0 ; aa==0
L1: SUBI F3, R2, #2
BNEZ R3, L2 ; br.b2 (bb!=2)
ADD R2, R0, R0 ; bb==0
L2: SUB R3, R1, R2; R3=aa-bb
BEQZ R3, L3 ; br.b3 (aa==bb)

## Slide 14: Conclusion from the example
B3 branch depends on b1 and b2. B3 is taken only when both b1 and b2 is untaken.
It’s impossible to predict B3 correctly only depending on its previous behavior.
A branch’s behavior not only rely on it’s previous behavior but also on recent behavior of other branches. 不光看自己的分支预测历史，也要看临近分支的行为

## Slide 15: Let’s check an example
If (d==0)
d=1;
if (d==1){
…...
}
Assume Reg[R1] = d
BNEZ R1, L1 ; br b1, (d!=0)
DADDIU R1, R0, #1 ; d==0, so d=1
L1: DADDIU R3, R1, #-1 ;
BNEZ R3, L2 ; br b2, (d!=1)
……
L2:

## Slide 16: Feature of the code:
d的 初值 | d==0? | B1 | 在b2以前的d值 | d==1? | b2
0 | Yes | Not taken | 1 | Yes | Not taken
1 | No | Taken | 1 | Yes | Not taken
2 | No | Taken | 2 | no | Taken
Conclusion: b2 will be not taken if b1 is not taken
So, we can get accurate prediction if using correlate predictor.
顺序执行
跳转

## Slide 17: Always mispredict if using one-bit predictor
d=? | b1预测 | b1动作 | 新的b1预测 | b2预测 | b2动作 | 新的b2预测
2 | NT | T | T | NT | T | T
0 | T | NT | NT | T | NT | NT
2 | NT | T | T | NT | T | T
0 | T | NT | NT | T | NT | NT
预测与实际动作 预测与实际动作
总是相反 总是相反
If (d==0)
d=1;
if (d==1){
…...
}
上一次分支预测结果会作为下一次分支预测的依据
表示时间推移

## Slide 18: Correlating predictor
Correlating predictor is composed of two parts ( two bits ):
  1st bit: prediction for previous br. is NT，
  2nd bit: prediction for previous br. Is T
Four combinations
预测 组合 | 上一次Br为NT,预测本次位(看第一位) | 上一次Br为T,预测本次为(看第二位)
NT/NT | NT | NT
NT/ T | NT | T
T /NT | T | NT
T / T | T | T
Note, previous Br might be a different br.

## Slide 19: Prediction with correlating predictor (1,1)
d = ? | b1预测 | b1动作 | b1新预测 | b2预测 | b2动作 | b2新预测
2 | NT/NT(00) | T | T/NT | NT/NT | T | NT/T
0 | T/NT | NT | T/NT | NT/T | NT | NT/T
2 | T/NT | T | T/NT | NT/T | T | NT/T
0 | T/NT | NT | T/NT | NT/T | NT | NT/T
b1与b2对应的1-bit预测器均初始化为（NT/NT）
if(d==0) //b1
d=1;
if(d==1) //b2
...
规则：
根据真实跳转情况更新对应预测器。如果预测和动作不符，则预测错误，更新对应预测器。可以看出，关联预测其预测仅在初始化时发生2次错误，剩余6次预测正确。
上次临近分支动作为T则看右预测器，上次为NT则看左预测器。
B1和B2预测包含两个独立预测器，一个1位，选择哪一个由上一次预测的动作决定，例子中有四个预测器

## Slide 20: Prediction with correlating predictor (1,1) with initial value =NT/NT.
粗体字表示本次预测
预测出错 b1动作与b2预测值选用关系
预测正确 b2动作与b1预测值选用关系
新预测值
粗体字表示本次预测
预测出错 b1动作与b2预测值选用关系
预测正确 b2动作与b1预测值选用关系
新预测值
If (d==0)
d=1;
if (d==1){
…...
}

## Slide 21: 3.Correlating Branches prediction buffer
Idea: taken/not taken of recently executed branches is related to behavior of next branch (as well as the history of that branch behavior)
  Then behavior of recent branches selects between, say, 4 predictions of next branch, updating just that prediction
(2,2) predictor: 2-bit global, 2-bit local
  Branch address (4 bits)
2-bits per branch local predictors
Prediction
2-bit global
branch history
(01 = not taken then taken)
PC 决定
硬件history buffer决定

## Slide 22: (m,n) predictor
(m, n) predictor
m: previous m branch instruction
n: n-bit branch prediction buffer
Total size = 2m × n bit

## Slide 23: 4.Correlating Branches prediction buffer
0 0 0 0 0 1 1 1 0 0 0 0 0 1 1 1 0 0 0 0 0 1 1 1
Predict: v v x
v v x v v v
下图反映branch i的branch history。红框内具有相同branch address
00
00
00
Branch i
00
11
11
Branch history
6次
3次

## Slide 24: Comparision of 2-bit predictors
4096 entries已经足够了，1024 entries还不够

## Slide 25: Accuracy analysis
Mispredict because either:
  Wrong guess for the branch
  Got branch history of wrong branch when index the table. Entry不够，选到了冲突的entry

## Slide 26: 4、Tournament Predictors
Motivation for correlating branch predictors is 2-bit predictor failed on important branches; by adding global information, performance improved
Tournament predictors: use 2 predictors, 1 based on global information and 1 based on local information, and combine with a selector
Hopes to select right predictor for right branch

## Slide 27: Tournament Predictor in Alpha 21264
4K 2-bit counters to choose from among a global predictor and a local predictor
Global predictor also has 4K entries and is indexed by the history of the last 12 branches; each entry in the global predictor is a standard 2-bit predictor
  12-bit pattern: ith bit 0 => ith prior branch not taken; ith bit 1 => ith prior branch taken;
00,10,11
00,11
10
Use 1
Use 2
Use 2
Use 1
00,01,11
00,11
10
10
01
01
01
4K  2 bits
1
3
2
12
.
.
.

## Slide 28: T-Predictor in Alpha 21264 （cont.)
Local predictor consists of a 2-level predictor:
  Top level a local history table consisting of 1024 10-bit entries; each 10-bit entry corresponds to the most recent 10 branch outcomes for the entry. 10-bit history allows patterns 10 branches to be discovered and predicted.
  Next level Selected entry from the local history table is used to index a table of 1K entries consisting a 3-bit saturating counters, which provide the local prediction
Total size: 4K*2 + 4K*2 + 1K*10 + 1K*3 = 29K bits! (~180,000 transistors)
1K  10 bits
1K  3 bits

## Slide 29: T-Predictor in Alpha 21264 （cont.)
Total size: 4K*2 + 4K*2 + 1K*10 + 1K*3 = 29K bits! (~180,000 transistors)

## Slide 30: % of predictions from local predictor in Tournament Prediction Scheme
98%
100%
94%
90%
55%
76%
72%
63%
37%
69%
0%
20%
40%
60%
80%
100%
nasa7
matrix300
tomcatv
doduc
spice
fpppp
gcc
espresso
eqntott
li

## Slide 31: Accuracy of Branch Prediction
94%
96%
98%
98%
97%
100%
70%
82%
77%
82%
84%
99%
88%
86%
88%
86%
95%
99%
0%
20%
40%
60%
80%
100%
gcc
espresso
li
fpppp
doduc
tomcatv
Profile-based
2-bit counter
Tournament
Profile: branch profile from last execution (static in that is encoded in instruction, but profile)
fig 3.40

## Slide 32: Accuracy v. Size (SPEC89)
0%
1%
2%
3%
4%
5%
6%
7%
8%
9%
10%
0
8
16
24
32
40
48
56
64
72
80
88
96
104
112
120
128
Total predictor size (Kbits)
Conditional branch misprediction rate
Local - 2 bit counters
Correlating - (2,2) scheme
Tournament

## Slide 33: 5. Branch Target Buffer
Branch Target Buffer (Branch Target Cache):
  Address of branch index to get prediction AND branch address (if taken)
  Note: must check for branch match now, since can’t use wrong branch address
Branch PC
Predicted PC
=?
PC of instruction
FETCH
Extra
prediction state
bits
Yes: instruction is branch and use predicted PC as next PC
No: branch not
predicted, proceed normally
(Next PC = PC+4)

## Slide 34: Branch Target “Cache”
Branch Target cache - Only predicted taken branches
“Cache” - Content Addressable Memory (CAM) or Associative Memory (see figure)
Use a big Branch History Table & a small Branch Target Cache
Branch PC
Predicted PC
=?
Prediction state
bits (optional)
Yes: predicted taken branch found
No: not found
PC

## Slide 35: Steps in handling an instruction with a Branch-Target Buffer

## Slide 36: Variations of Branch Target Buffer
Instead of storing just the branch address, the BTB can store the actual instruction as well.
Storing both the branch address and the actual instruction in the buffer
Very big branch Target buffer to cache addresses or instructions from multiple paths, ex, the predicted and unpredicted direction

## Slide 37: 6. Integrated Instruction Fetch Units
Increasing the number of instructions executed per clock, instruction fetch will become an significant bottleneck.
Integrated instruction fetch unit:
  Integrated branch prediction
  Instruction prefetch
  (see P438 hardward prefetch &
  P483 ex. Instruction prefetcher )
  Instruction memory access and buffering

## Slide 38: 7、Return Address Predictors
Technique for predicting indirect jumps, whoes destination address varies at run time.
Register Indirect branch hard to predict address
SPEC89: procedure return account for 85% of the indirect jumps.
Branch-target buffer doesn’t work well for procedure return

## Slide 39: Return Addresses Buffer
Since stack discipline for procedures, save return address in small buffer that acts like a stack:
  Caches the most recent return addresses.
  Push return address into stack at a call;
  pop an address off at a return
SPEC benchmark shows a stack with 8-16 entries works quite well. (fig-3.22)

## Slide 40: Dynamic Branch Prediction Summary
Prediction becoming important part of scalar execution
Branch History Table: 2 bits for loop accuracy
Correlation: Recently executed branches correlated with next branch.
  Either different branches
  Or different executions of same branches
Tournament Predictor: more resources to competitive solutions and pick between them
Branch Target Buffer: include branch address & prediction
Predicated Execution can reduce number of branches, number of mispredicted branches
Return address stack for prediction of indirect jump

## Slide 41: Change3-3 Hardware Based Speculation

## Slide 42: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264, IBM PPC 620 in CA:AQA 2/e, but not in silicon!
Many associative stores (CDB) at high speed, Performance limited by Common Data Bus
Non-precise interrupts!
  We will address this later
Partially overlapped basic blocks
  integer units get ahead, beyond FP operation
  the successor basic block can not start execution until the branch is resolved, in spite of that it can be issued.
Notes: We talked about Tomasulo algorithm and found that it gets better performance than scoreboard, but it’s not good enough for ILP exploration.
In spite of Non-precise interrupts, it can only provide partially overlapped basic blocks, which means
1) Next basic block can be issued before a branch is resolved.
2) Integer instructions in successor basic block can go ahead beyond the FP operations in previous block.
But it requires that a branch is resolved before actually executing any instruction in the successor basic block.

## Slide 43: Hardward-based Speculation
Speculating on the outcome of branches and executing the program as if the predictions were correct.
  Need to handle the situation where the speculation is incorrect.
Key ideas:
  Dynamic branch prediction to choose which instruction to execute
  Speculation to allow the execution of instructions before the control dependences are resolved.
  Dynamic scheduling to deal with the scheduling of different combinations of basic blocks.
Data flow execution:
  Operations execute as soon as their operands are available.
Notes: We talked about using dynamic branch predictor to increase predict accuracy, so that we can decrease the stalls due to control hazards.
We can go further. Get the predicted Instruction Address by combining the predictor with target PC avoiding Target address calculation.
Even further by combining the branch target instruction buffer with predictor, so that we can get the instruction avoiding memory access.
How about take a further step to execute the instructions in the predicted basic block ?
That’s the basic motivation of speculation !
branch prediction + speculatively execution + Dynamic scheduling
1) Using dynamic branch predictor to select which instructions to execute speculatively.
2) Speculation to execute the predicted instruction before a branch is resolved, with the ability to undo the effects of a wrong guess instruction sequence.
3) Schedule the instructions dynamically to deal with different combination of basic blocks.
So it’s a Data flow execution ignoring the control dependences between the instructions.

## Slide 44: Speculative execution based on Tomasulo's algorithm
Separate the process of completing execution and the bypassing of results among instructions from instruction commit (reg file or memory update).
Allows other (speculative) instructions to execute, but no results are committed until we know the instruction is no longer speculative.
Allow instructions to execute out of order but force them to commit in order, which helps with handling exceptions properly.
Notes: It needs to be able to undo the effects of the speculated instruction sequence, so that we should separate the bypassing results and the actual completion of an instruction.
So that we can allow the instructions to execute and bypass its results to other instructions which is required to execute speculatively, at the same time allow a instruction to update the register file or memory only when it is assured that the instruction is no longer speculative.
We call the stage of updating register file or memory “instruction commit”. And instruction commit should be kept in order so that we can undo the effects. So the instructions, speculative or not speculative are executed out of order and can have the execution results out of order, but instructions will be committed in order.
We need additional buffer to store the results that finish executing but not ready for commitment.

## Slide 45: Extend Tomasulo’s Algorithm to handle speculation
Notes: The reorder buffer takes the responsibility of reservation stations in Tomasulo algorithm, and more.
Works as cyclic FIFO queue to enable in-order commitment.
Buffer the results between the time finishing executing and the time instruction commits for normal instructions and speculative instructions.
Provide extra registers as a source of instruction operands, enable implicit register renaming.
Also act as store buffer.
We still need the reservation stations to buffer the operations between issue and execution. The only difference is that we tag the results using reorder buffer number.

## Slide 46
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
From Intruction unit

## Slide 47: Difference from Tomasulo Algorithm
Reorder Buffer is added
Eliminate store buffer (Mem write is ordered in Reorder buffer)
Register renaming is done via reorder buffer instead of reservation station
Reservation only for storing opcodes and operands during the instruction flying between issue and execution.
ROB hold the instruction results and supply operands in the interval between completion of instruction execution and instruction commit.

## Slide 48: Entry of ROB
Instruction type
Destination field
Value field
Ready field
Exception vector
Notes: Instruction type: ALU, LD, ST, Branch,
Destination field: Register number for ALU, LD
Memory address for ST
Value: hold the results between finishing execution
and waiting for commits.
Ready: result is ready or not.

## Slide 49: 4 Steps of Speculative Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station and reorder buffer slot free, issue instr & send operands & reorder buffer no. for destination (this stage sometimes called “dispatch”) , update control entries “in use”.
2.Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result; when both in reservation station, execute; checks RAW
3.Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting FUs & reorder buffer; mark the reservation station available.
4.Commit—update register with reorder result
  When instruction at head of reorder buffer & result present, update register with result (or store to memory) and remove instr from reorder buffer. Mispredicted branch flushes reorder buffer (sometimes called “graduation”)

## Slide 50: What to do when commit ?
when an instruction reaches the head of ROB and its result is present in the buffer, then
For non-Branch instruction
  Update the register with the result
  Remove the instruction from ROB
  When it’s a STORE, update the memory instead of Reg.
For a mispredicted branch
  ROB is flushed and execution is restarted at the correct successor of the branch
For a right-predicted branch
  End of branch instruction.

## Slide 51: Tomasulo With Reorder buffer:
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
2 clock cycles for pipelined memory access
LD F6,34(R2)
Dest
Oldest
Newest
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
LD F6,34(R2)
N
Done?
Dest
from
Memory
1 34+R2
Dest
Reorder Buffer
Registers
Busy, ROB No. Value
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 52: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F6
LD F2,45(R3)
LD F6,34(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
1 34+R2
2 45+R3
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 53: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD ROB2,R(F4)
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
N
N
1 34+R2
2 45+R3
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 54: Tomasulo With Reorder buffer:
4 SUBD ROB2,ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD ROB2,R(F4)
1 34+R2
2 45+R3
N
N
F8
SUBD F8,F2,F6
N
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
N
N
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
Note: The first LD will finish memeory access next cycle
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 55: Tomasulo With Reorder buffer:
4 SUBD ROB2,M[34+R2]
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD ROB2,R(F4)
2 45+R3
N
N
F8
SUBD F8,F2,F6
N
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
N
Y
DIVD F10,F0,F6
F10
5 DIVD ROB3,M[34+R2]
M[34+R2]
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
Note: The 2nd LD will finish memeory access next cycle
1 34+R2
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 56: Tomasulo With Reorder buffer:
4 SUBD M[45+R3],M[34+R2]
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD M[45+R3],R(F4)
N
N
F8
SUBD F8,F2,F6
N
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
Y
Y
DIVD F10,F0,F6
F10
5 DIVD ROB3,M[34+R2]
M[34+R2]
ADDD F6,F8,F2
F6
6 ADDD ROB4, M[45+R3]
M[45+R3]
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
1 34+R2
2 45+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 57: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD M[45+R3],R(F4)
N
N
F8
SUBD F8,F2,F6
Y
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
Y
Y
DIVD F10,F0,F6
F10
5 DIVD ROB3,M[34+R2]
M[34+R2]
ADDD F6,F8,F2
F6
6 ADDD V[1], M[45+R3]
M[45+R3]
V[1]
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 58: Speculation performance
Overlapped basic block
Is there any new problems ?
  Pay attention to the memory accessing

## Slide 59: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
LD F0,10(R2)
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 60: Tomasulo With Reorder buffer:
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
F0
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 61: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 62: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
ADDD F0,F4,F6
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
5 0+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 63: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ROB5
ST 0(R3),F4
ADDD F0,F4,F6
N
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
1 10+R2
6 0+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 64: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
ST 0(R3),F4
ADDD F0,F4,F6
Y
N
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
2 ADDD R(F4),ROB1
6 ADDD M[10],R(F6)
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 65: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 66: Tomasulo With Reorder buffer:
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
What about memory
hazards???
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 67: new problem--memory disambiguation
Question: Given a load that follows a store in program order, are the two related?
  (Alternatively: is there a RAW hazard between the store and the load)? Eg: ST 0(R2), R5 LD R4, 0(R3)
Can we go ahead and start the load early?
  Store address could be delayed for a long time by some calculation that leads to R2 (divide?).
  We might want to issue/begin execution of both operations in same cycle.

## Slide 68: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
-
ST R5,0(R2)
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 69: Tomasulo With Reorder buffer:
2 ADDD R(F4),R（F0)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
-
ADDD F10,F4,F0
ST R5,0(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 70: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),R(F0)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
-
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 71: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4), ROB?
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
ADDD F0,F4,F6
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
-
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
4 0+R3
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 72: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),R(F0)
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ROB5
ST 0(R3),F4
ADDD F0,F4,F6
N
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
4 0+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 73: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
ST 0(R3),F4
ADDD F0,F4,F6
Y
N
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
4 0+R3
Dest
Reorder Buffer
Registers
2 ADDD R(F4), ROB?
6 ADDD M[10],R(F6)
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 74: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4), ROB?
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
4 0+R3
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 75: Tomasulo With Reorder buffer:
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
3 DIVD ROB2,R(F6)
2 ADDD R(F4), ROB?
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
4 0+R3
Dest
Reorder Buffer
Registers
What if 0(R3)=0(R2)
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 76: Memory Disambiguation: Sorting out RAW Hazards in memory
Question: Given a load that follows a store in program order, are the two related?
  (Alternatively: is there a RAW hazard between the store and the load)? Eg: ST 0(R2), R5 LD R6, 0(R3)
Can we go ahead and start the load early?
  Store address could be delayed for a long time by some calculation that leads to R2 (divide?).
  We might want to issue/begin execution of both operations in same cycle.
  Today: Answer is that we are not allowed to start load until we know that address 0(R2)  0(R3)

## Slide 77: Hardware Support for Memory Disambiguation
Need buffer to keep track of all outstanding stores to memory, in program order.
  Keep track of address (when becomes available) and value (when becomes available)
  FIFO ordering: will retire stores from this buffer in program order
When issuing a load, record current head of store queue (know which stores are ahead of you).

## Slide 78: Hardware Support for Memory Disambiguation(2)
When have address for load, check store queue:
  If any store prior to load is waiting for its address, stall load.
  If load address matches earlier store address (associative lookup), then we have a memory-induced RAW hazard:
    store value available  return value
    store value not available  return ROB number of source
  Otherwise, send out request to memory
Actual stores commit in order, so no worry about WAR/WAW hazards through memory.

## Slide 79: Memory Disambiguation:
F4
LD F4, 10(R3)
N
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
--
<val 1>
ST 10(R3), F5
LD F0,32(R2)
ST 0(R3), F4
N
N
Y
Done?
Dest
Dest
Oldest
Newest
from
Memory
2 32+R2
4 ROB3
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 80: HW support for precise interrupts
Need HW buffer for results of uncommitted instructions: reorder buffer
  3 fields: instr, destination, value
  Use reorder buffer number instead of reservation station when execution completes
  Supplies operands between execution complete & commit
  (Reorder buffer can be operand source => more registers like RS)
  Once instruction commits, result is put into register
  As a result, easy to undo speculated instructions on mispredicted branches or exceptions
Reorder
Buffer
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations
FP Regs

## Slide 81
 | 记分牌 | Tomasulo | 带投机的Tomasulo
主要 思想 | 动态调度、按序发射、乱序 执行、乱序完成、集中控制。 | 动态调度、按序发射、乱序 执行、乱序完成分散控制。 增加RS（保留站）,CDB。 | 转移预测, 动态调度、投机执行、 按序完成。在RS基础上再增加ROB(reorder buffer)。
解决 何种 竞争 | RAW数据竞争。 WAW,WAR时stall | 解决数据竞争,避免WW,WAR 竞争;允许硬件支持的循环展 开，不局限于程序基本块。 | 解决数据竞争,避免WW,WAR 竞争;从数据竞争扩充到控制竞争。通过 预测减少控制竞争stall。
指 令 节 拍 | ISSUE：停顿于结构竞争和WAW竞争。 RO：等待两个操作数就绪,动态解决RAW。 EX：和普通流水线一样。 WB：停顿于WAR竞争。 | ISSUE：仅停顿于结构竞争（RS部件）。 EX：利用保留站（RS）进行换名，解决了WAW和WAR问题（即名字相关）。 WB：回写。 | ISSUE：仅停顿于结构竞争（RS部件和ROB部件）。 EX：等待操作数就绪，执行。 WB：结果写到ROB，其它指令可以引用该临时结果，但不更新寄存器。 COMMIT：保证按序完成，保证精确中断。
关键 部件 | 记分牌、集中控制、指令状 态、功能部件状态、寄存器 结果状态。 | CDB(通用数据总线)：执行结果通过CDB传递，及时。 RS(保留站)：换名功能以及暂存临时数据。 | ROB(REORDER BUFFER)重构序缓冲器： 对移到顶部的指令进行判断。。。ROB 负责寄存器重命名、暂存执行后和交付 前的结果、
其它 | 从静态调度到动态调度的过 渡算法。 | 一旦指令将临时结果放在保留站，则其它后续的指令都能立即在寄存器组中看见这个结果。 | 某指令将临时结果放在ROB后，其它指 令并不能从寄存器组中看到这个结果 （也就是说，寄存器组的值并没有更 新），而是等待该指令提交（commit） 后，寄存器组才更新。