## Slide 1: Ch3-- ILP & its exploration
Ch3-0 Extending 5-stage pipeline to support multicycle operations
App C5-C6
Simple & Creative

## Slide 2: Pipelined CPU supporting RISC V

## Slide 3: Extending the MIPS pipeline to handle MultiCycle Operations
Alternative resolutions to handle floating-point operations ( or complex operations)
  Complete operation in 1 or 2 clock cycles,
    Which means using a slow clock,
    or/and using enormous amounts of logic in FP units.
  Allow for a longer latency for operations
    The EX cycle may be repeated as many times as needed to complete the operation
    There may be multiple FP units

## Slide 4: 5-stage pipeline with FP units

## Slide 5: Pipelining some of the FP units
Two terminologies
  Latency----the number of intervening cycles between an instruction that produces a result and an instruction that uses the result.
  Initiation interval----the number of cycles that must elapse between instructions issue to the same unit.
    For full pipelined units, initiation interval is 1
    For unpipelined units, initiation interval is always the latency plus 1.

## Slide 6: Latencies and initiation intervals for functional units

## Slide 7: Pipeline supports multiple outstanding FP operations
IF
ID
M1
M2
M3
M4
M5
M6
M7
A1
A2
A3
A4
WB
EX
MEM
DIV

## Slide 8: Specifications
Memory bandwidth: double words/one cycle
New pipeline latches are required:
  M1/M2, M2/M3, M3/M4, M4/M5, M5/M6, M6/M7
  A1/A2, A2/A3, A3/A4
New connection registers are required:
  ID/EX, ID/M1, ID/A1, ID/DIV
  EX/MEM, M7/MEM, A4/MEM, DIV/MEM
Because the divider unit is unpipelined, structural hazards can occur.
Because the instructions have varying running times, the number of register writes required in a cycle can be larger than 1
New data hazards: WAW is possible due to disorder WBs
Due to longer latency of operations, stalls for RAW hazards will be more frequent.
Problems with exceptions resulting from disorder completion

## Slide 9: Issuing in order and completion out of order
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
MUL.D | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | WB |  | 
ADD.D |  | IF | ID | A1 | A2 | A3 | A4 | WB |  |  |  | 
MUL.D |  |  | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | WB
LD.D |  |  |  | IF | ID | EX | MEM | WB |  |  |  | 
SD.D |  |  |  |  | IF | ID | EX | MEM | WB |  |  | 

## Slide 10: Structural Hazards for the FP register write port
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
MUL.D F0,F4, F6 | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | WB
…… |  | IF | ID | EX | MEM | WB |  |  |  | 
…… |  |  | IF | ID | EX | MEM | WB |  |  | 
ADD.D F2, F4, F6 |  |  |  | IF | ID | A1 | A2 | A3 | A4 | WB
…… |  |  |  |  | IF | ID | EX | MEM | WB | 
LD.D F8, 0(R2) |  |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 11: How to solve the write port conflict ?
Increase the number of write ports
  Unattractive at all !
  No worthy since steady state usage is close to 1.
Detect and insert stalls by serializing the writes
  Track the use of the write port in the ID stage and to stall an instruction before it issues
    Additional Hardware: a shift register+ write conflict logic
    The shift register tracks when already-issued instructions will use the register file, and right shift 1 bit each clock.
    The stalls might aggravate the data hazards
    All interlock detection and stall insertion occurs in ID stage
  To stall a conflicting instruction when it tries to enter the MEM or WB stage.
    Easy to detect the conflict at this point
    Complicates pipeline control since stalls can now occur in two places.

## Slide 12: Types of data hazards
Consider two instructions, A and B. A occurs before B.
RAW( Read after write) true dependence
  Instruction A writes Rx，instruction B reads Rx
WAW(Write after write) output dependence
  Instruction A writes Rx，instruction B writes Rx
WAR( Write after read) anti-denpendence
  Instruction A reads Rx，instruction B writes Rx
Hazards are named according to the ordering that MUST be preserved by the pipeline

## Slide 13: RAW dependence
B tries to read a register before A has written it and gets the old value.
This is common, and forwarding helps to solve it.
S(A)
D(A)
S(B)
D(B)
Time
No hazard
S(A)
D(A)
S(B)
D(B)
If D(A)=S(B), hazard occur.

## Slide 14: WAW dependence
B tries to write an operand before A has written it.
After instruction B has executed, the value of the register should be B's result, but A's result is stored instead.
This can only happen with pipelines that write values in more than one stage, or in variable-length pipelines (i.e. FP pipelines).
S(A)
D(A)
S(B)
D(B)
Time
No hazard
S(A)
D(A)
S(B)
D(B)
If D(A)=D(B), hazard occur.

## Slide 15: WAR dependence
B tries to write a register before A has read it.
In this case, A uses the new (incorrect) value.
This type of hazard is rare because most pipelines read values early and write results late.
However, it might happen for a CPU that had complex addressing modes. i.e. autoincrement.
S(A)
D(A)
S(B)
D(B)
Time
No hazard
S(B)
D(B)
If S(A)=D(B), hazard occur.
S(A)
D(A)

## Slide 16: Stalls arising from RAW hazards
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
LD.D F4, 0(R2) | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  |  | 
MUL.D F0, F4, F6 |  | IF | ID | stall | M1 | M2 | M3 | M4 | M5 | M6 | M7 | WB |  |  |  | 
ADD.D F2, F0, F8 |  |  | IF | stall | ID | stall | stall | stall | stall | stall | stall | A1 | A2 | A3 | A4 | WB
SD.D F2, 0(R2) |  |  |  |  | IF | stall | stall | stall | stall | stall | stall | ID | EX | stall | stall | MEM

## Slide 17: The WAW hazards
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 16
MUL.D F0, F4, F6 | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | WB |  |  | 
…… |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  | 
…… |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  | 
ADD.D F2, F4, F6 |  |  |  | IF | ID | A1 | A2 | A3 | A4 | stall | WB |  | 
…… |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  | 
…… |  |  |  |  |  | IF | ID | EX | MEM | WB |  |  | 
LD.D F8, 0(R2) |  |  |  |  |  |  | IF | ID | EX | MEM | stall | stall | WB
LD.D F2, 0(R2)

## Slide 18: Solving the WAW hazard
Stall an instruction that would "pass" another until after the earlier instruction reaches the MEM phase.
Cancel the WB phase of the earlier instruction
Both of these can be done in ID, i.e. when LD is about to issue.
Since pure WAW hazards are not common, either method works.
Pick the one that simplest to implement.
The simplest solution for the MIPS pipeline is to hold the instruction in ID if it writes the same register as an instruction already issued.

## Slide 19: What other hazards are possible ?
Hazards among FP instructions.
Hazards between an FP instruction and an integer instruction.
  Since two register files exist, only FP loads and stores and FP register moves to integer registers involve hazards.

## Slide 20: Checks are required in ID
Check for structural hazards .
  The divide unit and Register write port.
Check for RAW hazards
  The CPU simply stalls the instruction at ID stage until:
    Its source registers are no longer listed as destinations in any of the execution pipeline registers (registers between stages of M and A) OR
    Its source registers are no longer listed as the destination of a load in the EX/MEM register.
Check for WAW hazards
  Check instructions in A1, ..., A4, Divide, or M1, ...,M7 for the same destination register (check pipeline registers.)
  Stall instruction in ID if necessary.

## Slide 21: Performance of FP pipeline

## Slide 22: Performance of FP pipeline

## Slide 23: The MIPS R4000 pipeline
IF－First half of instruction fetch. PC selection occurs. Cache access is initiated.
IS－Second half of instruction fetch.
－This allows the cache access to take two cycles.
RF－Decode and register fetch, hazard checking, I-cache hit detection.
EX－Execution: address calculation, ALU Ops, branch target calculation and condition evaluation.
DF/DS/TC
  － Data fetched from cache in the first two cycles.
  － The third cycle involves checking a tag check to determine if the cache access was a hit.
WB－Write back result for loads and R-R operations.

## Slide 24: Possible stalls and delays
Load delay: two cycles
  The delay might seem to be three cycles, since the tag isn't checked until the end of the TC cycle.
  However, if TC indicates a miss, the data must be fetched from main memory and the pipeline is backed up to get the real value.

## Slide 25: Load stalls – 2 stalls

## Slide 26: Example：load stalls

## Slide 27: Branch delay: 3 cycles
Branch delay: three cycles (including one branch delay slot)
  The branch is resolved during EX, giving a 3 cycle delay.
  The first cycle may be a regular branch delay slot (instruction always executed) or a branch-likely slot (instruction cancelled if branch not taken).
  MIPS uses a predict-not-taken method presumably because it requires the least hardware.

## Slide 28: Branch Delays： 3 stalls

## Slide 29: Pipeline status for branch latency
Predict-NOT-taken + Delayed Branch

## Slide 30: The FP 8-stage operational pipeline

## Slide 31: Latency and initiation intervals

## Slide 32: Structural hazards-1

## Slide 33: Structural hazards-2

## Slide 34: Structural hazards-3

## Slide 35: Structural hazards-4

## Slide 36: Performance loss measurements